## Slide 1
A Laser Heater for CompactLight FEL
S. Di Mitri, G. Perosa
Elettra Sincrotrone Trieste & University of Trieste

## Slide 2
The problem
kFEL = hkseed  mkubi
@ FERMI
magnetic compressor
linac
density mod.
energy mod.
LSC
R56, CSR
compression & amplification
  1 – 10 m
Peak at
uBI  4 m
uBI  7 m
SASE
Self-seeding
G. Marcus et al., PRAB 22 (2019)
,slice > FEL,
Lower FEL intensity
MBI  coh,
Larger FEL bandwidth

## Slide 3
A solution
A tool to increase the initial beam uncorrelated energy spread, 
damping
amplification
Gain = amplification of modulations
Why in a chicane ?
To wash out the laser modulation,
For laser injection collinear to the e-beam, and extraction.

## Slide 4
Modelling the microbunching instability
Input:
beam parameters at 100 MeV;
initial SES from tracking runs (2 keV @ 75 pC);
Linac gradients;
Compression factors (bunch core);
Emittance and average betatron functions.
Collective effects:
1.5-D LSC and CSR impedance;
2-D laser heater;
Intrabeam scattering;
transverse and longitudinal Landau damping.
Output:
spectral gain;
energy modulation;
SES (equivalent)

## Slide 5
Do we really need a LH ?
HX FEL: 4 kA @ 5.5 GeV
SX FEL: 4 kA @ 1.9 GeV

## Slide 6
A closer look to the energy spread
SX FEL: SES vs. LH at the spreader end
HX FEL: SES vs. LH at the linac end
The linear trend (---) corresponds to MBI fully damped.
Deviation from it (-.-.-) sets the minimum LH level for damping.
Although not essential for lasing, LH is highly recommended for an optimized brilliance

## Slide 7
Beam energy:
at as low energy as possible since damping  ELH/E0 (< 200 MeV or so)
better control if out of the beam space charge regime (> 80 MeV or so)
Laser:
short lambda for more efficient smearing of the laser modulation (1 or 0.5 micron)
must tolerate 1 kHz rep. rate (expected 10 mW average power)
Chicane:
bending angle is a compromise between length, laser injection, smearing and CSR-induced emittance growth (typically < 6 deg)
Should include 2 view screens and 2 BPMs
Undulator:
undulator period has to match the beam energy (typically, few cm)
the number of periods is a compromise between max. heating and coupling to the laser bandwidth (10 periods are usually enough)
Guidelines to LH design

## Slide 8
Design – educated assumptions
Educated assumption: Nund=8, Bund = 0.4 T
(depends on gap and period length)
From simulations:
ex,y = 70 m, E=110 MeV @ und (still ok up to 130 m, 150 MeV)
From instability model: E,LH  30 keV
(larger values from higher laser energies)
On the shelf: Yb laser @ 1064 nm. Spill 2nd harmonic from the PIL

## Slide 9
Design – optimization
With assumptions in the previous slide, the laser power only depends on the undulator period:
Power = 1 MW
gap = 30 mm
K = 1.2 (0.4 T)

## Slide 10
Design – chicane
For large smearing of the laser modulation, we impose: 18 mm.
emittance growth from laser interaction in a dispersive region
emittance growth CSR in a chicane
L = 0.1 m
 = 5.2 deg  Ldip = 0.1 m
x = 0.05%
Total LH length including diagnostics is  1.5 m
Does not need dedicated matching quads
At least 30 keV added

## Slide 11
Conclusions
Microbunching instability in CompactLight is not expected to be a show stopper.
A laser heater is highly recommended to maximize the FEL brilliance, especially for seeded schemes.
Tens’ of keV energy spread at 1 kHz are guaranteed in a 1.5 m-long insertion.
Thank you for Your kind attention – questions are very welcome