## Slide 1: FastCaloGAN: a fast simulation for the ATLAS calorimeter system using GANs
Michele Faucci Giannelli,
On behalf of the ATLAS collaboration
30/11/2020

## Slide 2: Motivation and strategy
Simulation has the largest CPU consumption
→ this will only increase in time
Calorimeters require the most CPU
→ we need a fast calo simulation
FastCaloGAN provides a full system calorimeter fast simulation using 300 Generative Adversarial Networks: ATL-SOFT-PUB-2020-006
The detector is segmented in 100 slices in η (0.05 wide)
  In each slice 15 energy points are used to train a GAN
  Three GANs are trained for electrons, photons and pions in each slice
The trained generators are used to simulate HITS in the ATLAS Athena software framework

## Slide 3: The GAN
Train the GANs on voxelised hits
NVoxel depends on PID and η

## Slide 4: Training

## Slide 5: Performance of the GANs
Differences within a few %

## Slide 6: Performance on di-jets events
AFII is the current ATLAS fast simulation, used for producing ~50% of MC samples

## Slide 7: Conclusion
FastCaloGAN use 300 GANs to simulate the interaction of photon, electrons and pions in the ATLAS calorimeter system
The GANs can reproduce the G4 distribution within a few %
FastCaloGAN outperform the current fast simulation (AFII) in the boosted regime
FastCaloGAN is being considered as one component of the next generation fast calorimeter simulation in ATLAS

## Slide 8: Backup

## Slide 9: Result of the training
Best epoch selected as the minimum χ2 calculated from the comparison between G4 and the generated events from all energies
Best epoch

## Slide 10: Simulation of single particles