## Slide 1
Arjan Verweij, 10/6/2020
Issues related to software, instrumentation, data acquisition, observed by MP3 during previous HWC campaigns
Zinur Charifoulline, Arjan Verweij, 10 June 2020

## Slide 2
Issues with hardware have triggered our continuous wish to improve the possibilities for post-mortem analysis (higher sampling rate, better resolution, more channels, etc).
The long time-span of the LHC, the long period between HWC campaigns, and rather small number of issues during operation, also calls for a coherent approach for analysis.
The following slides show a mix of issues linked to data acquisition, instrumentation, software and communication that were discussed by the MP3 in the last 10 years, that hopefully can be resolved in the future, possibly as part of future IST campaigns.
For sure, all systems work close to perfect but, due to our progressive insight in the LHC (especially for interplay between systems) and due to changes in systems, we still see some room for improvement.
Intro
Arjan Verweij, 10/6/2020

## Slide 3
PM analysis requires timing accuracy of 1 ms between PC, QDS, EE, QHs, PIC and BLMs (in case of beam-related events). We observed many timing issues, with errors up to O(1 sec).
  iQPS: PM timestamp and PM timescale are sometimes shifted
  iQPS PM with respect to nQPS PM
  600 A circuits: QDS signals with respect to FGC signals
  Beam induced quenches: QDS with respect to BLM
  iQPS voltages with respect to QHs
Timing errors
Arjan Verweij, 10/6/2020
A14R8:U_QS0
~800ms
A31R1:U_QS0 (iQPS)
A31R1:U_DIODE_RB (nQPS)

## Slide 4
Especially in non-standard cases (earth fault, QH problem, …) signals could be saturated. A good balance between signal resolution and maximum input should be discussed.
  iQPS: U_1, U_2 (high range, limited resolution), U_QS0 (limited range, high resolution )
  nQPS: U_EARTH (voltage feelers)
  FGC: I_EARTH (I_sat=54 mA, fuse blows at 1-3 A, FPA in RB gives I_earth > 54 mA)
Signal saturation & resolution
Arjan Verweij, 10/6/2020
A12.RB:IEARTH
A31R1:U_1
A31R1:U_2
A31R1:U_QS0

## Slide 5
High sampling PM data have limited duration, and trigger point is not always correct.
PM duration
Arjan Verweij, 10/6/2020

## Slide 6
Toggling was implemented in the Logging DB to store the signals from board A and B for all QDS units. (Important for the nQPS to deduce the resistance of the diode leads during a quench)
‘Toggling’
Arjan Verweij, 10/6/2020
Solution: Logging DB should contain both signals from boards A and B. The signals names should reflect the board, e.g.: U_xxx_A and U_xxx_B

## Slide 7
QPS voltage signals of the 2 apertures of many IPQ magnets were swapped with respect to FGC signals.
B1 vs B2 swap
Arjan Verweij, 10/6/2020
Solution: Check with tiny current (<100 A) during IST (or eventually a check can be added during PIC2 test).

## Slide 8
Very frequently one or more of the voltage feelers in an RB circuit show zero voltage.
Voltage feelers
Arjan Verweij, 10/6/2020

## Slide 9
Not always clear if thresholds for analysis coming from the system experts are ‘warning’ levels or ‘alarm’ levels.
Thresholds for analysis
Arjan Verweij, 10/6/2020
Solution: Re-iterate with system experts, and have ‘warning’ and ‘alarm’ for some signals.
Examples:
600 A: circuit resistances
DFB temperatures and valve opening
nQPS: bus bar resistances
Current differences / drift (QDS and FGC in 600 A)
EE analysis
Number of expected quench files (not always clear)

## Slide 10
Signal names are not always intuitive.
Signal names of boards A and B are the same.
Signal names
Arjan Verweij, 10/6/2020
Confusion between nQPS crate name and iQPS magnet name
IPD: strange naming for some circuits
Busbar segment naming
IPD and IPQ: B1 and B2 are not linked to beam 1 and beam 2
RQD/F versus int/ext versus B1/B2

## Slide 11
Signal names (or correspondence?) have to be the same for Front End, PM and Logging DB.
Signal names consistency
Arjan Verweij, 10/6/2020
PLI3.b1: RSD1.A12B1
RSD1.A12B1:U_DUMP_RES
RSF1.A12B1:U_DUMP_RES
RSD1.A12B1:I_MEAS
The list of the 600AEE-circuits, where the EE logging data are swapped:
  DQEMC.UA23.RSD1.A12B1 <-> DQEMC.UA23.RSF1.A12B1
  DQEMC.UA23.RSD1.A12B2 <-> DQEMC.UA23.RSF1.A12B2
  DQEMC.UA23.RSD2.A12B1 <-> DQEMC.UA23.RSF2.A12B1
  DQEMC.UA23.RSD2.A12B2 <-> DQEMC.UA23.RSF2.A12B2
While the PM-data for QDS (DQAMGNA) and for EE (DQAMSN600) are correct.

## Slide 12
We work with analysis tools written by many people and which are not coherent (different access, loading, saving, buttons, graphs, colors, formats, …)
Different tools
Arjan Verweij, 10/6/2020
Solution: We are heading for analysis tools (notebooks, Python-based) that came as spin-off from the ‘Signal Monitoring Project’.
Labview tools from several people from Adriaan’s/Odd’s section
Labview tools from Zinur
Tools for analysis of EE (Arek -> MS section) and PIC (LV for mains, eDSL for 600 A)
eDSL (MS section)

## Slide 13
QDS of four 600 A circuits on the same crate -> trip
Opening EE -> trip
Firing QHs -> trip
Quench in MB in cells 8-10 can trip IPQ
Mutual coupling between busbars
Coupling in the DFB
Parallel execution of powering tests
Arjan Verweij, 10/6/2020
Analysis of HWC tests / quenches / trips is often complicated due to the execution of powering tests of circuits that have known mutual coupling.

## Slide 14
Tests to be signed in AccTesting, PMEA, and/or LabView tools, and in the future also Swan notebooks.
Not always clear where to sign and if signatures are communicated between PMEA and AccTesting.
Test signatures
Arjan Verweij, 10/6/2020

## Slide 15
Transfer of PM files of the RB and RQ circuits takes very long, especially for snapshots.
No bottleneck for timely quench analysis (in shadow of re-cool-down of the sector), just a bit annoying.
Long duration for data transfer
Arjan Verweij, 10/6/2020
MTF
We are still writing lots of results to MTF, although I think nobody ever tried to extract something.
Is this useful? It might be much easier and more correct to re-analyse data from the past with one well defined tool.