J/Ψ measurement in 7 TeV pp collisions at mid-rapidity in the e+e- channel with ALICE
Ionut Arsene
for the ALICE Collaboration

---
Contents
- Introduction
- ALICE experiment
- Analysis
  - Cuts
  - Efficiencies
  - Signal extraction
  - Systematics
- Results and discussion
- Outlook
- Summary

---
Introduction
p + bar{p} @ sqrt {s} = 1.8 TeV
J/Ψ production mechanisms:
- Direct production via the interaction of initial partons
- Feed-down from charmonium states, mainly Ψ(2S) and χc (~35% of prompt production rate)
- B-hadron decays (10% of the inclusive J/Ψ cross-section at Tevatron at Pt=1.5 GeV/c)
CDF Collaboration, PRL 79 (1997) 572
CDF Collaboration, PRL 79 (1997) 578

---
Introduction
Some of the most remarkable approaches to explain the quarkonium production:
- Color Singlet Model (CSM) S.D.Ellis, M.B.Einhorn, C.Quigg, PRL 36 (1976) 1263
- Color Evaporation Model (CEM) H.Fritzsch, PLB 67 (1977) 217
- Non-relativistic QCD G.Bodwin, E.Braaten, G.Lepage, PRD51 (1995) 1125

---
The ALICE setup

---
Time Projection Chamber
557,568 readout channels
Central electrode at 100 kV
94 μs maximum drift time
90 m3 gas volume
Ne - CO2 – N2 (85.7-9.5-4.8)
Very good momentum resolution (~10% at 20 GeV/c)
Particle identification via linear energy loss (dE/dx)

---
Inner Tracking System
6 layers, three technologies:
- Silicon pixels (0.2 m2, 9.8M channels)
- Silicon drift (1.3 m2, 133k channels)
- Silicon strip (4.75 m2, 2.6M channels)
- Material budget ~1% X/X0 per layer
Rejection of electrons from conversions by requiring a hit in the two innermost layers
The extraction of the fraction of J/Ψ's from b-hadron decays is posible via the reconstruction of secondary vertices. This analysis requires high statistics and is in progress.

---
Analysis
- Cuts
  - Kinematics
  - Track selection
  - Particle identification
- Signal extraction
- Efficiencies
- Systematics

---
Kinematic cuts
Monte-Carlo: Single unpolarized J/Ψ
- Fiducial rapidity cut to avoid detector edge effects
- Pt cut on the electrons to reject background without loosing too much in efficiency
  ALICE can measure J/Ψ's down to Pt=0 at mid-rapidity
abs {y^{J/%PSI}} < 0.88, abs {%eta_{legs}} < 0.88
p_{T}^{e} > 1.0 GeV/c

---
Track selection
Spatial distribution of photon conversion points
Select only well defined TPC tracks:
  - # TPC clusters > 90/159
  - χ2 / cluster < 4
- Rejection of kink daughters
- Rejection of secondaries
  - DCA to event vertex cut
Rejection of electrons from conversions:
  - At least one hit in the first 2 ITS layers (SPD)

---
Particle identification
TPC dE/dx
Particle identification uses the Bethe-Bloch parameterization of the linear energy loss (dE/dx) in the TPC
- Electron selection is made in a ±3σ band around the Bethe-Bloch curve.
- Pions and protons are rejected in ±3σ bands around their Bethe-Bloch curves.

---
Signal extraction
- Like sign substraction method :
- Some residual background still remains after the like-sign subtraction (R~1.04)
- The signal shape is in agreement with the Monte-Carlo simulation
- 69% of the total yield is in the integration range 2.90-3.15 GeV/c2
S = N_{PM} - 2 R sqrt{N_{PP} times N_{MM}}

---
Efficiencies
Monte-Carlo: Pythia + 1 J/Ψ per event
- Efficiencies are calculated using Monte-Carlo simulations matching the exact setup of ALICE at the moment the data were taken.
- Differential J/Ψ efficiencies are factorized in 3 different contributions:
  - Kinematics
  - Tracking
  - Particle identification

---
Systematic errors
Mismatch between data and Monte-Carlo	10%
Particle identification cuts	10%
Normalization (mainly due to uncertainty on the / LHC beam intensity)	10%
Signal extraction range	4%
J/Ψ Pt spectrum assumption	1%
We are still working on decreasing our systematics

---
Systematics from J/Ψ polarization
Monte-Carlo: Pythia + 1 J/Ψ per event
{dN} over {d cos(%theta)} sim 1 + %alpha times cos^2(%theta)
Uncertainty considering the extreme cases:
Reference frame	α = -1	α = +1
Collins-Soper	+24.8%	-11.9%
Helicity	+19.7%	-9.7%

---
Systematics (MC vs. data)
- The material budget is very well understood in our simulations.
- We observe a disagreement between data and Monte-Carlo for the distribution of the number of TPC clusters.
- We apply a correction for this (~3%)

---
J/Ψ production cross-section
left ( {d%sigma_{J/%PSI}} over {dy} right )_{y=0} = {{1} over {L_{i nt}}} times {{N_{J/%PSI}} over {(eff) times %DELTA y times (B.R.)}}
(eff.) = (kinematics) x (track quality) x
        (PID) x (Minv integration range)
(B.R.) = (J/Ψ→e+e-) branching ratio
{1} over {L_{i nt}} = {{1} over {N_{CINT1B}}} times left ( {{N_{CINT1B}} over {N_{V0and}}} right )_{reference} times %sigma_{V0and}
CINT1B – inelastic trigger used in the analysis
V0and – non-single diffractive trigger with cross-section measured in a Van der Meer scan
int L^{ee} dt = 1.5 nb^{-1 }
%sigma_{V0and} = 62.3 +- 6.2(syst.) mb
Total luminosity accumulated ~ 10.0 nb-1, but final refinements from detectors are still ongoing

---
Energy dependence
int L dt = 1.5 nb^{-1 }
- Solid line is a NLO calculation for the c-cbar cross-section scaled to the CDF data.
- Our data is consistent within errors with the lower energy experiments
PHENIX Collaboration, PRL 98 (2007) 232002
CDF Collaboration PRD71 (2005) 032001

---
Pt dependence
int L dt = 4.0 nb^{-1}
The Color Evaporation Model calculations underestimates the data at low transverse momentum.
Data is from a larger sample with partial calibration and it is not fully normalized yet.

---
Outlook
Extending of the particle identification with TOF and TRD detectors
Measure J/Ψ polarization
- Trigger on events with at least one or two tracks above 1 GeV/c. This will significantly increase the number of measured J/Ψ's in the high event rate provided by LHC.
- Analyze the fraction of J/Ψ's originating from beauty decays.

---
Using PID with TOF and TRD
- TOF improves the background rejection at low momentum (p<3 GeV/c)
- TRD improves electron identification at high momentum

---
Future J/Ψ Polarization measurement
Monte-Carlo: Single J/Ψ
- Will significantly reduce the systematic error due to polarization
- Very interesting observable by itself and provides information on the production mechanisms
- ALICE has a very good acceptance for polarization measurements
- J/Ψ polarization is not well understood by theory
CDF Collaboration, PRL 99 (2007) 132001

---
Summary
- We presented the mid-rapidity J/Ψ production cross section in non-single diffractive p+p collisions at 7 TeV extracted via the di-electron channel with the ALICE barrel detectors.
- The measured cross-section at mid-rapidity is consistent with the c-cbar cross section from an NLO calculation scaled to the J/Ψ yield from CDF data.
- The Pt dependence at low transverse momenta does not follow the CEM calculations
- With more statistics from future running the polarization measurements will be posible. This will decrease our systematics and provide a valuable observable.
- We are looking forward to the heavy ion collisions run from LHC!