## Slide 2: A simple coke can…
A typical 330 ml coke can, resembles a cylindrical cavity.
Field solutions can be found analytically with the correct boundary conditions.
  TM and TE modes (see lecture notes)
TM010 – accelerating mode.
  Resonant frequency given by:
  c – speed of light
  D – diameter
  x1 – 2.40483
f=~3.5 GHz
~65.6 mm
~115.2 mm

## Slide 3: 2D Model
Model A
Superfish
  2D cylindrical symmetry assumed.
Geometry
Mesh

## Slide 4: 2D Model
Model A
Superfish
Field normalisation: 1J stored energy/cavity
f=~3.548 GHz
Field Lines
1D Field Line (Ez on axis – full can)

## Slide 5: 3D Model
Model B
CST MicroWave Studio
Symmetric (like the 2D model)
Geometry
Mesh

## Slide 6: 3D Model
Model B
CST MicroWave Studio
f=~3.549 GHz
Electric Field
Magnetic Field

## Slide 7: 3D Model
Model B
CST MicroWave Studio
  Field Normalisation: 1J stored energy/cavity
1D Field Map (Ez on axis)
Comparison with the 2D Superfish result

## Slide 8: 3D Model
Model C
CST MicroWave Studio
Asymmetric (closer to an actual coke can geometry)
Geometry
Mesh

## Slide 9: 3D Model
Model C
CST MicroWave Studio
  Different scaling
f=~3.531 GHz
Electric Field
Magnetic Field

## Slide 10: 3D Model
Model C
CST MicroWave Studio
  Field Normalisation: 1J stored energy/cavity
1D Field Map (Ez on axis)
Comparisons…

## Slide 11: 3D Model
Model D
CST MicroWave Studio
Most Details (curves, corners, etc)
Geometry
Mesh

## Slide 12: 3D Model
Model D
CST MicroWave Studio
  Different scaling
f=~3.398 GHz
Electric Field
Magnetic Field

## Slide 13: 3D Model
Model D
CST MicroWave Studio
  Field Normalisation: 1J stored energy/cavity
1D Field Map (Ez on axis)
Comparisons…

## Slide 14: 3D Model
Model E
CST MicroWave Studio
Full Details Imported CAD Model (www.grabcad.com)

## Slide 15: 3D Model
Model E
CST MicroWave Studio
Geometry
Mesh

## Slide 16: 3D Model
Model E
CST MicroWave Studio
  Different scaling
f=~3.371 GHz
Electric Field
Magnetic Field

## Slide 17: 3D Model
Model E
CST MicroWave Studio
  Field Normalisation: 1J stored energy/cavity
1D Field Map (Ez on axis)
Comparisons…

## Slide 18: Experimental Measurement
Network Analyser: Rohde & Schwarz ZNB8
  Frequency
  Q-factor