## Slide 1: L4 Test Bench Dump Design
Cesare Maglioni ‹
EN/STI-TCD b
May 4, 2010

## Slide 2: Parameters
Dump and beam
    Dumping system : fixed, in vacuum
    beam : 65mA, 100ms pulse, 1Hz rep rate both @ 3MeV and 12MeV
Considerations
    Layout : dimension limitations, integration (SEM-GRID interface)
    Energy (density) deposition and Power evacuation
    Mechanical stability: stress and deformation minimization
    Vacuum tightness and effectiveness, minimization of vacuum degradation risks
    Handling : weight, maintenance
    Water cooling only if necessary (operation rate, ..)
C. Maglioni L4 Test Bench Dump - May 4, 2010 2

## Slide 3: Test Bench Layout
C. Maglioni L4 Test Bench Dump - May 5, 2010 3
Diagnostic beam
Main beam
    2 dumps, 2 energy levels → 1 design

## Slide 4: Actual Dump design
C. Maglioni L4 Test Bench Dump - May 5, 2010 4
Flange - interface with SEM-GRID
5.5
Water Cooling
Beam
Stainless Steel Vacuum vessel
Core:
solid Aluminum (6063) sectioned cylinder (absorber core)
Seal
640mm

## Slide 5: Actual Dump on Layout
C. Maglioni L4 Test Bench Dump - May 5, 2010 5

## Slide 6: Actual Dump design
C. Maglioni L4 Test Bench Dump - May 5, 2010 6
Flange - interface with SEM-GRID
5.5
Water Cooling
Beam
Stainless Steel Vacuum vessel
Core:
solid Aluminum (6063) sectioned cylinder (absorber core)
Seal
?
Needs
RP
?
May be increased
-> shorter dump

## Slide 7: Dump design
C. Maglioni L4 Test Bench Dump - May 4, 2010 6
3MeV NON-DIFFUSIVE ADIABATIC MODEL:
235 J/cm3/pulse peak
@ ~ 3.5 m depth
DTpeak ~ 108 K (Fluka)
DTpeak ~ 98 K (Ansys)
r () = 42.1 m
12MeV NON-DIFFUSIVE ADIABATIC MODEL:
87 J/cm3/pulse peak
@ ~ 40 m depth
DTpeak ~ 51 K (Fluka)
DTpeak ~ 37 K (Ansys)
r () ~ 41.7 m
Thermal diffusivity :
 = k/Cp [m2/s]
Hold the relation :
 r2 =   
 = pulse length
r = characteristic diffusivity length
3MeV DIFFUSIVE (ADIABATIC) MODEL:
DTpeak ~ 50 K (Ansys)
12MeV DIFFUSIVE (ADIABATIC) MODEL:
DTpeak ~ 20 K (Ansys)

## Slide 8: Energy deposition
Chart: 3MeV, energy density and DT distribution
C. Maglioni L4 Test Bench Dump - May 4, 2010 8
mesh size

## Slide 9: Temperature distribution
C. Maglioni L4 Test Bench Dump - May 4, 2010 7

## Slide 10: Deformations
C. Maglioni L4 Test Bench Dump - May 4, 2010 9
Maximum)

## Slide 11: What next
Some improvements (if needed) …[ongoing]
Final design guidelines to Design office …[ongoing]
Technical/Engineering Spec Definition …[ongoing/end May]
Production of Technical Drawings …end June/July
Manufacturing
    Dump Core (Main workshop) …end September/October
    Steel vessel (EN\STI-TCD workshop) …end September
Dump Assembly (EN\STI-TCD workshop) …end November
Cooling, vacuum testing (EN\STI-TCD workshop) …mid December
Installation …end December
C. Maglioni L4 Test Bench Dump - May 5, 2010 11

## Slide 12: Thank You 
Cesare Maglioni ‹
EN/STI-TCD b