## Slide 1: New Spiral Load RF Design
09.09.2020
Hikmet Bursali, Alexej Grudiev

## Slide 2: Outline
Motivation
Straight Load Model
Design Process
  Straight to Spiral Model
  Spiral Model with WR90 Transition
  Spiral Model with Vacuum Holes
  Spiral Model with Pumping Port
Reflection Optimisation
Final RF Model
Conclusion & Future Work

## Slide 3: Reminder
Why do we use RF loads?
In order to absorb remaining RF power passing through the RF system. (Not used for beam acceleration or dissipated on resistive walls.)
(Ex: TD26CC Pin= 43.3MW – unloaded for 100MV/m)*
Where do we use RF loads?
At the RF output of traveling wave type structures.
RF Load
Power Source
Beam Direction
Traveling Wave Linac
*https://edms.cern.ch/document/1078698/1

## Slide 4: X-Band RF Loads (produced by Additive Manufacturing)
We have several RF spiral loads which were designed (CLIACOMP0071
, CLIACOMP0094), fabricated (at CERN or Vendor companies) and tested successfully. (Materials; Stainless-Steel “316L”, Titanium alloy “Ti6A14V”)
For more info, please see the document;
https://edms.cern.ch/document/2323664/1
The current designs allow to produce only one load during an additive manufacturing cycle because of 45° oblique placing and 3D printing machine dimensions.
*Photos from Romain Gerard
*
*
Support parts
(removing after production)
Spiral Load in 3D printing machine

## Slide 5: Motivation
The aim of this study is to optimise the internal cross-section of RF loads in order to create a stackable design to increase number of products per additive manufacturing cycle and so decreasing the unit price.
Previous RF Design with rectangular internal cross section
with 45° oblique placing to allow additive manufacturing
New cross-section
Placing directly (without 45°)
Less space allowing stackable design (allows producing more than one load during one manufacturing cycle)
Material saving with reducing material for support parts (cost reducing)
*
45°
45°
45°
45°
90°
*Development of X Band High Power RF Load for CLIC Applications Using Additive Manufacturing Techniques; D’Alessandro, Gian Luigi (https://cds.cern.ch/record/2139981?ln=en)
Current cross-section

## Slide 6: Straight Model Reference Design
*Development of X Band High Power RF Load for CLIC Applications Using Additive Manufacturing Techniques; D’Alessandro, Gian Luigi (https://cds.cern.ch/record/2139981?ln=en)
The dimensions of previous design were used directly and optimised with the new cross-section.
Model with new cross-section
Previous model with rectangular cross-section
Ti6A14V
Conductivity: 6.105 S/m
Tapered part
Straight Part
Parametric Design

## Slide 7
Electric Field (Complex Magnitude)
Line for E-field & Poynting Vector Calculation

## Slide 8
BE-RF-MK
Poynting Vector
Line for E-field & Poynting Vector Calculation

## Slide 9
BE-RF-MK
Line 1
Line 2
The peaks are at the junction place of tapered and straight parts.

## Slide 10
BE-RF-MK
Reflection

## Slide 11: Straight Model on HFSS-Parameters
H2=14.3mm
H1=14.3mm
L2=1.2m
L1=1.7m
w1=2mm
w2=2mm
b=10.16mm
a=22.86mm
Total Length=3.067m
WR90 Waveguide Dimensions

## Slide 12: Design Process
12
RF Simulations
(HFSS)
Mechanical Model by Design Team*
(CATIA)
*Oleg Gumenyuk, Benoit Riffaud, Romain Gerard
Meetings
&
Feedbacks
&
Updates
Parametric Model from Design Team

## Slide 13: Straight to Spiral Model
Transition part
Tapered part
Straight part
Starting section to make spiral

## Slide 14: Straight Model with WR90 Transition
Oleg Gumenyuk
Model with Bent Transition
Model with Straight Transition
RF simulations for transition parts to select the model.

## Slide 15
Better reflection!
S-parameters (dB)

## Slide 16
Spiral Model Dimension Parameters
a
w0
H0
Connection
Connection
2mm (gap)
H1=H2
2mm (gap)
w1=w2
End of the load
(Same cross-section)
b
Same straight design parameter dimensions were used on spiral model.
(22.86mm)
(10.16mm)
(5mm)
(25mm)
(14.3mm)
(2mm)

## Slide 18: Spiral Model with Vacuum Holes
vacuum holes with 2mm diameter

## Slide 19
Frequency shift
due to holes
~350 MHz
Model with holes
Model without holes
Frequency shift due to vacuum holes
11.9942 GHz
To compensate frequency shiftChanging H2 from 14.3 to 14.6mm

## Slide 20
Spiral Model Dimensions (Updated)
22.86mm
5mm
25mm
Connection
Connection
2mm (gap)
H2
14.6mm
2mm (gap)
2mm
End of the load
(Same cross-section)
10.16mm

## Slide 21
Model with holes
(H2=14.6mm)
H2 determines cut-off frequency
Frequency shift due to vacuum holes
Model with holes
(H2=14.3mm)
Model without holes
(H2=14.3mm)
There is a peak at our target frequency!
11.9942 GHz

## Slide 22
Reflection Improvement on HFSS
There is a peak @ 11.9942 GHz
Model with holes
H2=14.6mm

## Slide 23
Inner waveguide of model has vacuum holes both sides.
Outer face of model has vacuum holes only one side, this causes reflection cumulation at the last hole (under transition part).
Tuning holes
To overcome this; we have added different number of tuning holes to see how reflection changes.

## Slide 24: Spiral Model with Pumping Port
Oleg Gumenyuk
CF16 Vacuum Flange

## Slide 25: Reflection (model with vacuum port)
11.9942 GHz
2 tuning holes with 2mm diameter

## Slide 26
11.9942 GHz
3mm
Reflection Optimisation
Material: Ti6A14V
(σ= 6.105 S/m)
1 tuning hole with 3mm diameter

## Slide 27: Electric Field & Surface Loss Density @12GHz
Input Power=1W

## Slide 28: Final Model (in HFSS)
Upper View
Tuning hole
Side View
Mechanical Design by Oleg Gumenyuk

## Slide 29: Final Model (in CATIA)
Pedro Morales Sanchez
Internal Views
Side Views

## Slide 30: Conclusion & Future Work
RF Design of spiral load with new cross-section is ready!
(https://edms.cern.ch/document/2404437/1)
Cooling Circuit Integration
Mechanical Design (Ongoing by Pedro Morales Sanchez)
Thermal Simulations
Production by Additive Manufacturing
RF Test

## Slide 31: Thank you for your attention!
Special thanks to;
Nuria Catalan Lasheras, Benoit Riffaud, Oleg Gumenyuk, Romain Gerard, Joel Sauza Bedolla, Pedro Morales Sanchez

## Slide 32: Backup Slides

## Slide 33
Spiral Model Dimensions-Final Version
22.86mm
5mm
25mm
Connection
Connection
2mm (gap)
14.6mm
2mm (gap)
2mm
End of the load
(Same cross-section)
10.16mm
(a)
(w0)
(H0)
(H1)
(w1)
(b)
(H2,w2)

## Slide 34
11.9942 GHz
S11 without roughness
S11 with *50 um roughness
* Average roughness for Ti alloy
M.Heretis, P.Spanoudakis, N.Tsourveloudis, ‘’Surface Roughness characteristics of Ti6Al4V alloy in conventional lathe and mill machining’’, Technical University of Crete, p.5 2009
Spiral Model without vacuum port