## Slide 1: Test Platform for Automated Scan of Multiple Sensors

## Slide 2: Test Platform for Automated Scan of Multiple Sensors
The CMS MTD: MIP Timing Detector for HL-LHC
UFSDs for the MTD End Caps
Characterization of a Timing Detector
Development of an automated scanning platform:
  Magnetic spectrometer for Sr90
  Trigger and time reference
  Hardware: designed using easily available and accessible components
  Software: custom control and measurement software/firmware
Generic problem!

## Slide 3: CMS MIP Timing Detector
x
y
x
y
t
A precise timing detector can be used for Particle Identification or for pile-up suppression
Barrel Timing Layer LYSO + SiPM
Endcap Timing Layers (ETL) LGADs
z (cm)
t (ns)
200 pileup interactions in 4D space
CMS MIP Timing Detector:
30-40 ps timestamp for every track
Spurious track-to-PV association suppressed by factor of ~3

## Slide 4: UFSDs for the MTD End Caps
Using UFSDs for a “CMS size” detector poses many challenging
Two disks of UFSDs (per side) :
Average 1.8 hits per track
Designed for σ < 50 ps per hit
Pad size: 1.3 x 1.3 mm2
High fill factor (>85% per layer)
16624 sensors of 2x4 cm2
  Up to 2x1015 neq/cm2 for 15% of sensors
  Less than 4x1014 neq/cm2 for 50% of sensors

## Slide 5: LGAD read out by the ETROC
Ultra Fast Silicon Detectors (UFSDs) are Low Gain Avalanche Diodes (LGADs) optimized for timing measurements employing a thin multiplication layer to increase the output signal at the passage of a particle of a factor ~20
Time precision: 25~30 ps
The low-gain mechanism, obtained with a moderately doped p-implant, is the defining feature of the design.
The low gain allows segmenting and keeping the shot noise below the electronic noise, since the leakage current is low.
DAC
Waveform sampling
Charge Injection
Bump pad
PreAmp
Discriminator
Pulse Injection
PLL
Phase Shifter
I2C
Fast Control
16 x 16
channels
65 nm
Digital
Buffer and Read-out
TOA
TOT
  Main requirements:
  ASIC contribution to time precision <40 ps
  Power consumption: <4 mW/ch (80 kW total)
  Trigger rate: Up to 1 MHz

## Slide 6: Characterization of a Timing Detector
~50 μm LGAD
Silicon substrate
PCB with hole under the sensor
Time reference
SiPM or MCP-PMT
If a particle hits the scintillator, for sure it crossed the LGAD as MIP
~50 μm LGAD
Silicon substrate
ETROC
PCB
i.e., complete modules, with cooling plates…
Common approach (with radioactive source):
Not Extensible! Not Flexible!
To characterize a timing detector it is mandatory to have a precise time reference
Time reference
SiPM or MCP-PMT

## Slide 7: Characterization of a Timing Detector
~50 μm LGAD
silicon
ETROC
PCB
Precise timing and low material budget (no MCP-PMT…)
To characterize a timing detector it is mandatory to have a precise time reference
Time reference
SiPM or MCP-PMT
it should still be MIP after passing through the time reference
Possibilities:
Thin plastic scintillator
Thin plastic Cherenkov radiator
Ultrathin silicon sensor

## Slide 8: MIP portable source
The design goal is to have a compact source with a trigger and a time reference before the sensors
~0.5 MeV/mm
Chart: Beta energy (MeV)
Chart: Range (mm)
| 0 | 0.27110000000000001 | 0.54039999999999999 | 0.80699999999999994 | 1.069 | 1.198 | 1.3250000000000002 | 1.4490000000000001 | 1.57 | 1.6880000000000002 | 1.7999999999999998 | 1.9059999999999999 | 2.0049999999999999 | 2.0590000000000002 | 2.1079999999999997 | 2.1390000000000002 | 2.1659999999999999 | 2.1790000000000003 | 2.1909999999999998 | 2.202 | 2.2120000000000002 | 2.2159999999999997 | 2.2200000000000002 | 2.2239999999999998 | 2.2279999999999998 | 2.2320000000000002 | 2.2349999999999999 | 2.2370000000000001 | 2.2400000000000002 | 2.2410000000000001 | 2.242 | 2.2429999999999999 | 2.2429999999999999
Range | 0.3682 | 0.3699 | 0.3729 | 0.3777 | 0.3855 | 0.3909 | 0.3979 | 0.4069 | 0.4188 | 0.4345 | 0.4563 | 0.4874 | 0.5348 | 0.5766 | 0.6359 | 0.6913 | 0.7675 | 0.8175 | 0.8791 | 0.9568 | 1.058 | 1.121 | 1.196 | 1.286 | 1.395 | 1.532 | 1.71 | 1.948 | 2.289 | 2.576 | 2.965 | 3.315 | 3.779
1 MeV electron in Silicon
Selecting electrons with >1 MeV, after 1 mm of Si, they’ll still be MIPs
Spectrum of Sr90 and Ru106
Both radioactive sources emit >20% (25% for Sr90) of the electrons with >0.9 MeV
Ruthenium-106 Half-Life ~ 370 days
Strontium-90 Half-Life ~ 29 years
https://nucleonica.com/

## Slide 9: Source spectrometer
The design goal is to have a compact source with a trigger and a time reference before the sensors
Source: Sr90
Magnets with fine tunable support
Selection Slot
Rotating support
Collimator
Trigger and time reference
Simulations show that it is possible to select >1MeV using small permanent magnets

## Slide 10: Radioactive Source Spectrometer
First prototype built and tested; a second prototype is in production.
37 MBq (1 mCi)
Holder with collimator
Permanent magnet spectrometer
Open/close
~2 mm opening
Momentum selector tested
Remotely controlled shutter
Commercially available Sr90

## Slide 11: Trigger System: thin plastic scintillator
Trigger generated by plastic scintillators read out by SiPM
SiPM 3x3 mm2 or 1x1 mm2
Charge (A.U.)
SMA output
Plastic scintillator read out on both sides
(for coincidences)
Small “all-in-one” boards with SiPM and amplifier, available for 1x1 mm2 and 3x3 mm2 (compatible with different brands of SiPM)
Amplifier
# of photoelectrons
MICROFC-30050-SMT-TR1
MICROFC-30050-SMT-TR1
2 photoelectrons

## Slide 12: Trigger System: thin plastic scintillator
Trigger generated by plastic scintillators read out by SiPM
t2
t1
Time precision of single measurement:
Time precision of combined measurement:
Time reference
SiPM or MCP-PMT
Still work to do…

## Slide 13: Time reference system: “ultra-thin” LGAD
Trigger generated using an ultra-thin silicon sensor that can provide also a time reference
KU MoVe-IT 8ch board
MoVe-IT LGAD sensor
KU 8ch board
ETL 5x5 LGAD
Prototype of thin LGAD designed for Hadrotherapy
Thickness ~150 um
The first prototypes were affected by “pop-corn noise”, therefore the sensor was not operated in ideal conditions
8 ch board designed for linearity up to 10 MIPs and for very high rates (>200 MHz)
Not optimized for MIP time measurements
Thanks to
R. Sacchi, S. Giordanengo, V. Monaco, et al.
(INFN Torino)
www.tifpa.infn.it/projects/move-it/
MoVe-IT - Modeling and Verification for Ion beam Treatment
To measure the time precision of the thin LGAD, a reference sensor (CMS MTD) was installed on a KU board designed for precise timing with MIP.
The expected time precision of this setup is <30 ps

## Slide 14: Time reference system: “ultra-thin” LGAD
KU MoVe-IT board is designed with a lower gain (hence lower noise) to avoid saturation with ~10 MIPs charge deposit.
The output signal is quite smaller and faster wrt the board optimized for MIP detection
PRELIMINARY
Assuming that the MIP sensor/board has a negligible contribution (~30 ps):
The time precision measured for the thin sensor is ~90 ps.
Trigger generated using an ultra-thin silicon sensor that can provide also a time reference
Still work to do…

## Slide 15: Fully automated test of devices
All DUTs can be identified by a SN using a QR code
SN | Sensor Type | Sensor SN | Max Bias | Tested | …
ETLTEST1 | S10938-6130 | EXX33760-WNo42 | 250V | OK | 
… |  |  |  |  | 
The SN is linked to a database with all relevant information, then the module is tested and results are stored in the database

## Slide 16: Scanning Platform
Precise XY positioning of the spectrometer
25 x 25 cm2 available
Precision ~10 um
Accuracy ~100um over 20 cm
Easy encapsulation for light and dry air
FPGA for
“fast” processing
Raspberry PI 4 for “smart” processing
Arduino for “easy” processing
Motor control, shutter control, laser control, etc..
Trigger control, coincidences, counters, etc..
Camera acquisition, object recognition, data base, etc...

## Slide 17: Scanning Platform: automated object location
XY movement with automatic object recognition
Full video: https://youtu.be/R01_67eKrPA
RPi Camera
RPi Camera
(corrected) perspective
Microscope
(not used in this demo)
Laser Pointer

## Slide 18: Scanning Platform: a technical slide!
Motor control
Object recognition
Coordinate transform
Arduino Nano Every
The motors need two signals: DIR and STEP
(open loop)
Low jitter and fast: timers
Acceleration: very demanding
2 independent axis: even more demanding
Pi Camera or WebCam (bird-eye)
USB microscope (detail)
Acquired and processed using OpenCV framework
Camera: Perspective correction
Point the laser at 3 (or more) known positions and use those as reference point in the camera reference system
XY platform:
Rotation and scaling
Z might not be perfectly perpendicular
X and Y could be rotated
Compatible with our probe station…

## Slide 19: Conclusions
Within the upgrade program of the CMS MIP Timing Detector an automated test platform has been designed
The platform has 2 axis precise motion (XY) and fully custom control hardware/firmware
  The platform can be also modified to be used with particle beams (YZ movement)
The platform has cameras for object recognition and precise positioning
The platform is equipped with a Sr90 radioactive element and with a magnetic spectrometer to select electrons > 1MeV
A “thin” trigger/time reference system is under development: further research and tests are needed, but promising results.