## Slide 1: Xboxes Update
02/09/2020

## Slide 2: Summary
XBOX1: LLRF & Software Testing
XBOX2:
  33.6MW and stable.
  Measurable dark current signal.
XBOX3AB: T42 Structures
  Has been offline due to a modulator problem.
XBOX1: LLRF & Software Testing
XBOX2:
  Didn’t run during weekend (chiller alarm).
  Now at 35.5 peak input power and stable.
  If we run without interruptions we might reach 100MV/m this month.
  Difficulty with transmitted power measurement.
XBOX3AB: T42 Structures
  Restarted last Wednesday after being OFF for 10 days
  Bad restart – Line 1 dropped back to 12MW (previously at 22MW)
  Line 2 is fine, low BDR and flat running at 23MW
  This morning I found the K6 chiller has stopped running

## Slide 3: XBOX2
Chiller alarm on Friday evening, didn’t run during the weekend. Also had a software crash on Monday evening, so not much runtime.
Now at 35/31 MW (highest we have ever been!).
Parameters:
0.7us klystron pulse
50ns pulse
50Hz rep rate
Target Power: 40MW Peak in structure B
BDR Setpoint: 3E-5

## Slide 4: XBOX2 – Pulse Shape study.
Occasionally it is mentioned that the structures receive different pulse shapes.
Following last week I ran a quick study for different pulse lengths.
Shown are the pulses seen at Port 2 and Port 3.
As expected the dispersive effect more prominent at shorter pulse lengths.
Port 2
Port 3

## Slide 5: XBOX2 – Pulse Shape study.
Cause: Appears to be due to the difference between the S21 and S31 values of the power splitter. One filters high frequency components, the other filters lower frequency components.

## Slide 6: XBOX2 – Phase Shifter.
Phase Shifter has a negligible effect.

## Slide 7: XBOX2 – Pulse Shape study.
If we deliver all power to port 2 or all power to port 3, the pulses are the same.
Piston Inserted
Piston Retracted

## Slide 8: XBOX3 AB –Line 1 Structure Temp
Parameters:
1.3us klystron pulse
50ns pulse
50Hz rep rate
Current Power: 15.7MW

## Slide 9: XBOX3 AB –Line 1 Pulses
Parameters:
1.3us klystron pulse
50ns pulse
50Hz rep rate
Current Power: 15.7MW
Bad Restart 1
Bad Restart 2

## Slide 10: XBOX3 AB –Line 1 Time
Parameters:
1.3us klystron pulse
50ns pulse
50Hz rep rate
Current Power: 15.7MW

## Slide 11: XBOX3 AB –Line 1 BD Example
Parameters:
1.3us klystron pulse
50ns pulse
50Hz rep rate
Current Power: 15.7MW

## Slide 12: XBOX3 AB –Line 1 Full Reversed History
Parameters:
1.3us klystron pulse
50ns pulse
50Hz rep rate
Current Power: 23MW

## Slide 13: XBOX3 AB –Line 2 Time
Parameters:
1.3us klystron pulse
50ns pulse
50Hz rep rate
Current Power: 23MW

## Slide 14: XBOX3 AB –Line 2 Time
Parameters:
1.3us klystron pulse
50ns pulse
50Hz rep rate
Current Power: 23MW

## Slide 15: XBOX3 AB –Line 2 Time
Parameters:
1.3us klystron pulse
50ns pulse
50Hz rep rate
Current Power: 23MW

## Slide 16: XBOX3 AB –Line 2 Time
Parameters:
1.3us klystron pulse
50ns pulse
50Hz rep rate
Current Power: 23MW

## Slide 17: XBOX3 AB –Line 2 Full Reversed History
Parameters:
1.3us klystron pulse
50ns pulse
50Hz rep rate
Current Power: 15.7MW