## Slide 1: Gyroklystron Update
Electron gun design and simulation
8th Oct. 2020
L. J. R. Nix, L. Zhang, A. W .Cross

## Slide 2
Recap: 36GHz Gyroklystron Specifications
Beam voltage / Beam current | 150 kV / 50 A
Output power / 2nd harmonic power | 3.2 MW / 2.3%
Output power stability | 0.4% @0.5% variation of the modulator voltage
Output frequency / 3dB bandwidth | 36 GHz / 108 MHz (0.3%)
Magnetic field and frequency drift | 1.46 T and < 1 MHz frequency drift due to the drift of magnetic field
Frequency drift due to beam voltage | 24 MHz @0.5% / 4.8MHz @0.1% variation of the modulator voltage
Pulse repetition rate / Duration | 1000 Hz / 1.5 us
Drive power / Gain | 410 W / 39 dB
Input / output waveguide mode | Input TE10 (Rectangular) mode, output TE02 (Circular) mode
Efficiency | 43% (without energy recovery), 58.0% (with single stage depressed collector)
Average spent beam power | 6.5 kW (mm-waves on),11.3kW (mm-waves off)
Dimensions | 60 cm (W) * 60 cm (L) * 1200 cm (H)
Phase stability | 17.0 degree @ 0.5% variation in modulator voltage 3.4 degree @ 0.1% variation in modulator voltage 0.34 degree @ 0.01% variation in modulator voltage

## Slide 3: Practical considerations for the cathode
Small beam radius
High current
High Power
Lower operating mode
Large emission density
Large emitter thickness
Life time?
Larger alpha spread
Smaller output power
Magnetron injection gun (MIG) was achieved by global optimization to minimize the alpha spread at given design condition (journal paper [1] has been published).
A ~20 A/cm2 current density is still needed. The availability of high current density thermionic cathodes was investigated.
[1] L. Zhang, L. J.R. Nix, A. W. Cross, Magnetron Injection Gun for high-power gyroklystron, IEEE Transactions on Electron Devices, 2020, DOI:10.1109/TED.2020.3025747

## Slide 4: High Emission Density Cathodes
  Commercial solution exists and has been experimentally demonstrated in a MIG application
    MIG designed and tested with 30A/cm2 Spectra-Mat 612X cathode
      (L. R. Barnett, N. C. Luhmann, C. C. Chiu, and K. R. Chu, "Relativistic performance analysis of a high current density magnetron injection gun," Physics of Plasmas, vol. 16, no. 9, p. 093111, 2009/09/01 2009, doi: 10.1063/1.3227649.)
  some experimental solutions have been demonstrated:
    a scandia-doped Dispenser Cathode, life test >5000 hours at 40A/cm2
      (F. Yang, J. Wang, Y. Wang, W. Liu, and X. Zhu, "Investigation of Nanosized-Scandia-Doped Dispenser Cathodes With Machined Surfaces," IEEE Trans. Electron Devices, vol. 63, no. 4, pp. 1728-1733, 2016, doi: 10.1109/TED.2016.2528580.)

## Slide 5: High Emission Density Cathodes
Overview from Spectra-Mat website
The range and viability of other options is discussed in this paper:
  Kirkwood, D. M. et al. Frontiers in Thermionic Cathode Research. TED 65, 2061-2071, doi:10.1109/ted.2018.2804484 (2018)
The ease of manufacture, emission uniformity, and lifetime vary, but several potentially viable high-emission density cathodes have been demonstrated.
The 48GHz MIG uses a 20A/cm2 cathode and the 36GHz MIG uses a 22A/cm2 cathode, both of which are feasible based on available cathode technology and the pulsed operation of the gyroklystron