## Slide 1: C, X and K band accelerating modules
XLS injector layout, 02/10/2020
M. Diomede (INFN-LNF)
On behalf of CompactLight-XLS project

## Slide 2
2.5 CELL GEOMETRY ELECTROMAGNETIC SIMULATIONS AND FINAL PARAMETERS
Ecath | 160 MV/m
Δf/2- | ≈ 52 MHz
Q0 | 11600
 | 3
Filling time (F) | 160 ns
Pdiss @160MV/m | 9.7 MW
 | 51.4 [MV/m/(MW)0.5]
Rep. Rate | 1000 Hz
Peak Input power PIN | 17.5 MW
Pulsed heating (Tpuls) | <20 oC
RF pulse length (TRF) | 300 ns
Av diss power (Pav) | 2300 W
Ecath | 160 MV/m
Δf/2- | ≈ 52 MHz
Q0 | 11600
 | 3
Filling time (F) | 160 ns
Pdiss @160MV/m | 9.7 MW
 | 51.4 [MV/m/(MW)0.5]
Rep. Rate | 1000 Hz
Peak Input power PIN | 17.5 MW
Pulsed heating (Tpuls) | <20 oC
RF pulse length (TRF) | 300 ns
Av diss power (Pav) | 2300 W
Accelerating cells
RF ports
Pumping ports
Laser ports
solenoid
NB: in the present configuration 2 klystrons are needed to reach 160 MV/m on the cathode at 1 kHz.
With 1 klystron, simply scaling the performances of the present C-band sources (w/o R&D), we obtain 120 MV/m at 1 KHz
Optimum value to maximize the peak field on cathode
UPDATE: 1 high rep rate klystron is enough

## Slide 3
(@200 MV/m)
(@240 MV/m)
RF System | 
Operating frequency [GHz] | 5.996
Klystron pulse length [us] | 2
Klystron peak power [MW] | 15
Pulse rate [pps] | 1000
Q0 of BOC | 216000
Qe of BOC | 19100
Acc. Structure | 
Phase advance | 2pi/3
Cell length [mm] | 16.667
Number of cells | 120
Total length [m] | 2
Average iris radius [mm] | 6.6
Tapering angle [deg] | 0.02
Iris radius (first - last) [mm] | 6.943 – 6.257
Shunt imp. [MΩ/m] | 71 - 77
Q | 9986 - 9943
Group velocity/c [%] | 2.4 – 1.6
Filling time [ns] | 336
Repetition rate [Hz] | 1000
Avg. acc. gradient [MV/m] | 15
Kly. Power per module [MW] | 9
NEW C-Band module WITH BOC
MODULATOR HALL
LINAC HALL
15 MW, 2 µs,
1 kHz
BOC

## Slide 4
Module (linear t No. 2) |  |  | 
Frequency [GHz] | 11.994 |  | 
RF pulse (250 Hz) [µs] | 1.5 (0.15) |  | 
Average iris radius <a> [mm] | 3.5 |  | 
Iris radius a [mm] | 4.3-2.7 |  | 
Iris thickness t [mm] | 2.0-2.24 |  | 
Structure length Ls [m] | 0.9 |  | 
Unloaded SLED Q-factor Q0 | 180000 |  | 
External SLED Q-factor QE | 23300 |  | 
Shunt impedance R [MΩ/m] | 85-111 |  | 
Effective shunt Imp. Rs [M/m] | 349 |  | 
Group velocity v_g/c [%] | 4.7-0.9 |  | 
Filling time [ns] | 146 |  | 
Repetition rate [Hz] | 100 | 250 | 1000
SLED | ON | OFF | ON
Kly. Power per module [MW] | 44 | 44 | 9
Avg. acc. gradient [MV/m] | 65 | 30 | 30
X-Band Module
10 MW, 1.5 µs,
1 kHz
SLED
MODE CONVERTER
MODE CONVERTER
CIRCULAR WAVEGUIDE
MODULATOR HALL
LINAC HALL
CPI VKX-8311A
RF switch
50 MW, 1.5 µs,
100 Hz
X-Band (11.994 GHz)