## Slide 1: Accelerator Design
D. Schulte

## Slide 2: Tentative Roadmap
Exploratory Phase
Definition Phase
1
2
3
4
1
2
3
4
1
2
3
4
1
2
3
4
1
2
3
4
4
Explore design
Identify critical issues
Explore and prioritise issues
Make design choices
Define realistic goals
Define design
Address feasibility issues
Develop design, refine choices
Develop R&D programme to demonstrate performances

## Slide 3: Tentative Roadmap
Exploratory Phase
Definition Phase
1
2
3
4
1
2
3
4
1
2
3
4
1
2
3
4
1
2
3
4
4
Explore design
Identify critical issues
Explore and prioritise issues
Make design choices
Define realistic goals
Define design
Address feasibility issues
Develop design, refine choices
Develop R&D programme to demonstrate performances
Initial list ready
Prioritised list ready
Work
Work
Tentative list
Go through full collider to complete and update tentative list
Study the most critical issues from initial list to find solutions, further refine understanding, iterate

## Slide 4: Proton-driven Muon Collider Concept (MAP)
Short, intense proton bunches to produce hadronic showers
Pions decay into muons that can be captured
Muon are captured, bunched and then cooled
Acceleration to collision energy
Collision
No CDR exists, no fully integrated baseline
No cost estimate
Need to extend to higher energies (10+ TeV)
But did not find something that does not work
From the MAP collaboration: Proton-driven source (M. Palmer et al.)

## Slide 5: Tentative R&D List: RF
Superconducting high-energy accelerating cavities
  Maintain beam quality for short high-charge bunch
    longitudinal and transverse stability and emittance
  High efficiency for low current but high-charge, short bunch
Normal-conducting 6D cooling RF
  Gas-filled, high-gradient cavities
  High charge bunch, important losses
Front-end RF
  To capture muons
Other RF

## Slide 6: Tentative Target Parameters
Parameter | Unit | 3 TeV | 10 TeV | 14 TeV
L | 1034 cm-2s-1 | 1.8 | 20 | 40
N | 1012 | 2 | 2 | 2
fr | Hz | 6 | 4 | 4
Pbeam | MW | 5.8 | 12.8 | 17.9
C | km | 4.5 | 10 | 14
<B> | T | 7 | 10.5 | 10.5
εL | MeV m | 7.5 | 7.5 | 7.5
σE / E | % | 0.1 | 0.1 | 0.1
σz | mm | 5 | 1.5 | 1.07
β | mm | 5 | 1.5 | 1.07
ε | μm | 25 | 25 | 25
σx,y | μm | 3.0 | 0.9 | 0.63
Emittance is constant
Collider ring acceptance is constant
Bunch length decreases
Betafunction decreases
Scaled from MAP parameters

## Slide 7: Tentative Target Parameters
Parameter | Unit | 3 TeV | 10 TeV | 14 TeV
L | 1034 cm-2s-1 | 1.8 | 20 | 40
N | 1012 | 2 | 2 | 2
fr | Hz | 6 | 4 | 4
Pbeam | MW | 5.8 | 12.8 | 17.9
C | km | 4.5 | 10 | 14
<B> | T | 7 | 10.5 | 10.5
εL | MeV m | 7.5 | 7.5 | 7.5
σE / E | % | 0.1 | 0.1 | 0.1
σz | mm | 5 | 1.5 | 1.07
β | mm | 5 | 1.5 | 1.07
ε | μm | 25 | 25 | 25
σx,y | μm | 3.0 | 0.9 | 0.63
Beam power of CLIC is 28 MW @ 3 TeV
130 MW @ 14 TeV
Scaled from MAP parameters

## Slide 8: Cooling Design
MAP design almost achieves target performance on paper
Final stage needs to be improved
Hardware performances were better than assumed in design
Additional options proposed (parametric cooling)
Considering MAP design and MICE experience, develop overall concept
Design of cooling for demonstrator
Highest-field solenoids for final cooling (> 30 T)
High-field superconducting magnets for 6D cooling
50+ MV/m, normal conducting RF in magnetic field
Targets
Optics design
Safety, instrumentation, vacuum, …
Highly integrated, compact cells

## Slide 9: Cooling Concept
MAP collaboration
Superconducting solenoids
High-field normal conducting RF
Liquid hydrogen targets
Compact design

## Slide 10: Cooling: The Emittance Path
Y
Transverse Emittance (microns)
Longitudinal Emittance (mm)
Bunch
Merge
For acceleration to multi-TeV collider
Final
Cooling
post-merge 6D Cooling
For acceleration to NuMAX (325MHz injector acceptance 3mm,24mm)
Initial Cooling
Target
Phase
Rotator
Front End



pre-merge 6D Cooling (original design)
Exit Front End
(15mm,45mm)
Specification
For acceleration
to Higgs Factory
MAP collaboration

## Slide 11: Cooling: The Emittance Path
Y
Transverse Emittance (microns)
Longitudinal Emittance (mm)
Bunch
Merge
For acceleration
to Higgs Factory
For acceleration to multi-TeV collider
Final
Cooling
post-merge 6D Cooling
For acceleration to NuMAX (325MHz injector acceptance 3mm,24mm)
Initial Cooling
Target
Phase
Rotator
Front End



pre-merge 6D Cooling (original design)
Exit Front End
(15mm,45mm)
Initial
(X)
Initial
(Y)
VCC &
Hybrid
HCC
Final
Specification
Achieved (simulations)
MAP collaboration

## Slide 12: Cooling: The Emittance Path
Y
Transverse Emittance (microns)
Longitudinal Emittance (mm)
Bunch
Merge
For acceleration
to Higgs Factory
For acceleration to multi-TeV collider
Final
Cooling
post-merge 6D Cooling
For acceleration to NuMAX (325MHz injector acceptance 3mm,24mm)
Initial Cooling
Target
Phase
Rotator
Front End



pre-merge 6D Cooling (original design)
Exit Front End
(15mm,45mm)
Initial
(X)
Initial
(Y)
VCC &
Hybrid
HCC
Final
Specification
Achieved (simulations)
Several ideas to improve final cooling
Need to work out the solution
Highest field HTS helps
Phase space manipulations of beam
Higher gradient helps
Maybe can improve this
MAP collaboration

## Slide 13: Design Challenges and Status
MuCool: >50 MV/m in 5 T field
Very high gradients because muon lifetime is limited
Operation in a magnetic field (several T)
Strong beamloading
Different frequencies, from 200 MHz to 650 MHz
Final cooling reduces frequencies down to 20 Mhz or less
Induction linacs for lower frequencies
Solutions:
High pressure gas (H2) to suppress breakdowns
Allows 50 MV/m in 3 T
Design to minimise breakdown by minimising pulsed heating
Use of different materials
Be walls allow 50 MV/m in 3 T
Al might be good and is much safer
Goal:
10-5 breakdown probability
Highest possible gradient

## Slide 14: Proton Source and Front-end Design
Proton complex
Optics
Efficient RF
Magnets
Based on MAP design, optimise complex
Choice of target (solid/liquid, …)
Identify suitable existing proton installations for demonstrator
  Design required modifications
Design front end for demonstrator
Front-end
High power target
Capture solenoid (20 T, 1.2 m aperture)
Radiation from target
Buncher
Phase rotator
Optics

## Slide 15: Demonstrator
Demonstrator facility to produce useful muon beam
Demonstrator needs
to be based on muon collider source concept
a more detailed design than the collider source
to be based on technologies available in 5 years
to be affordable (0.5 GCHF?)
Hence we need to
Need to confirm choice of muon source concept
Have to have concept of full muon source
Identify use exiting infrastructure (e.g. proton beams)
Scale design to funding and available technology
Explore if it serve some physics
Develop source concept over the first two years
Then design demonstrator, preferably the same people

## Slide 16: Accelerator Design
  Two bunches accelerated simultaneously: one μ+ one μ-
Charge about 1.5-2 x 2 x 1012 muons
Five pulses per second
Need to compress m-long initial bunch maintaining it longitudinal emittance
In whole complex require average gradient > 1 MV/m to limit loss of muons
more at the beginning
Gradient in cavities O(20 MV/m), the higher the better
Initial linacs 0.2 to 1 GeV with 325 MHz and to 5 GeV with 650 MHz
Then recirculating linac
Finally accelerator ring

## Slide 17: Accelerator Design, cont.
Final bunch parameters (14 TeV):
charge 2 x 1012 muons, length 1 mm, energy spread 0.1%
Length maybe be different in the accelerator ring
Efficiency consideration
O(100) turns in ring, i.e. few ms beamloading
bunch spacing tens of microseconds
At 400 Mhz extract O(1%) of stored energy per passage
  higher frequencies proposed in MAP, is this reasonable?
Short bunch induces important higher order modes
  total loss factor effect up to 1 MV/m in four cell cavity
  approximately 6% energy difference between head and tail if not compensated
Need to mitigate single-bunch wakefield effect
Longitudinal beam profiles are important
In whole complex need to chose frequencies, mitigate beamloading, understand longitudinal dynamics
Assume pulsed superconducting system, but could one do differently?

## Slide 18: Collider Ring
Need to control longitudinal motion in collider ring
average lifetime is O(3000) turns
want short bunches O(1mm) @ 14 TeV
significant energy spread O(10-3)
large ring (14 km @ 14 TeV)
Need very small momentum compaction
Almost completely suppress motion for
i.e. 2.5 x 10-8 @ 14 TeV
5 x 10-6 @ 3 TeV
Or need enough RF voltage
e.g. 4 GV @ 14 TeV, α = 10-6, fRF = 1 GHz
e.g. 86 MV @ 3 TeV, α = 10-5, fRF = 1 GHz
Need to minimise momentum compaction
RF needs not yet known but could become important
Probably similar design to accelerator ring RF

## Slide 19: Accelerator and Collider Ring
Additional challenges
neutrino radiation
combined accelerator and collider ring
Neutrino radiation
option1: concentrate RF in straights in accelerator and buy land to which we point
Option 2: distribute many short (m-long) RF sections around the ring
  But how compact can this be, can we operate in magnetic field?
Combined rings
can we switch from acceleration to steady state rapidly enough?

## Slide 20: Conclusion
Plenty of exciting RF work
Normal and superconducting