## Slide 1: Gamma Factory: Proof of Principle Experiment SPSC-I-253
Yann Dutheil (CERN), Aurélien MARTENS (IJCLab Orsay),
Mieczyslaw Witold KRASNY (LPNHE Paris and CERN), on behalf of
The Gamma Factory study group
88 people from 34 institutes from 15 countries

## Slide 2: Outline
Gamma Factory
Scientific context
Why a Proof of principle experiment ?
The Proof of principle experiment

## Slide 3: Gamma Factory: The scientific context

## Slide 4: A striking fact
Weise, LINAC 2006 proceedings;
Few 100’s keV at most

## Slide 5: A striking fact
Weise, LINAC 2006 proceedings;
No bright photon source for nuclear and particle physics applications !
FEL and synchrotron impracticable
Inverse Compton scattering ?
Excellent monochromaticity but
O(1barn) cross-section is low !
10’s keV—100 MeV
ICS lie here
Example : HI𝛾S@Duke, 1010 ph/s, 1-100MeV

## Slide 6: Physics concept
💡: Exploit high cross-section of atomic resonances & existing CERN accelerator complex
E. J. Bessonov & K.J. Kim Phys. Rev. Lett. 76, 431, M.W. Krasny arXiv:1511.07794,
D Winters et al 2015 Phys. Scr. 2015 014048
Very similar with Inverse Compton scattering but O(109) larger cross-section !
PSI: Partially stripped ions
High-energy
Energy upshifting by a factor 4𝛾2
H-like Xenon at LHC (𝛾=3000)  180 MeV
Li-like Calcium at SPS (𝛾=130)  80 keV
For instance

## Slide 7: Physics concept
💡: Exploit high cross-section of atomic resonances & existing CERN accelerator complex
E. J. Bessonov & K.J. Kim Phys. Rev. Lett. 76, 431, M.W. Krasny arXiv:1511.07794,
D Winters et al 2015 Phys. Scr. 2015 014048
Very similar with Inverse Compton scattering but O(109) larger cross-section !
PSI: Partially stripped ions
High-energy
Energy upshifting by a factor 4𝛾2
H-like Xenon at LHC (𝛾=3000)  180 MeV
Li-like Calcium at SPS (𝛾=130)  80 keV
For instance
A technique already employed for spectroscopy
also with relativistic ion beams (𝛾⋍1) at FAIR (ESR, 2005)
but Never used as a photon source so far !!!

## Slide 8: Physics concept
💡: Exploit high cross-section of atomic resonances & existing CERN accelerator complex
Very similar with Inverse Compton scattering but O(109) larger cross-section !
PSI: Partially stripped ions
High-energy
👍🏻 PSI recycling in ring is very efficient (relative energy loss << beam energy spread)
👍🏻 Energy tunability provided by PSI species choice and ion beam energy (<400MeV w/ LHC)
👎🏻 Laser wavelength must be « tuned » to PSI species and beam energy
👎🏻 Laser must be placed in a harsher environment (compared to e- accelerators)
E. J. Bessonov & K.J. Kim Phys. Rev. Lett. 76, 431, M.W. Krasny arXiv:1511.07794,
D Winters et al 2015 Phys. Scr. 2015 014048

## Slide 9: Implications of Gamma Factory
High potential to open new opportunities in many branches of physics
M. W. Krasny et al. SPSC-I-253, M.W. Krasny arXiv:1511.07794

## Slide 10: Implications of Gamma Factory
High potential to open new opportunities in many branches of physics
M.W. Krasny et al., Progress in Particle and Nulcear Physics. 114 (2020) 103792,
D. Budker etal., Ann. Phys. (Berlin) 2020, 532, 2000204

## Slide 11: Implications of Gamma Factory
High potential to open new opportunities in many branches of physics
Currently being assessed for various « applications » of the concept

## Slide 12: Gamma Factory: Why a Proof of Principle experiment ?

## Slide 13: Two critical milestones
The ‘raison d’être’ of the Gamma Factory Proof of principle experiment
Demonstration at the SPS that there is no showstopper for the operation GF concept
Quantitative evaluation of the Gamma Factory potential for various branches of physics
On-going detailed case-by-case studies
Necessary inputs to a further implementation at LHC

## Slide 14: Atoms in the LHC !
1
Demonstration of efficient production, acceleration and storage of atomic beams in the CERN accelerator complex
Building up the physics cases for the LHC-based GF research programme and attracting wide scientific communities to use the GF tools in their respective research.
Elaboration of the Technical Design Report (TDR) for the (HL-)LHC-based GF research programme.
Extrapolation of the SPS PoP experiment results to the (HL-)LHC case and realistic assessment of the performance figures of the LHC-based GF programme.
6
5
4
Successful execution of the GF PoP experiment in the SPS.
Development of the requisite GF research programme simulation tools.
3
2
✓
2018 demonstration allowed us to estimate the Al-foil thickness optimized fo Pb79+

## Slide 15: Simulation tools: cross-checked
1
5
Extrapolation of the SPS PoP experiment results to the (HL-)LHC case and realistic assessment of the performance figures of the LHC-based GF programme.
6
Elaboration of the Technical Design Report (TDR) for the (HL-)LHC-based GF research programme.
4
2
3
Successful execution of the GF PoP experiment in the SPS.
Building up the physics cases for the LHC-based GF research programme and attracting wide scientific communities to use the GF tools in their respective research.
Demonstration of efficient production, acceleration and storage of atomic beams in the CERN accelerator complex
Development of the requisite GF research programme simulation tools.
✓
✓
Two existing softwares improved for GF use + dedicated ones provide consistent
Excitation rates
Angular distributions
Energy distributions
Polarisation (on-going)
M. W. Krasny et al. SPSC-I-253

## Slide 16: Where do we stand ?
1
5
Extrapolation of the SPS PoP experiment results to the (HL-)LHC case and realistic assessment of the performance figures of the LHC-based GF program.
6
Elaboration of the Technical Design Report (TDR) for the (HL-)LHC-based GF research program.
4
2
3
Successful execution of the GF PoP experiment in the SPS.
Building up the physics cases for the LHC-based GF research program and attracting wide scientific communities to use the GF tools in their respective research.
Demonstration of efficient production, acceleration and storage of atomic beams in the CERN accelerator complex
Development of the requisite GF research program simulation tools.
✓
✓
TODAY’s subject to approval
M. W. Krasny et al. SPSC-I-253, M.W. Krasny arXiv:1511.07794

## Slide 17: Gamma Factory: The PoP experiment Testing the concept with minimum cost and nuisance

## Slide 18: LOI submission and review
25/09/2019
LOI submission
23/01/2020
Questions received
18/02/2020
answer document issued
08/05/2020
Follow-up questions
28/05/2020
updated answer document issued
12/06/2020
invitation to SPSC meeting
Also presented @ 257th LHC Injector and Experimental Facilities Committee : https://indico.cern.ch/event/861645/
M. W. Krasny et al. SPSC-I-253, M.W. Krasny arXiv:1511.07794

## Slide 19: New ion stripper foils system
Common need with other experiments to add flexibility in stripping capability:
4 foils
Angle (thickness) can be tuned
Pulse to pulse operation !
35% stripping efficiency for Pb79+
Will allow parasitic Gamma Factory Proof of principle operation

## Slide 20: Beam parameters
As extrapolated from 2018 run meassurements and ordinary SPS operations with ions
75 ns
150 ns
75 ns
3 bunches/injection, 12 injections max.
100 ns
4 bunches/injection, 9 injections max.
100 ns
100 ns
150 ns
Lifetime is large enough at flat top for Pb80+
 Extrapolated for Pb79+: about 100s
Common harmonic frequency=40MHz
M. W. Krasny et al. SPSC-I-253, M.W. Krasny arXiv:1511.07794

## Slide 21: Collision scheme
Beams must be aligned, synchronized
Not specific to Gamma Factory scheme
M. W. Krasny et al. SPSC-I-253

## Slide 22: Spectrum matching
Linewidth of atomic resonance << bandwidth of laser spectrum (in ref. frame of atoms)
energy
Probability density
At resonance:
detuning

## Slide 23: Spectrum matching
Atomic (PSI) beam energy spread ⋍ bandwidth of laser spectrum (in ref. frame of atoms)
energy
Probability density
At resonance:
detuning
Excitation rate of atoms depend on their position in the energy spectrum
A relatively high laser energy is required to excite nearly all atoms
Ultimately: 1017 ph/s

## Slide 24: Ion beam cooling
Ion beam efficiently cooled
Observe it with wall current monitors
Large (horizontal) dispersion relation at the interaction point:
 transverse cooling in a similar fashion by mis-aligning the beams
No detuning
Detuned laser spectrum
M. W. Krasny et al. SPSC-I-253

## Slide 25: Laser system at the state of the art
State of the art system, already operated in low emittance KEK ATF ring
But: need to ensure the system can be operated fully remotely
Fabry-Perot resonator to reach about 5mJ at 40MHz 200kW already exists
Built and operated by IJCLab (Orsay) team
L. Amoudry et al., Applied Optics 59 (2020) 116; Chaikovska et al., Scientific Reports 6 (2016) 36569

## Slide 26: Synchronisation & alignment
Beam with constant revolution frequency at flat-top
Cavity tuning range is limited
Varying transverse beam alignment: use existing orbit correctors
Not specific to Gamma Factory
Already realized in the past (for instance KEK ATF exp.)
Alignment provided by BPMs on the girder of optical cavity
Only needs to be adapted to SPS specifics
Similar to AWAKE
Inputs from relevant experts at CERN : H. Damerau (RF) and V. Fedosseev (Laser)
H. Damerau et al. IPAC2016-THPMY039; Chaikovska et al., Scientific Reports 6 (2016) 36569

## Slide 27: Optical system: laser and amplifier
Required quality factor of optical cavity
very low phase noise laser
Pouysegur et al. Opt. Lett. 40, 5184-5187 (2015);
Industrial system exist !
Laser pulse duration/spectrum tunable
Unique provider !
Required laser power and robust performances

## Slide 28: Radiation hardness
Ageing of laser system’s components is not expected to be limitation if TID<150krad
Sensitive laser-system must be shielded (side TI18 tunnel)
Gamma Factory PoP laser will only operate a few weeks a year
With R2E team: FLUKA simulations to be done to decide on the need of extra shielding or not
G. Buchs et al., Opt. Express 23 (2015) 9890 ; S. Girard et al., Opt. Express 20 (2012) 8457

## Slide 29: Optical system: integration
SPS half-cell 621 with side tunnel TI18
M. W. Krasny et al. SPSC-I-253

## Slide 30: Optical system: integration
SPS half-cell 621 with side tunnel TI18
Thanks to Liam Dougherty for the help

## Slide 31: Detection system
Laser-ion interaction Point
Ion beam direction
Central opening for ion beam passage
‘BTV’ system: YAG:Ce + camera
Remotely controlled manipulator
M. W. Krasny et al. SPSC-I-253

## Slide 32: Impact on regular SPS operations
Vacuum
Impedance
Parasitic operations
Optical cavity requires similar or better vacuum compared to SPS
Valves to break vacuum on a limited section of SPS  CERN experts
Past experience on low emittance KEK ATF
Remote operations
Require formal validation of final design by CERN experts
Will be addressed during cavity and laser system implementation in lab
Laser beam has no sizeable effect on proton/fully stripped hadronic beam
M. W. Krasny et al. SPSC-I-253

## Slide 33: Project planning
2021
2022
2023
Operational after 2023-2024 YETS
6 months of operation of optical cavity in lab
Installation of laser beam transport line in 2022-2023 YETS
optical cavity assembly in fall 2022
Laser room in TI18 during 2021-2022 YETS
M. W. Krasny et al. SPSC-I-253

## Slide 34: PoP milestones and beam requests
Resonance finding
Optimisation and characterisation
Atomic physics precision measurement
Realize synchronization, alignment 4x8h in SPS supercycle // NA ops
Optimize interaction rate 8h dedicated beamtime
Cooling demonstration
Stable measured rate of photons over >5s 8h in SPS supercycle // NA ops
Show increase of beam current at constant charge 2x8h dedicated beamtime
First measurement of Pb79+ transition energy 8h in SPS supercycle // NA
Confront theory (strong field QED,…) to experiment 8h dedicated beamtime
Commissioning with PSI before yearly ion run 8h dedicated beamtime
Measure transverse beam size reduction 8h in SPS supercycle // NA
In 2024
M. W. Krasny et al. SPSC-I-253

## Slide 35: Summary
An international proto-collaboration of people
with very broad physics interests in the Gamma Factory concept;
that would like to demonstrate before LS3 generation of unprecedented rates of photons
and ion beam cooling with laser,
in order to trigger a new avenue for atomic measurements
and new opportunities for particle and nuclear physics

## Slide 36: Summary
An international proto-collaboration of people
with very broad physics interests in the Gamma Factory concept;
that would like to demonstrate before LS3 generation of unprecedented rates of photons
and ion beam cooling with laser,
in order to trigger a new avenue for atomic measurements
and new opportunities for particle and nuclear physics
The Proof of principle experiment for the Gamma Factory is a critical step
to allow this very broad physics programme to happen

## Slide 37: BACKUP

## Slide 38: Project funding
Already covered

## Slide 39: X-ray detector
‘BTV’ system: YAG:Ce + camera
Remotely controlled manipulator to go to garage position for non GF operations
Post LS3 upgrade ability to mesaure energy-position correlations, timepix ?
>1011 visible photons/second
 above sensitivity of standard camera

## Slide 40: Optical system: laser and amplifier
Lock of laser to optical cavity of finesse 25k and length 7.5m
very low phase noise laser
Up to now: we know only one provider that delivered compliant performances
Risk mitigation:
reduce cavity selectivity i.e. finesse and gain (change coupling mirror, not expensive)
Use laser amplifier with higher average power to keep intracavity pulse energy high
Pouysegur et al. Opt. Lett. 40, 5184-5187 (2015)
Industrial system exist !
Bottomline: such an industrial system, with spectrum/pulse duration tunability should be very robust compared to any home made solution
Laser pulse duration/spectrum tunability is an asset

## Slide 41: Why a Proof of Principle experiment ?
1
5
Demonstrate ion beam cooling: longitudinal and then transverse
6
Perform atomic physics measurement
4
2
3
Demonstrate stable and repeatable operation
Confront data to simulations
Demonstrate that an adequate laser system (5mJ@40MHz) can be (remotely) operated in the high radiation field of SPS and LHC.
Demonstrate that very high rates of photons are produced : almost all PSI’s excited for every bunch crossing

## Slide 43: Optical system optimization
Fraction of excited ions
Fraction of excited ions
A muti-dimensional approach to optimize the laser beam parameters
Optimum parameters depend on ion-bunch length
𝜎X
Laser pulse duration/spectrum tunability is an asset

## Slide 44: Optical system: design
A several mJ pulsed laser at 40 MHz is a natural candidate:
  Compatible with the atoms filling schemes
  Compatible with what one would naturally expect for LHC operations
  State of the art technology: pulsed laser (freq. comb) + amplifier + resonant cavity
A 10m mirror Radius of curvature is preferred
A 2-mirror (plano-concave) cavity is considered:
 simpler operation, delivers naturally beam sizes close to optimum
We expect to operate the optical cavity with an enhancement factor >5000
>4.5mJ pulses @ 40MHz, 180kW in cavity

## Slide 45: Laser phase noise
T=2p/wr
Dfce
The whole comb must be locked:
dilatation (frep)
translation (fCEP)
T. Udem et al. Nature 416 (2002) 233
Phase noise of the laser must be low to lock to a high finesse cavity
Noise limits coupling