## Slide 1: Measurement of the fission cross-section of 240Pu and 242Pu at CERN’s n_TOF facility
CERN-INTC-2010-042, INTC-P-280
Spokespersons: M. Calviani (CERN), E. Berthoumieux (CEA)
TC: V. Vlachoudis (CERN)
n_TOF Collaboration

## Slide 2: Outline
Motivations
Detector description
Samples characteristics
240Pu, 242Pu count-rate evaluation
Beam time request

## Slide 3: The issue of nuclear waste
Main problem of nuclear energy production are the transuranic actinides: Pu and MA (Np, Am, Cm…)
1.5% in mass but give the biggest contribution to radiotoxicity and heat after 100 y
Problem persists for more than 105 y
Some isotopes are fissionable (proliferation and criticality concerns)
Present generation reactors have a low burn-up efficiency and produce large amount of radioactive waste
Generation-IV reactors are aimed to recycle large amount of spent fuel (actinides)
Dedicated Burners (ADS…)
In all cases a large reduction of actinides inventory is achieved by means of neutron-induced fission reactions

## Slide 4: Motivations for fission measurements
 |  | Energy Range | Current Accuracy (%) | Target Accuracy (%)
U238 | Inel | 0.5 ÷ 6.1 MeV | 10 ÷ 20 | 2 ÷ 3
 | Capt | 2.04 ÷ 24.8 keV | 3 ÷ 9 | 1.5 ÷ 2
Pu241 | Fiss | 454 eV ÷ 1.35 MeV | 8 ÷ 20 | 2 ÷ 5
Pu239 | Capt | 2.04 ÷ 498 keV | 7 ÷ 15 | 4 ÷ 7
Pu240 | Fiss | 0.498 ÷ 1.35 MeV | 6 | 2 ÷ 4
Pu242 | Fiss | 0.498 ÷ 2.23 MeV | 19 ÷ 21 | 4 ÷ 7
Pu238 | Fiss | 0.183 ÷ 1.35 MeV | 17 | 3 ÷ 5
Am242m | Fiss | 67.4 keV ÷ 1.35 MeV | 17 | 3 ÷ 4
Am241 | Fiss | 2.23 ÷ 6.07 MeV | 9 | 2
Am243 | Fiss | 0.498 ÷ 6.07 MeV | 12 | 3
Cm244 | Fiss | 0.498 ÷ 1.35 MeV | 50 | 5
Cm245 | Fiss | 67.4 ÷ 183 keV | 47 | 7
Aliberti, Palmiotti, Salvatores – Validation of simulation codes for future systems, NEMEA-4 Workshop, October 2007
OECD/NEA WPEC Subgroup 26, (2008)
Uncertainty reduction requirements for Gen-IV fast reactors
Objective is to meet integral parameters target accuracies
The development of advanced nuclear systems requires data on minor actinides  Pu isotopes
n_TOF is a key facility

## Slide 5: Motivations – 240Pu(n,f)
Energy range | Initial Unc. (%) | Target Unc. (%)
2.23 – 6.07 MeV | 5 | 3
1.35 – 2.23 MeV | 6 | 2-3
0.498 – 1.35 MeV | 6 | 2-4
0.454 – 2.03 keV | 22 | 9-13
NEA Nuclear Data High Priority list (May 2010)
OECD/NEA WPEC Subgroup 26, (2008)
Uncertainty request above fission threshold is challenging but feasible
Data in the keV region:
Important for fast reactors
Discrepancy up to 20-30%
100 keV – 50 MeV
8 keV – 20 keV
http://www.nndc.bnl.gov
~8%
~10%

## Slide 6: Motivations – 242Pu(n,f)
Energy range | Initial Unc. (%) | Target Unc. (%)
6.07 – 19.6 MeV | 37 | 15
2.23 – 6.07 MeV | 15 | 5-8
1.35 – 2.23 MeV | 21 | 4-7
0.498 – 1.35 MeV | 19 | 4-10
183 – 498 keV | 19 | 9
NEA Nuclear Data High Priority list (May 2010)
OECD/NEA WPEC Subgroup 26, (2008)
~15%
Disagreement up to 15% at the threshold
Step in ENDF/B-VII.0 and strong disagreement between measurements
100 keV – 10 MeV
1 keV – 1 MeV
http://www.nndc.bnl.gov
~25%

## Slide 7: Detectors
We propose to perform 240,242Pu(n,f) measurements:
Large area MicroMegas detector
10 cm active diameter
Presently working in the n_TOF EAR:
  10B(n,a) and 235U(n,f)
Foreseen 10 samples in the beam for simultaneous measurement of the fission cross-section
Advantages:
Transparent detector (very low background)
Not very much sensitive to g-flash  high energy
T. Papaevangelou et al., MPGD2009 Proceedings (2009)
S. Andriamonje et al., ND2010 Proceedings (2010)
M. Calviani et al., Phys. Rev. C 80, 044604 (2009) (FIC)
M. Calviani et al., NIM A594, 220-227 (2008) (FIC)

## Slide 8: Detector performances - MicroMegas
10 cm diameter MicroMegas with 10B and 235U samples in ISOLDE Work Sector Type A
neutrons
10 cm diameter MicroMegas in n_TOF EAR-WSTA
Fission yield from 235U sample in MicroMegas
a background
fission fragments
Pulse height distribution from 235U(n,f)

## Slide 9: Samples and radioprotection limits
240Pu sample |  | 242Pu sample | 
 |  | 238Pu | 0.004%
239Pu | 0.019% | 239Pu | 0.005%
240Pu | 99.879% | 240Pu | 0.019%
241Pu | 0.001% | 241Pu | 0.023%
 |  | 242Pu | 99.949%
Samples to be provided by IRMM, Belgium
A high purity material batch is already available at the Institute and a request has been submitted
Measurement at CERN now feasible, thanks to the new classification of the experimental area as
“Work Sector Type A”
See E. Chiaveri, “Report from n_TOF”
240Pu: 15 mg (four samples of 25 MBq each)
242Pu: 25 mg (four samples of 7 MBq each)
Respects the “1 mSv criterion” established at CERN for radioactive isotopes
Chosen mass according to CR, a-activity and detection efficiency
Samples deposited on Ø=6 cm (flat beam)

## Slide 10: Countrates 240Pu (1/2)
240Pu
239Pu
241Pu
request
15 mg 240Pu, 133 mg/cm2
< 100 eV, most of the contaminant contribution is due to 239Pu(n,f): subtraction possible, with relatively small uncertainties
Fission rate per proton bunch
> 300 eV the measurements is mostly unaffected by the presence of contaminants in the sample  measurement ok!

## Slide 11: Countrates 240Pu (2/2)
With 20 bins/neutron energy decade (statistical uncertainty):
  Above 1 keV: <3%/bin
  Above threshold: <1%/bin
3%
1%
Expected systematic uncertainties: ~3-4%
Fission counts and statistical uncertainties using 8x1018 protons

## Slide 12: Countrates 242Pu (1/2)
< 100 eV, the contribution of the contaminants on the fission yield is > 2 orders of magnitude higher than that of 242Pu(n,f)
> 1 keV the contribution of the fission yield due to the contaminants is < 1%  measurement ok!
25 mg 242Pu, 220 mg/cm2
Fission rate per proton bunch
242Pu
241Pu
239Pu
Contaminant is predominant at low energies
request

## Slide 13: Countrates 242Pu (2/2)
With 20 bins/neutron energy decade (statistical uncertainty):
  1-100 keV: ~5%/bin
  >100 keV: <3%/bin
  above threshold: <1%/bin
3%
5%
1%
Data adequate for Gen-IV reactors
Expected systematic uncertainties: 4-5%
Fission counts and statistical uncertainties using 8x1018 protons

## Slide 14: Beam time request
Isotope | Mass (mg) | Stat. Uncertainties (%) | # protons
240Pu | 15 | ≤ 2 (500 eV – 10 MeV) | 8x1018
242Pu | 25 | ≤ 3 (100 keV – 10 MeV) | 
235U | 5 | < 1 | n. d.
238U | 5 | < 1 | n. d.
Beam request sufficient to reach the goal of the measurement in the URR and threshold region and to study selected resonances at lower energie
Measurements relative to:
  235U(n,f) cross-section is a standard from 150 keV to 200 MeV
  238U(n,f) cross-section is a standard from 2 to 200 MeV
http://www-nds.iaea.org/standards/

## Slide 15: Conclusions
Sensitivity studies for Generation-IV critical reactors, show that a drastic reduction of uncertainties on fission cross-section is needed for high mass plutonium isotopes
Present proposal aims at collecting data on 240Pu(n,f) and 242Pu(n,f)
Goal: reach an accuracy of around
  3-5% in the URR up to around 50 MeV for 240Pu
  6-7% for 242Pu
Requested protons: 8x1018

## Slide 16
Thanks a lot for your attention

## Slide 17
Isotope | t1/2 (y) | Inh. Coefficient (Sv/Bq) | Authorization limit (LA) (Bq) | Public protection (“1 mSv criterion”) | 
235U | 7.04x108 | 2.56x10-13 | 800 | 3.9x109 Bq | 4.9x107 mg
238U | 4.47x109 | 2.38x10-13 | 900 | 4.2x109 Bq | 3.4x108 mg
240Pu | 6.56x103 | 4.10x10-12 | 200 | 2.44x108 Bq | 28.9 mg
242Pu | 3.74x105 | 3.93x10-12 | 200 | 2.54x108 Bq | 1750 mg
0.6 – 1 keV