## Slide 1: MKPL impedance measurements with and without serigraphy
M. Barnes, O. Bjorkqvist, C. Zannini
Ack.: P. Blaise, L. Ducimetiere, Y. Sillanoli

## Slide 2: MKP configuration
MKP-S
MKP-L
Beam
#1
#2
#3
#4

## Slide 3: Beam induced power loss
Beam induced heating
Present MKPs could strongly suffer of beam induced heating with high intensity beam
MKP-I: Impedance considerations, C. Zannini et al., LIU-SPS 50 ns Injection System for Pb Ions Review, 4 October 2013 (slides).

## Slide 4: 2018 thermal behavior of MKPL,MKPS and MKE
Reached high temperatures even without dedicated scrubbing, just from nominal operation and high intensity studies on Thursdays

## Slide 5
Operational Scenarios for SPS
Confident: Below Tc (Curie Temp.)
Could exceed Tc: risk of mis-kicking beam
Risk of mechanical damage
Very low risk of damage
Not OK (> Tc)
Basic table courtesy Hannes Bartosik, Giovanni Rumolo & Carlo Zannini
M. Barnes

## Slide 6: MKP impedance reduction
  Concept with longitudinal serigraphy exists (4, 5 and 6 stripes)
Q20 | PL per LHC fill cycle
MKP-L | 874 W
MKP-S | 234 W
MKP-L ser. (6 stripes) | 28 W
MKP-L ser. (4 stripes) | 99 W
M. Beck
CERN-THESI015-374
Impact on beam stability has been studied and estimated to be negligible
C. Zannini, I. Karpov, Impact of new MKP-L serigraphy, summary from BD analysis. Presented at the LIU-SPS coordination meeting, March 2020.

## Slide 7: MKP impedance measurements
Port1
Port2
Matching resistor
Alumina plate
Silver serigraphy

## Slide 8: MKP impedance measurements
Good agreement between simulation models and measurements
Frequency shift of the peak due to serigraphy
probably due to the effect of wire and terminations

## Slide 9: Summary
The MKPL was predicted to suffer of beam induced heating with LIU beam already in 2013
  2018 temperature data confirm the criticality of the kicker
The MKPL is expected to limit operation and scrubbing during run III
Impedance mitigation solution is available and validated with impedance measurements
  Ongoing: simulation of the measurement setup (C. Antuono)

## Slide 10: Thank you very much for your attention