## Slide 1: Afterburner FEL performance
For 250 eV and 600 eV
Hector Mauricio Castaneda Cortes
SCU (Helical)
APPLE
Kicker

## Slide 2
FEL performance of afterburner
Hector Mauricio Castaneda Cortes
Daresbury Laboratory
09/11/2020

## Slide 3
Parameter | Value | Notes
Beam Energy | 1.45 GeV | (maximum value found by Neil, 1kHz repetition rate)
Sliced Energy Spread | 0.02% | 
Sliced emittance | 0.2 mm-mrad | 
Photon Energy | 250 eV | 
aw0 | 2.42 | 
Noise realisations | 20 | 
Undulator period | 13 mm | (recommended by Neil)
Peak Current | 5 kA | Neil’s peak current (5.5 kA)
Bunch length | 4.85 µm | Cuarge = 75 pC
Simulation parameters (650 eV)

## Slide 4
Parameter | Value | Minimum (Deliverable 2.2) | Notes
Beam Energy | 2.36 GeV | 2.36 GeV | (maximum value found by Neil, 1kHz repetition rate)
Sliced Energy Spread | 0.04% | 0.04% | 
Sliced emittance | 0.2 mm-mrad | 0.2 mm-mrad | 
Photon Energy | 600 eV | 0.5 – 1 keV | 
Undulator type | SCU Nb3Sn | Nb-Ti | Neil did his analysis initially with Nb3Sn
aw0 | 2.3893 | 0.62-1.32 | 
Noise realisations | 20 |  | 
Gap | Approx. 4.3 mm | 4.3 mm | (found by Neil)
Undulator period | 13 mm | 13 mm | (recommended by Neil)
Peak Current | 700 A | 650 A | Neil’s peak current (5.5 kA)
Bunch length | 32.12 µm | Total Charge 75 pC | 
Simulation parameters (II)

## Slide 5: SXR: Polarisation control via Afterburner (250 eV)
SCU (Helical)
APPLE
SCU (Helical)
APPLE
Decoupling
chicane
Kicker
 | Only SCU (max B- helical) | Only APPLE (max B - planar) | SCU+AB (best- planar, max B)
Pulse energy (µJ) | 572.5 | 408.4 | 248 (43%, 60%)
B | 2.5×1031 | 7.4×1030 | 1.32×1031 (52%, 1.78 times larger)
Length (m) | 4.03 | 6.59 | 5.628
To recover 64% pulse energy of SCU at maximum B (91% of APPLE at max. B) , the AB needs to have 1 section ( 372 µJ, 6.27×1030) |  |  | 
Best scenario: SCU with 1 section and AB with 1.5 sections

## Slide 6: SXR: Polarisation control via Afterburner (650 eV)
SCU (Helical)
APPLE
SCU (Helical)
APPLE
Decoupling
chicane
Kicker
 | Only SCU (max B- helical) | Only APPLE (max B - planar) | SCU+AB (best- planar, max B)
Pulse energy (µJ) | 191 | 73 | 91.478 (47%, 80%)
B | 3.6×1030 | 5.7×1029 | 1.86×1030 (50%, 3.7 times larger)
Length (m) | 9.9 | 20.59 | 16
A SCU with 3 sections will provide a larger pulse energy than the APPLE at highest B (even with an AB with one section, pulse energy = 102 uJ) |  |  | 
APPLE highest peak brilliance around 20.59 m. Pulse Energy at highest brilliance: 73 µJ.
Best scenario: SCU with 3 sections and 2 sections (total length around 16 m). Pulse energy of 91 µJ (1.28 times the pulse energy of the APPLE at highest peak brilliance)

## Slide 7
Summary

## Slide 8
Summary (250 eV, 5kA)
Best scenario: SCU with two segments and 1.5 sections (43% the highest brightness of the SCU ). For larger SCUs, the electrons enter into the afterburner after saturation, so they are overbunched.
Pulse energy of the APPLE undulator at maximum peak brilliance recovered for an afterburner with more than 2 segments (around 92% the pulse energy of SCU at highest brightness
Maximum peak brilliance within the afterburner (SCU with one segment) around 6.2 ×1031 for afterburners with 2.5 segments
Best scenario shorter than length of maximum B for the APPLE planar undulator (14% shorter)

## Slide 9
Summary (650 eV, 700A)
Best scenario: SCU with 3 segments. For larger SCUs, the electrons enter into the Afterburner after saturation, so they are overbunched.
Pulse energy of the APPLE undulator at maximum peak brilliance recovered for an afterburner with more than 2 segments. For a SCU with one segment and one afterburner segment, the pulse energy obtained at the end of such afterburner is around 25% of the pulse energy of the APPLE undulator at peak brilliance
The SCU with 3 sections will have a pulse energy larger than the pulse energy at highest brightness for the APPLE at z = 20 m and around 1.5 times the brightness of the SCU at highest B
Best scenario shorter than length of maximum B for the APPLE planar undulator (20% shorter)

## Slide 11
Extra-slides
Results of after-burner (250 eV and 650 eV)

## Slide 12: SXR: Polarisation control via Afterburner (250 eV)
SCU (Helical)
APPLE
SCU (Helical)
APPLE
Decoupling
chicane
Kicker
Pulse energy (µJ) | AB (1 sect) | AB (2 sect) | AB (3 sect) | AB (4 sect) | AB (5 sect)
SCU(1 sect) | 84 | 372 | 313 | 340 | 297
SCU(2 sect) | 4 | 6 | 10.65 | 15 | 18
SCU(3 sect) | 1.19 | 1.47 | 1.75 | 1.90 | 2.03
SCU max B length = 4.03 m and max B energy = 572 µJ |  |  |  |  | 
APPLE max B length = 6.59 m and max B energy = 408 µJ |  |  |  |  | 
Best scenario: SCU with 1 section and AB with 2 sections Pulse energy of 372 µJ

## Slide 13: SXR: Polarisation control via Afterburner (250 eV)
SCU (Helical)
APPLE
SCU (Helical)
APPLE
Decoupling
chicane
Kicker
B(×1029) | AB (1 sect) | AB (2 sect) | AB (3 sect) | AB (4 sect) | AB (5 sect)
SCU(1 sect) | 13.173 | 62.2 | 9.14 | 1.26 | 3.48
SCU(2 sect) | 0.14 | 0.12 | 0.0793 | 0.0793 | 0.13
SCU(3 sect) | 0.027 | 0.006 | 0.004 | 0.003 | 0.002
SCU max B length = 4.03 m and B = 2.25×1031 |  |  |  |  | 
APPLE max B length = 6.59 m and B = 7.4×1030 |  |  |  |  | 
Best scenario: SCU with 1 sections and AB with 2 section. Peak Brilliance of 6.2×1030

## Slide 14: SXR: Polarisation control via Afterburner (650 eV)
SCU (Helical)
APPLE
SCU (Helical)
APPLE
Decoupling
chicane
Kicker
Pulse energy (µJ) | AB (1 sect) | AB (2 sect) | AB (3 sect) | AB (4 sect) | AB (5 sect)
SCU(2 sect) | 1.6 | 19 | 59.88 | 74 | 87
SCU(3 sect) | 102 | 130 | 149 | 160 | 167
SCU(4 sect) | 59 | 71 | 79 | 85 | 89
SCU max B length = 9.02 m and max B energy = 191 µJ |  |  |  |  | 
APPLE max B length = 20.35 m and max B energy = 73 µJ |  |  |  |  | 
APPLE highest peak brilliance around 20 m. Pulse Energy at highest brilliance: 73 µJ.
Best scenario: SCU with 3 sections and 2 sections (total length around 16 m). Pulse energy of 102 µJ

## Slide 15: SXR: Polarisation control via Afterburner (650 eV)
SCU (Helical)
APPLE
SCU (Helical)
APPLE
Decoupling
chicane
Kicker
B(×1029) | AB (1 sect) | AB (2 sect) | AB (3 sect) | AB (4 sect) | AB (5 sect)
SCU(2 sect) | 0.08 | 0.348 | 1.02 | 0.535 | 0.48
SCU(3 sect) | 5.8 | 2 | 0.93 | 0.65 | 0.48
SCU(4 sect) | 2.29 | 0.5 | 0.3 | 0.15 | 0.14
SCU max B length = 9.02 m and max B = 3.6×1030 |  |  |  |  | 
APPLE max B length = 20.35 m and max B = 5.6×1029 |  |  |  |  | 
APPLE Highest peak brilliance at 20 m. Highest peak brilliance 5.6×1029
Best scenario: SCU with 3 sections and 2 sections (total length around 16 m). Peak Brilliance of 2×1029 (21% of peak brilliance of the APPLE)

## Slide 16
Afterburner performance
(250 eV, 5 kA)

## Slide 17
Only for the 1st scenario (SCU with one segment), the maximum pulse energy is achieved within the afterburner.
Maximum pulse energy around 400 µJ for afterburners with 2.75 segments
Pulse energies

## Slide 18
Only for the 1st scenario (SCU with one segment), the peak brilliance is achieved within the afterburner.
Maximum peak brilliance around 1.5 ×1031 for afterburners with 2.5 segments
Peak brilliance

## Slide 19: Comparison with pulse energy of APPLE at maximum brightness
For the optimum scenario, the pulse energy of the APPLE at maximum peak brilliance is recovered for an afterburner with 2 segments

## Slide 20: Comparison with pulse energy of SCU at maximum brightness

## Slide 21
Afterburner performance
(600 eV, 700 A)

## Slide 22: Pulse energy and maximum peak power over all slices
Pulse Energy (highest brightness):
SCU (around 9.9 m) 191 µJ
APPLE (around 20 m)  73 µJ
Best scenario SCU with 3 sections (2 sections AB have around the pulse Energy of the SCU at highest B)

## Slide 23: Brightness and Bandwidth
z (highest brightness):
SCU (around 9.9 m) 3.6×1030
APPLE (around 20 m)  5.6×1029
Best scenario SCU with 3 sections. Smaller B afterwards

## Slide 24: Comparison with pulse energy at highest brightness (SCU, left and APPLE, right)
The SCU with 2 sections can recover the pulse energy of the SCU at highest B at the end of an AB with 2.5 segments.
The SCU with 3 sections will have a pulse energy larger than the pulse energy at highest brightness for the APPLE at z = 16 m and around 1.5 times the brightness of the SCU at highest B

## Slide 25: Comparison with Brightness at highest brightness (SCU, left and APPLE, right)
Brightness for best scenario around 20% of the highest brightness for the SCU.