## Slide 2: L4 Status
13 Nov 2020

## Slide 3: General news/schedule
As from FOM
Quite some investigation on RF phases drift
Next 2 weeks only beam to main dump, bo beam to LBE
After: 1 week last setups  connection to PSB Dec 7th
TS stop (with access possible) : 4-6 January

## Slide 4: BI MDs
ToF tests (next Tuesday): CCDTL1 @ nominal, downstream cavities at minimum power (as during phasing)  scan phase of low power cavities  monitor any change in ToF
SIS (to be scheduled) to shorten pulse while grids/scanners IN
  Systematic studies to check it works  no long pulsed go through wires

## Slide 5: Outstanding issues

## Slide 6: L4T.BWS.0243 H
Distorted signal when L4T trajectory == nominal
Signal OK when displace beam ( not nominal trajectory but toward nominal 0 of scanner…)
Obstacle upstream? Loose wire moving with fork?

## Slide 7: L4T-L4Z-LBE grids
Again hint of overheated wires
L4T.0223 H
L4T.0243 H
LBE 0025 V
… some others being checked, including inter-tanks

## Slide 8: Plan
Access possible sometimes in the next two weeks (no beam to SWY, only possible to L4 dump)
  Spares: 2 scanner, xx grids available
  See with OP and VSC opportunity to open vacuum at least in tank L4T.0243
Would profit to:
  Try swapping 1 laser EM fiber with spare
  Check L4T-L4Z bias voltage status (two ggrids make the HV power supply trip)
  Change BSM1 EM (Jocelyn for January, same VSC sector as L4T grids)