## Slide 1
Cherenkov and Transition Radiation Detectors
Christian Joram
CERN
Acknowledgement: I make use of a lot of material provided by
Peter Krizan, JSI, Ljubljana (Cherenkov)
Christoph Rembser, CERN (Transition Radiation)
Thanks!

## Slide 2
Outline
Cherenkov radiation
Short introduction to photodetectors
Cherenkov detectors
Transition radiation
Transition radiation detectors

## Slide 3
Cherenkov Radiation
A charged particle, moving through a medium at a speed which is larger than the speed of light in the medium, produces Cherenkov light.
Classical analogue: fast boat on water
q

## Slide 4
… back to Cherenkov radiation
Cherenkov
threshold
‘saturated’ angle (b=1)
d
d·tanq
The dielectric medium is polarized by the passing particle.
A coherent wave front forms if
(n = refr. index)
“the radiator”
qC
vwave = c/n
vparticle = bc
radiator of
limited thickness
Cherenkov
cone

## Slide 5
Number of emitted photons per unit length and unit wavelength/energy interval
dN/dl
l
dN/dE
E
0
UV cut-off
Cherenkov effect is a weak light source.
There are only a few tens or hundreds of photons produced per cm.
UV cut-off

## Slide 6: Cherenkov detectors
Energy loss by Cherenkov radiation small compared to ionization (0.1%)
Cherenkov effect is a very weak light source
 need highly sensitive photodetectors
Number of detected photo electrons
DE = E2 - E1 is the width of the sensitive range of the photodetector (photomultiplier, photosensitive gas detector...)
N0 is also called figure of merit ( ~ performance of the photodetector)
Example: for a detector with
and a Cherenkov angle of
one expects photo electrons

## Slide 7
Photodetection
(Detection of light in the optical and UV domain)

## Slide 8
Purpose:
Convert light into detectable electronic signal
(we are not covering photographic emulsions!)
Principle:
Use photoelectric effect to ‘convert’ photons (g) to photoelectrons (pe)
Details depend on the type of the photosensitive material (see below).
Photon detection involves often materials like K, Na, Rb, Cs (alkali metals) . They have the smallest electronegativity  highest tendency to release electrons.
Basics of photon detection

## Slide 9
(Photonis)
Eg
h
e-
semiconductor  vacuum
Basics of photodetection
Nγ
photodet
Npe
P [W]
I [A]
photodet
Many solid photosensitive materials are semiconductors …
but photoeffect can also be observed from gases and liquids.
Internal photoeffect
External photoeffect
EA = electron
affinity
Internal photoeffect: Eg > Eg
External photoeffect: Eg > Eg + EA

## Slide 10
Requirements on photodetectors
High sensitivity, usually expressed as: quantum efficiency
or radiant sensitivity S (mA/W), with
QE can be >100% (for high energetic photons) !
Good Linearity: Output signal  light intensity, over a large dynamic range (critical e.g. in calorimetry (energy measurement).
Fast Time response: Signal is produced instantaneously (within ns), low jitter (<ns), no afterpulses
Low intrinsic noise. A noise-free detector doesn’t exist. Thermally created photoelectrons represent the lower limit for the noise rate  AoT2exp(-eWph /kT). In many detector types, noise is dominated by other sources.
+ many more (size, fill factor, radiation hardness, cost, tolerance/immunity to B-fields…)
Basics of photon detection

## Slide 11
Frequently used photosensitive materials / photocathodes
100 250 400 550 700 850 l [nm]
12.3 4.9 3.1 2.24 1.76 1.45 E [eV]
Visible
Ultra Violet (UV)
Multialkali
NaKCsSb
Bialkali
K2CsSb
GaAs
TEA
TMAE,
CsI
Infra Red (IR)
Remember :
E[eV]  1239/l[nm]
NaF, MgF2, LiF, CaF2
Si
(1100 nm)
normal
window glass
borosilicate glass
quartz
Cut-off limits of window materials
begin of arrow indicates threshold
Almost all photosensitive materials are very reactive (alkali metals). Operation only in vacuum or extremely clean gas.
Exception: Silicon, CsI.

## Slide 12
Basic principle:
Photo-emission from photo-cathode
Secondary emission from N dynodes:
dynode gain g  3-50 (function of incoming electron energy E);
total gain M:
Example:
10 dynodes with g = 4
M = 410  106
Very sensitive to magnetic
fields, even to earth magnetic
field (30-60 mT = 0.3-0.6 Gauss).
 Shielding required (mu-metal).
Photo-multiplier tubes (PMT’s)
http://micro.magnet.fsu.edu/
pe
(http://micro.magnet.fsu.edu)
(Hamamatsu)

## Slide 13: Latest generation of high performance photocathodes
0
10
20
30
40
50
200
300
400
500
600
700
Wavelength [nm]
Quantum Efficiency [%]
QE Comparison of semitransparent bialkali QE
Example Data for
UBA : R7600-200
SBA : R7600-100
STD : R7600
UBA:43%
SBA:35%
STD:26%
x1.3
x1.6
Ultra Bialkali available only for small metal channel dynode tubes
Super Bialkali available for a couple of standard tubes up to 5”.

## Slide 14
Multi-anode PMT (Hamamatsu)
Up to 8  8 channels (2  2 mm2 each);
Size: 28  28 mm2;
Bialkali PC: QE  25 - 45% @ lmax = 400 nm;
Gain  3 105;
Gain uniformity typ. 1 : 2.5;
Cross-talk typ. 2%
Flat-panel (Hamamatsu H8500):
8 x 8 channels (5.8 x 5.8 mm2 each)
Excellent surface coverage (89%)
Multi-anode and flat-panel PMT’s
50 mm
(Hamamatsu)
(Hamamatsu)
Cherenkov rings from
3 GeV/c p– through aerogel
(T. Matsumoto et al., NIMA 521 (2004) 367)

## Slide 15: Micro Channel Plate (MCP) based PMTs
Window/Faceplate
Photocathode
Dual MCP
Anode
Gain ~ 106
Photoelectron
DV ~ 200V
DV ~ 200V
DV~ 2000V
photon
MCP-OUT Pulse
Typical secondary yield is 2
For 40:1 L:D there are typically 10 strikes (210 ~ 103 gain per single plate)
Pore sizes range from <10 to 25 mm.
Small distances  small TTS and good immunity to B-field
Anode & Pins
Dual MCP
Ceramic Insulators
Gain stage and detection are decoupled  lots of potential and freedom for MA-PMTs: Anode can be easily segmented in application specific way.
Available with up to 1024 (32 x 32) channels (1.6 x 1.6 mm2)
50 mm
MCPs are usually based on glass disks, with lots of aligned pores.
The surface of the pores are metal coated.

## Slide 16
Hybrid Photon Detectors (HPD’s)
Basic principle:
Combination of vacuum photon detectors and solid-state technology;
Optical window, (semitransparent) photo-cathode;
Electron optics (optional: demagnification)
Charge Gain: achieved in one step by energy dissipation of keV pe’s in solid-state detector anode;
Energy loss eVth in (thin) ohmic contact
WSi = 3.6 eV
e-h
DV = 20 kV
 M ~ 5000
F = Fano factor
FSi ~ 0.1
1 p.e.
pulse height (ADC counts)
2 p.e.
3 p.e.
4 p.e.
5 p.e.
pulse height signals of
1 Si pad
HVHPD = 26 kV
Pedestal cut
 low gain fluctuations;

## Slide 17
Cross-focused electron optics
pixel array sensor bump-bonded to binary electronic chip, developed at CERN
8192 pixels of 50 × 400 mm.
specially developed high T° bump-bonding;
Flip-chip assembly, tube encapsulation (multi-alkali PC) performed in industry (VTT, Photonis/DEP)
Pixel-HPD’s for LHCb RICH detectors
50mm
Pixel-HPD anode
72mm  active
During commissioning: illumination of 144 tubes by beamer. In total : 484 tubes.
T. Gys, NIM A 567 (2006) 176-179

## Slide 18
(Si) – Photodiodes (PIN diode)
P(I)N type
p layer very thin (<1 mm), as visible light is rapidly absorbed by silicon
High QE (80% @ l  700nm)
Gain = 1
Avalanche photodiode (APD)
High reverse bias voltage: typ. few 100 V
Special doping profile  high internal field (>105 V/cm)  e and h avalanche multiplication
Avalanche must stop due to statistical fluctuations.
Gain: typ. O(100)
Rel. high gain fluctuations (excess noise from the avalanche). CMS ECAL APD: ENF = 2 @G=50.
Very high sensitivity on temp. and bias voltage DG = 3.1%/V and -2.4 %/K
Solid-state photon detectors
h e
p+ i(n) n+
g
Hamamatsu S8148.
(140.000 pieces used in CMS barrel ECAL).

## Slide 19
Solid-state … Geiger mode Avalanche Photodiode (G-APD)
How to obtain higher gain (= single photon detection) without suffering from excessive noise ?
Operate APD cell in Geiger mode (= full discharge),
however with (passive) quenching.
Photon conversion + avalanche short-circuits the diode.
J. Haba, RICH2007
J. Haba, RICH2007
J. Haba, RICH2007

## Slide 20
GM-APD
Quench
resistor
1mm
100 – several 1000 pix / mm2
Bias bus
Multi pixel G-APD, called G-APD, MPPC, SiPM, …
Musienko @PD07
Quasi-analog detector allows photon counting with a clearly quantized signal
20 x 20 pix
-Vbias


GM-APD
g
g
Q
Q
2Q
Quench
resistor
1 g
2 g
3 g
Sizes up to 6×6 mm2 now standard.
Only part of surface is photosensitive!

## Slide 21
SiPM designs (just examples)
Hamamatsu HPK (http://jp.hamamatsu.com/)
25x25µm2, 50x50µm2, 100x100µm2 pixel size
1x1mm2
3x3mm2
Arrays
1x4mm2
1x4 channels
6x6 mm2
2x2 channels
FBK-IRST
50x50µm2 pixel size
1x1mm2
2x2mm2
3x3mm2
4x4mm2
4x4mm2
2x2 channels
3x3 cm2
8x8 channels
SensL (http://sensl.com/)
20x20µm2, 35x35µm2, 50x50µm2, 100x100µm2 pixel size
3.16x3.16mm2
4x4 channels
3.16x3.16mm2
4x4 channels
6 x 6 cm2
16x16 channels

## Slide 22: Gaseous Photodetectors
e.g. CH4 + TEA
Thin CsI coating
on cathode pads
Principle:
Ionize photosensitive molecules, admixed to the counter gas: TMAE (labs = O(cm), TEA (labs = O(mm).
release photoelectron from a solid photocathode (CsI, bialkali...). labs = 0.
In both cases free photoelectrons create Townsend avalanches  Gain
The dream: Bialkali works in visible domain, however requires VERY clean gases.
Long term operation in a real detector not yet demonstrated.
Challenges: How to achieve high gain (105) ? How to control ion feedback and light emission from avalanche? How to purify gas and keep it clean? How to control aging ?
e.g. CH4 + TMAE
long drift
TPC-like
Cut-off of quartz windows
Quantum efficiency
 few cm 
 few mm 
 few mm 
TEA, TMAE, CsI work only in deep UV region.

## Slide 23: Gaseous photodetectors: A few implementations...
CsI on readout pads
photocathode
HV
Proven technology:
Cherenkov detectors in ALICE, HADES, COMPASS,
J-LAB…. Many m2 of CsI photocathodes
Micro Pattern Structures
(GEM) + CsI
HBD (RICH) of PHENIX.
R&D:
Thick GEM structures
Visible PC (bialkali)
Sealed gaseous devices
CsI on multi-GEM structure
Sealed gaseous photodetector with bialkali PC. (Weizmann Inst., Israel)
CsI

## Slide 24: Cherenkov detectors
Cherenkov detectors can exploit ...
Nph(b)  Threshold detector. Do not measure qC
q(b)  Ring Imaging Cherenkov detectors “RICH”
 Detection of Internally reflected Cherenkov light “DIRC”.
Knowing both the speed b = v/c and the momentum p of the particle allows to derive the mass of the particle and hence identify it (e.g. p, K, p, d,…).
Particle ID.
Prompt emission of Cherenkov light (different from scintillation) plus angular information  very fast timing detectors. TOP, TORCH
1
2
3
Measure qC

## Slide 25: Cherenkov detectors
Threshold Cherenkov detectors
Principle of a simple in-beam threshold Cherenkov counter
Beam
p and k
mirror
radiator medium
PM
Often used in secondary beamlines (e.g. CERN PS, SPS) to tagg particle type
Dipole magnets select momentum,
e.g. 2 GeV/c
p threshold
k threshold
b(p)
b(k)
n = 1.03
radiator with
n = 1.03, bthr = 0.97
momentum (GeV/c)

## Slide 26: Cherenkov detectors
BELLE threshold aerogel counters
p/K separation up to 3.5 GeV/c
Almost 1200 independent detector modules in total.
6 different aerogels.

## Slide 27
.
.
.
.
.
.
.
.
.
.
.
RICH detectors determine qC by intersecting the Cherenkov cone
with a photosensitive plane
 requires large area photosensitive detectors, e.g.
wire chambers with photosensitive detector gas
PMT arrays
(J. Seguinot, T. Ypsilantis,
NIM 142 (1977) 377)
Detect Np.e. photons (photoelectrons) 
minimize
 maximize Np.e.
n = 1.28
C6F14 liquid
n = 1.0018
C5F12 gas
p/K
p/K/p
K/p
p/h
p/K/p
K/p
DELPHI
Ring Imaging Cherenkov detectors (RICH)


## Slide 28
Determination of qC requires:
space point of the detected photon (x,y,z)
  photodetector granularity (sx, sy), depth of interaction (sz)
emission point (xe,ye,ze)
  keep radiator thin
  or use focusing mirror
particle direction qp, fp
  RICH requires
  good tracker
radiator
window
window
detector
Ring Imaging Cherenkov detectors (RICH)
Reconstruction and resolution of Cherenkov angle
(xe,ye,ze)
the chromatic error - an ‘irreducible’ error
nrad = n(E)
qC
sE is related to the sensitivity range of the photodetector DE
DE   Npe  good sE  bad DE   Npe  bad sE  good
qC

## Slide 29
DELPHI and SLD:
A RICH with two radiators and a common photodetector plane
covers a large momentum range.
p/K/p separation 0.7 - 45 GeV/c:
Two particles from a hadronic jet (Z-decay) in the DELPHI gas and liquid radiator.
Circles show hypotheses for p and K
(W. Adam et al. NIM A 371 (1996) 240)
C6F14 (1 cm, liquid)
C5F12 (40 cm, gas)
C4F10 (50 cm, gas)
spherical mirror
TPC-like Photodetector
TMAE-based
‘slow’
Ring Imaging Cherenkov detectors (RICH)
Generation 1

## Slide 31
The RICH detectors are sandwiched between tracking detectors which provide precise particle track extrapolation

## Slide 32
The DELPHI RICHes were complex and delicate, and required 24/24h care, 365 days a year. It took years to make them work and perform.
Working in the VUV posed strict requirements on purity of all liquids and gases.
The windows were made of quartz. The whole detector was kept at 1030 mbar, 40°C the whole year.
Materials were attacked by CxFy fluids. Leaks between radiator systems, shorts in the TPC drift field and many more things had to be taken care of.
But it finally worked!
p
K
p
p
K
p

## Slide 33
M. Artuso et al.
https://doi.org/10.1016/j.nima.2005.07.056
CLEO RICH @ CESR, Cornell
ALICE RICH @ LHC
QE (%)
Generation 1.5
Fast RICH detectors

## Slide 34: ALICE RICH = HMPID
The largest scale (11 m2) application of CsI photo-cathodes in HEP!
CsI photo-cathode is segmented in 0.8x0.84 cm pads
Six photo-cathodes per module

## Slide 35: The LHCb RICH counters
250 mrad
10 mrad
Vertex
reconstruction:
VELO
Trigger:
Muon Chambers
Calorimeters
Tracker
PID:
RICHes
Calorimeters
Muon Chambers
Kinematics:
Magnet
Tracker
Calorimeters
Generation 2

## Slide 36
radiator CF4
qC 1.8°
n 1.0005
pthresh (p) 4.4 GeV/c
Np.e. 23
sq 0.6 mrad
p (3s) 98.5 GeV/c
RICH 1
RICH 2
radiator C4F10 aerogel
qC 3.03° 13.8°
n 1.0014 1.03
pthresh (p) 2.6 0.6 GeV/c
Np.e. 31 6.8
sq 1.29 2.19 mrad
p (3s) 56 13.5 GeV/c
2 RICH detectors in LHCb
aerogel
radiator
spherical mirror
flat mirror
photodetectors (HPD)
L(C4F10) ~ 85 cm

## Slide 37
RICH 2
photodetector plane
beam test in 2004 with 6 HPDs
2 RICH detectors in LHCb

## Slide 38
2 RICH detectors in LHCb
Beam test results with C4F10 radiator gas (autumn 2004).
Single pion (10 GeV/c)
Superimposed events (100 k pions, 10 GeV/c)

## Slide 39: Performance of LHCb RICHes
RICH 1
RICH 2
Single event

## Slide 40: LHCb Upgrade (under way, LS2)
New photon detectors: MaPMTs Hamamatsu R13743 (H12700) and R13742 (R11265)
New electronics working at 40 MHz readout rate
New optics layout for RICH 1 (no aerogel)
2.9 mm
6 mm
8x8
8x8
RICH2
RO plane
RICH 1

## Slide 41: Future LHCb Upgrade (LS4!!)
Provide PID at p-p luminosity of 1034 in the forward region
Aim to use SiPM (cryo-cooled?) photodetectors
Need ultralight mirrors (in active region)
Incremental improvements in:
  Improve Cherenkov angle resolution
    More photons in the green  lower chromatic error
  Reduced event complexity with timing
  Enhanced number of photons
Generation 3?
New optics
New optics

## Slide 42: SiPM as photosensor for a RICH counter ?
Improve the signal to noise ratio:
Reduce the noise by a narrow (<10ns) time window (Cherenkov light is prompt!)
Increase the number of signal hits per single sensor by using light collectors
Reduce the noise even further by cooling the SiPMs
E.g. light collector with reflective walls or plastic light guide
SiPM
PCB

## Slide 43: Photon detector with SiPMs and light guides
SiPMs: array of 8x8 SMD mount Hamamatsu S10362-11-100P with 0.3mm protective layer
64 SiPMs
20mm
Korpar et al., NIM A594 (2008) 13; NIM A613 (2010) 195
module was moved to 9 positions to cover the ring area. Save $$$ !

## Slide 44: DIRC @BaBar: Detection of Internally Reflected Cherenkov light
During propagation: angle of Cherenkov light is conserved, except of left/right and up/down ambiguities
Use the internally reflected C-light, which would normally be lost!

## Slide 45: DIRC @ BaBar
BaBar spectrometer at PEP-II
e-
e+
Quartz Barbox
Standoff box
Compensating coil
Support tube (Al)
Assembly flange
Only radiator is in active volume of detector. Photodetectors & electronics do not disturb!

## Slide 46: DIRC performance
Lots of photons!
Excellent p/K separation
NIM A553 (2005) 317

## Slide 47: Belle II Cherenkov detectors
Aerogel radiator
Hamamatsu HAPD + readout
Barrel PID: Time of Propagation Counter (TOP)
Aerogel radiator
Hamamatsu HAPD
+ new ASIC
Cherenkov photon
200mm
n~1.05
Endcap PID: Aerogel RICH (ARICH)
200
Quartz radiator
Focusing mirror
Small expansion block
Hamamatsu MCP-PMT (measure t, x and y)
mirror

## Slide 48
Time of propagation (TOP) counter
quartz radiator
Photon detector
Similar to the DIRC, Cherenkov ring imaging with precise time measurement.
Reconstruct Cherenkov angle from two photon hit coordinates and the time of propagation of the photon
Photon detector (MCP-PMT)‏, pixels of ~5 x 5 mm2, very fast multi-GHz sampling electronics
    Excellent time resolution ~ 40 ps
    Single photon sensitivity at 1.5 T

## Slide 49
Pattern in the coordinate-time space (‘ring’) of a pion and kaon hitting a quartz bar
Time distribution of signals recorded by one of the PMT channels (slice in x): different for p and K (~shifted in time)
TOP ‘image’ reconstruction
Patterns for p and K
The name of the game: analytic expressions for the 2D likelihood functions M. Starič et al., NIMA A595 (2008) 252-255
simulation
simulation

## Slide 50: TOP first events
The early BELLE II data demonstrates that the TOP principle is working

## Slide 51: TORCH
A special type of Time-of-Propagation counter, part of a future LHCb upgrade.
Aim for p,k,p separation, 2-10 GeV/c.
At 10 GeV/c: Dt of p-k = 35 ps
Can be achieved with 30 photons and 70 ps resolution for single photons.
CERN-LHCC-2017-003
TORCH area 5 x 6 m2
18 module system
11 MCPs per module
Just radiator in active volume

## Slide 52: TORCH principle
Cylindrical mirrored surface maps the photon angle qz to a y’ position
Cyl. mirror
qx
qz
Particle impact point known  qx can be derived from measurement of coordinate x on segmented MCP photodetector.
 x
C-angle known
Photon arrival time can be corrected for time of propagation
Precise TOF information
Photek, custom development (64 x 64 pixels)

## Slide 53
Expected performance (simulation)
Test-beam campaigns (2017 & 2018):
Single-photon time resolutions around 80 – 100 ps have been achieved
Photon yields are measured to be within∼10% and∼30% of simulation, respectively
https://doi.org/10.1016/j.nima.2020.163671
TORCH test beam results

## Slide 54: Particle ID by Transition radiation
only high energetic e± emit TR of detectable intensity.
 particle ID
medium
vacuum
TR is electromagnetic radiation, emitted when a charged particle traverses a medium with a discontinuous refractive index, e.g. the boundaries between vacuum and a dielectric layer.
A (too) simple picture
Radiated energy per medium/vacuum boundary
(there is an excellent review article by B. Dolgoshein (NIM A 326 (1993) 434))
Transition Radiation was predicted by Ginzburg and Franck in 1946
(G. Garibian, Sov. Phys. JETP63 (1958) 1079)
A correct relativistic treatment shows that…
electron
Lorentz boost

## Slide 55: Particle ID by Transition radiation
Number of emitted photons / boundary is small
   Need many transitions  build a stack of many thin foils with gas gaps
Emission spectrum of TR = f(material, g)
Typical energy:
 photons in the keV range
Simulated emission spectrum
of a CH2 foil stack
X-rays are emitted with a sharp
maximum at small angles
 TR stay close to track
Particle must traverse a minimum distance, the so-called formation zone Zf, in order to efficiently emit TR.
Zf depends on the material (wp), TR frequency (w) and on g.
Zf (air) ~ mm, Zf (CH2) ~ 20 mm  important consequences for design of TR radiator.

## Slide 56: Particle ID by Transition radiation
R D R D R D R D
alternating arrangement of radiators stacks and detectors  minimizes reabsorption
TR Radiators:
stacks of thin foils made out of CH2 (polyethylene), C5H4O2 (Mylar)
hydrocarbon foam and fiber materials
Low Z material preferred to keep re-absorption small (Z5)
Detector should be sensitive for 3  Eg  30 keV.
Mainly used: Gas detectors: MWPC,
        drift chamber, straw tubes…
Detector gas: sphoto effect  Z5
 gas with high Z required, e.g. Xenon (Z=54)
TR X-ray detectors:
Intrinsic problem: detector “sees”
TR and dE/dx
Pulse height
(1 cm Xe)
Q
TR (10 keV)
500 e-
Discrimination
by threshold
Very Schematic!
dE/dx
200 e-

## Slide 57: Particle ID by Transition radiation
The ATLAS Transition Radiation Tracker (TRT)
~300’000 straw tubes (d = 4mm)
Every straw is a mini drift tube. Measure drift time of electrons to anode wire
680 cm
anode wire
Active gas is Xe/CO2/O2 (70/27/3) operated at ~2x104 gas gain;
drift time ~ 40ns ( fast!)

## Slide 58
with radiator in front
without radiator in front
sensor (straw tube)
radiator (foam or fibres)
wire thickness = 30µm
straw diameter = 4mm
traversing particle
Spectrum of the energy deposit in a straw tube
data test beam 20GeV electrons
Signal in straw is superposition of dE/dx and TR
Basic principle

## Slide 59
radiator (foam or fibres)
Special challenges at the LHC
Very high occupancy: up to 30% of straws receive a signal in a bunch crossing;
Very high counting rate: up to 20 MHz/straw
Short bunch crossing interval: 25 ns
High spatial resolution needed ⇒ many measurement points (35/track);
Radiation environment: ~10 MRad and 1014 n/cm2 year;
Fast and chemically passive straw gas: otherwise ageing!
Chemically resistant straw materials: operating straw acts like an electrochemical reactor
Minimum amount of material ( in radiation lengths)
Extremely precise and robust mechanical structure of ~100µm/few m =~10-5;
Temperature stable: cooling required.

## Slide 60: The sensor - a straw
  layers of a straw wall
  straws in an end-cap wheel
Cathode foil
Anode
wire
New for ATLAS: stiff straw, supported by carbon fibre strips, allows self supporting structures, thus reduced material inside the detector; Length: 144 cm in barrel, 39 cm in end-cap.

## Slide 61
Optimal TR threshold (~6.5 keV)
Fibers (TRT barrel)
Regular foils (TRT end-caps)
Foam (TRT barrel)
easy to build structures!
What was new about these foams?
No impurities from other material, always present in other type of foams
Polypropylene foam
Polypropylene fibres
Polypropylene foils
Carbon foam
~probability to produce detectable TR photon
Choice of Radiator materials: ensure balance between TR-performance and simple construction.
The radiator

## Slide 62
empty barrel module
test with radioactive source
inserting the radiator
module shell half filled with radiator material
inserting the straws
connecting the straw walls
stringing straw wires
mounting electronics & cooling
connecting the wires
TRT barrel module production

## Slide 63
Barrel support structure
Filled barrel support structure
inserting modules
TRT Barrel detector (with semi conductor detector inserted)
insertion into ATLAS
From modules to a complete barrel detector

## Slide 64
assembly of a basic element, a wheel with 4 straw layers/planes
Fixating and connecting wires
(tests wire tension & HV)
Installation of straws
(tests leak tightness)
Transfer of wheel…
…to string wires
Final acceptance tests
(test wire centricity etc.)
Sealing of wheel
(tests leak tightness & HV)
TRT end-cap wheel production

## Slide 65
A TRT event display

## Slide 66
“bad” materials
“good” materials
Check ratio of height of signal amplitude for test straw (radiated) and monitor straw (not radiated)
Mandatory in high radiation environments: test of all materials
Example: tests for radiation hardness of TRT wires

## Slide 67
Original TRT gas mixture (70% Xe, 20% CF4, 10% CO2) was destroying the detector (2002)
glass wire joints of barrel TRT “melting” with radiation 0.3-04 C/cm, less than 1 year nominal LHC operation
Reason: hydrofluoric acid HF
Within one year, a new mixture was developed: 70% Xe, 27% CO2, 3% O2
O2 very unusual, strong quencher (“eats” electrons)
only works for TRT as straws have small diameter (we are very lucky! … for once)
ATLAS TRT: bad surprise during assembly (2)

## Slide 68
TRT pipes
cracks
ATLAS TRT: bad surprise during operation
Cracks in outlet pipes of active gas developed in 2012
gas losses: 150l/day instead of <0.5l/day up to 2011;
reason: aggressive ozone produced when active gas mixture is radiated, ozone attacks plastic gas pipes (although plastic material has been validated - but material seem to have changed properties when being heated and bent....)
no chance to fix leaks
Difficult to access!!!
For effected region, switched to Argon based gas mixture in the straws.
Reduce PID performance.

## Slide 69
low occupancy (number of collisions per bunch crossing <𝝻> low)
high occupancy (number of collisions per bunch crossing <𝝻> high, i.e. Heavy Ion Collisions)
Argon
Xenon
increasing occupancy
TRT Performance - Tracking
in 2016: already suffering from broken gas pipes
⇒ detector partially operated with Argon mixture

## Slide 70
TR turn ON curve: HL probability VS gamma factor
TRT Performance - Particle Identification
10 GeV m vs 10 GeV e
Typical Figure of Merit for a TR detector:
Event with an electron (yellow track):
hits with high signal (=TR, passing a high level HL threshold) are indicated in red

## Slide 71
ALICE TRD
7.36 m
7.34 m
Time Expansion Chamber with Xe/CO2 gas (85%-15%)
TRD
TPC
CERN-EP-2017-222
fibre/foam sandwich

## Slide 72
ALICE TRD performance
integ. charge method
charge + tD method
Pulse height vs drift time
TMQ = Truncated mean of charge
L-Q = Likelihood on charge
L-QX = 2D Likelihood on charge and x-coord.

## Slide 73: 11 take home messages
Cherenkov radiation is produced by a charged particle traversing a dielectric medium at a speed v ≥ c/n (threshold).
Weak light source, visible and UV.
Light intensity increases like sin2q = 1 - (n2b2)-1  saturated angle at b ≈ 1
Detection of C-light requires low-noise single photon sensitive photodetectors.
Main applications are PID (p/k) by threshold, Ring Imaging or Time Of Propagation counters (incl. TORCH).
Transition radiation is produced by a charged particle at the edge of a dielectric medium.
Intensity scales with Lorentz boost g. In HEP experiments, only e± reach high enough g values (> 1000)
Extremely weak light source, X-ray, O(10keV)
Need many transitions  foil stacks, foams
Detection by gas detector (drift chamber / tubes) operated with high-Z gas (Xe)
Main application is tracking with e ± enhancement.

## Slide 74
BACK-UP
MATERIAL

## Slide 75: Propagating waves
A stationary boat bobbing up and down on a lake, producing waves

## Slide 76
Now the boat starts to move, but slower than the waves
No coherent wavefront is formed

## Slide 77
Next the boat moves faster than the waves
A coherent wavefront is formed

## Slide 78
Finally the boat moves even faster
The angle of the coherent wavefront changes with the speed
cos q = vwave / vboat
q

## Slide 79
Detection of charged particles
Particles can only be detected if they deposit energy in matter.
How do they lose energy in matter ?
Discrete collisions with the atomic electrons of the absorber material.
Reminder: Interaction of charged particles
e
-
W.W.M. Allison, J.H. Cobb,
Ann. Rev. Nucl. Part. Sci. 1980. 30: 253-98
If are in the right range  ionization.

## Slide 80
Instead of ionizing an atom or exciting the matter, under certain conditions the photon can also escape from the medium.
 Emission of Cherenkov and Transition radiation.
This emission of real photons contributes also to the energy loss.
Optical behaviour of medium is characterized by the complex dielectric constant e
Refractive index
Absorption parameter
Interaction of charged particles
eV O(10) eV keV

## Slide 81
… more interactions of charged particles
schematically !
A photon in a medium has to follow the dispersion relation
Emission of photons if
e
-
q
Assuming soft collisions + energy and momentum conservation  emission of real photons:
A particle emits real photons in a dielectric medium if its speed v = b×c
is greater than the speed of light in the medium c/n.  Cherenkov radiation.
… solve for w

## Slide 82
Estimate the energy loss by Cherenkov radiation in quartz
lmin = 160 nm  Emax ≈ 1234 / l ≈ 7.7 eV
lmax ≈ 3 mm = 3000 nm  Emin ≈ 0
nquartz ≈ 1.46
 sin2q = 1 - cos2q = 1 - 1/n2= 0.53
DE = 7.7 eV
<Eg> = DE/2 = 3.85 eV
Cherenkov effect is a weak but very useful light source.
Private exercise

## Slide 83
The classical domains of application
Calorimetry
  Readout of organic and inorganic scintillators, lead glass, scint. or quartz fibres  Blue/VIS, usually 10s – 10000s of photons
Particle Identification
  Detection of Cherenkov light UV/blue, single photons
  Time Of Flight  Usually readout of organic scintillators (not competitive at high momenta) or Cherenkov radiators
Tracking
  Readout of scintillating fibres  blue/VIS, few photons
Photodetection in HEP

## Slide 84
Mainly determined by the fluctuations of the number of secondary electrons mi emitted from the dynodes;
Poisson distribution:
Standard deviation:
 fluctuations dominated by 1st dynode gain m1 = d1
Pulse height
Counts
(H. Houtermanns,
NIM 112 (1973) 121)
Gain fluctuations of PMT’s
(Photonis)
1 pe
Pedestal noise
CuBe dynodes EA>0
GaP(Cs) dynodes EA<0
SE coefficient d
Energy E
(Photonis)
Pulse height
Counts
SE coefficient d
Electron energy
1 pe
2 pe
3 pe
(Photonis)

## Slide 85
Light absorption in Silicon
(http://pdg.ge.infn.it/~) deg/ccd.html
At large l, temperature effects become important

## Slide 86
Uozumi@VCI2007
Multi pixel G-APD = G-APD, MPPC, SiPM, …
You cannot get "something for nothing”
G-APD show dark noise rate in the O(100 kHz – MHz / mm2) range.
The gain is temperature dependent O(<5% /°K)
The signal linearity is limited
The price is (still too) high
Hamamatsu catalog
~10 producers are now in the market. Continuous improvement in technology and performance.

## Slide 87
Barrel RICH
2  6 parabolic mirrors
gas radiator volume
1 single vessel
ca. 40 cm C5F12
p = 1030 mbar
2 liquid radiator
1 cm C6F14,
quartz windows
p = 985 mbar
2 drift tubes + 2 MWPC
(= 1 bitube)
gas: 75% CH4 + 25% C2H6, TMAE @ 28C
1 of 212 sectors

## Slide 88
3 liquid radiator trays
1 cm C6F14,
quartz windows
p = atm.
5 spherical mirrors
Forward RICH
1 of 212 sectors
2 drift boxes + 2 MWPC’s
gas: C2H6 + TMAE (24ºC)
Tvessel  30°C, unregulated.
aL  50°
gas radiator volume
2 half vessels / side
ca. 50 cm C4F10
p = atm.

## Slide 89: Separation of kaons and pions
Pions vs kaons in TOP:
different patterns in the time vs PMT impact point coordinate
Pions vs kaons:
Expected PID efficiency and misidentification probability.

## Slide 90
1 p.e.
pulse height (ADC counts)
2 p.e.
3 p.e.
4 p.e.
5 p.e.
pulse height signals of
1 Si pad
HVHPD = 26 kV
Pedestal cut
10-inches (25.4 cm)
10-inch prototype HPD (CERN)
for Air Shower Telescope CLUE.
Photon counting. Continuum due to electron back scattering.
Hybrid Photon Detectors (HPD’s)

## Slide 91
Thickness
monitor
PC
Remote controlled
enclosure box
CsI photocathode produced with a well defined, several step procedure, with CsI vacuum deposition and subsequent heat conditioning.
CsI doesn’t like water !!!
 Assembly of cathode and wire chamber in a glove box.
4 CsI sources
+ shutters
protective box
pcb substrate
CERN CsI deposition plant

## Slide 92: Next step: use arrays of SiPMs
E. Tahirović et al., NIM A787 (2015) 203
Example: Hamamatsu MPPC S11834-3388DF
8x8 SiPM array, with 5x5 mm2 SiPM channels
Active area 3x3 mm2
+ array of quartz light collectors

## Slide 93: Digital SiPM
Digital SiPM (Philips): instead of an analog sum of signals from all cells of a single SiPM, use on board electronics for a digital sum + time stamp
 A.Y. Barnyakov et al., NIM A732 (2013) 352

## Slide 94: Particle ID by Transition radiation
only high energetic e± emit TR of detectable intensity.
 particle ID
medium
vacuum
TR is electromagnetic radiation emitted when a charged particle traverses a medium with a discontinuous refractive index, e.g. the boundaries between vacuum and a dielectric layer.
A (too) simple picture
Radiated energy per medium/vacuum boundary
(there is an excellent review article by B. Dolgoshein (NIM A 326 (1993) 434))
Transition Radiation was predicted by Ginzburg and Franck in 1946
(G. Garibian, Sov. Phys. JETP63 (1958) 1079)
A correct relativistic treatment shows that…
electron

## Slide 95
event with an electron (yellow track)
hits with high signal (=TR, passing a high level HL threshold) are indicated in red
TR turn ON curve: HL probability VS gamma factor
HL hit probability for electrons 4 times higher than for minimum ionising particles (muons)
TRT Performance - Particle Identification

## Slide 96: Particle ID by Transition radiation
one order of magnitude in Rejection Power is gained when the TRD length is increased by ~ 20 cm
Rejection Power : Rp/e = ep/ee (90%)