## Slide 1
CRP and mechanical structure design for Vertical Drift
B.Aimard, G.Deleglise, D.Duchesneau, N.Geffroy, H.Meringolo
Overview and general characteristics
  Layout and dimensions
  Thermal contraction aspects
Preliminary mechanical calculations
  Anode attachment points
  Supporting PCB frame
  Super CRP structures
Summary

## Slide 2: Mechanical design
CRP
CRP
Super-structure
Top
Bottom

## Slide 3: Top Detection plane design
6720 mm
9000 mm

## Slide 4: Super-CRP design
1500 mm
1680 mm
Structural PCB Sandwich
- less than 200 kg (to be refined)
Super-structure
Invar
About 1600 kg (before diet)
3 anchoring points
Anode plane
46kg (four panels of 11,5 kg)
3000 x 3375 mm
Total Super-CRP mass : 2800 kg
Cathode mass estimation : 600 kg
Mass/suspension cable : 1200kg
Anode planarity specification : +/-2,5mm @ cold

## Slide 5: Top plane – mechanical concepts
Cathode, 10kg/m²
Super-structure (invar)
PCB Sandwich
PCB Sandwich
Cable suspensions
Suspension
Lateral decoupling
+ Vertical pre-tuning
Suspension
Planarity tuning from below
Anode plane, planarity +/- 2,5mm
Cathode plane, planarity +/- 5mm
Liquid level
Cathode support structure design is started with IJCLab and interface to the superstructure is being defined
Suspension feedthroughs (SPFT)

## Slide 6: Top plane – Decoupling/adjusting systems
- Easy connection
- Lateral sliding
- Vertical adjustment
-> 5 pieces / CRP
- Vertical adjustment
- Compacity
- Electrical insulation
(non-metallic screw)
-> 36 pieces / Anode plane
PCB frame
Anode
PCB frame

## Slide 7
14000mm
Top membrane
bottom membrane
Top CRP
bottom CRP
Liquid level
Ullage space: 4% of total volume = 560mm
=> vertical space CRP structure to membrane = 100mm
13340mm
cathode
13.34m available for:
  bottom CRP (~100mm)
  top CRP (~350mm)
  cathode (~50 mm)
  2 drift regions
~6.4 m
~6.4 m
Vertical dimension range:

## Slide 8: Top part – Some dimensions
Liquid level
560 mm
~350 mm
~6400 mm
~ 400 mm ?
~ 550 mm ?
Indicative numbers to be refined after optimisation steps
Suspension FT (SPFT)

## Slide 9: Integration
SuperStructure type 1 (x12)
SuperStructure type 2 (x4) (proposal)
6 CRPs
2 CRPs instead of 4
Functionnal clearances used for this work:
Inside Super-structure : 2mm between CRPs
Inter super-structure: 20-40 mm (for the moment)
=> it adds +140mm along beam direction
=> it adds+24mm along transverse direction
Total detector max length at warm should be 60200mm and a maximal width of 13700mm
(to stay within the Field Cage area) => even less to have some clearance with FC
L = 60140 mm (clearance to be studied)
W = 13530 mm 

## Slide 10: INVAR – Possible Clearances wrt Field Cage
Field Cage
Clearance between SuperStructure and Field Cage is small along longitudinal axis
78 mm
40 mm
18 mm
20 mm

## Slide 11
Top plane – Thermal contraction pattern
Superstructure: Invar CRP: PCB material
WARM
COLD
Each interCRP gap increases by about 4mm inside a superstructure and by 7 mm inter Superstructure
– More details in following slides
Sketch of the complete VD area
Gaps due to thermal shrinkage are uniformly distributed if functional clearances between Superstructures are kept minimal
(comparison with Stainless steel Superstructure material under progress)

## Slide 12: Invar Superstructure Type 1 and CRPs: thermal contraction
COLD
WARM
Thermal shrinkage (external anode plane dimensions of a full superstructure) :
  D(length) = 7,17 mm
  D(width) = 6,81 mm
Each individual CRP shrinks by about 5-6 mm
Inter CRP gaps increase from 2mm to 6mm within a superstructure

## Slide 13: Anode relative positions at COLD
Illustrated gaps are distances between anodes of 2 consecutive SuperStructures
frame
anode
frame
anode
Warm
Cold
20
26,81
23,34
The 20mm functionnal clearance needs to be fine tuned to allow enough for installation and cope with the field cage area

## Slide 14: SPFT wrt cryostat
Possible positions of SPFT – Functionnal clearance defines SPFT positions
(yellow circles diameters are arbitrary - just for eye guidance)

## Slide 15: SPFT wrt cryostat
In order to avoid interference with cryostat structure, the position of suspension cables will have to be adjusted
(the optimal would have been to have the triangle centered wrt SSt) but not possible with actual cryostat layout
If the displacement is unavoidable => to be optimised in the calculations for the 3 suspensions to allow enough space between the SPFT and the cryostat structure.
The superstructrure asymmetric deformation will be treated at installation in that case
Example of the SPFT offset
Drawing from Dimitar (5/11/20)

## Slide 16: Bottom plane design
Individual CRPs structure is identical to Top-plane
Consists of 4 anodes planes
3000 x 3375 mm
Supporting PCB sandwich frame
3m
3.375m

## Slide 17: Bottom plane – Mechanical concepts
Lateral decoupling
(PTFE, bearing, … )
Vertical adjustment
Only laid on the membrane
No fixation, no sliding on the membrane

## Slide 18: Bottom plane – Mechanical concepts
One rotation is locked
PCB
100 mm for membrane corrugation + cables
Center point lateral displacement is locked
Thermal contraction pattern is idendical to Top-Plane, based on the membrane
« Squares » of the membrane are contracting around their own center

## Slide 19: Mechanical simulations
Anode attachement points
PCB support frame
Super-CRP structure
1
2
3

## Slide 20: Anode material caracterisation for simulation
Young Modulus adaptation : 3390 MPa (26400 MPa for initial material in Ansys library)
To be confirmed and validated with real tests (to discuss with PCB suppliers)
Adapted Young Modulus :
3390 MPa
Initial Young Modulus :
26400 MPa
Dimensions : 1500 x 1680 (=3x0,56) x 3,2 mm
PCB initial density : 1850 kg/m3
PCB corrected density for anode simulation : 1424,32 kg/m3
Corrected Young Modulus : 3390 MPa (26400 for initial material)
Anode Mass for a 3000 x 3375 mm plane : 46 kg
Hole pattern as tested on small scale proto at CERN

## Slide 21: Simulation 1 : Anode support – Initial config
  Initial configuration :
  -> 1,5m x 1,68m anode plane, supported by 36 uniformaly distributed screws
    Max displacement : 0,3 mm
    Average displacement : 0,15 mm (similar along borders)

## Slide 22
Bo suggestion from 9/11/2020 : 37 suspension points, higher density along borders
Simulation 1 : Anode support – Bo’s pattern
  Results :
    Max displacement (planarity deviation) : 0,75 mm
    Less than 0.2mm on the borders
    Has to be refined with exact screws positions
    Pattern to be discussed to conciliate electronics and deformations

## Slide 23
¼ of a CRP (TOP)
¼ of a CRP (Bottom)
1500 mm
1680 mm
1500 mm
1680 mm
288
Induction: 3.375m
Collection: 3 m
320
608
320
288
288
320
320
288
Full CRP (TOP)
Anode Layout, considered for further developments
In contact with Bo to integrate the design
the electronic adapter boards to be included in a next step

## Slide 24: Simulation 2 : Anode supporting structure
Anode plane suspended to PCB sandwich
G10 has different thermo-mechanical behaviour than PCB
=> use PCB to support PCB instead of G10
3000 x 3375

## Slide 25: Simulation 2 : Anode supporting structure
5 Anchoring points to super structure
Considered PCB ‘s material properties :
  E =26400 Mpa
  ᵨ =1850 kg/m3
Loading :
  Gravity
  451 N Force spread over 144
    (36 x 4) anode suspension points to stand for anode weight
Internal sandwich structure : - 50 mm high vertical stiffeners - Pitch corresponding to anode fixation (~300mm)

## Slide 26: Simulation 2 : Anode supporting structure
  3m x 3,375m PCB supporting structure :
    Max displacement : ~ 0,15 mm
    Weight of the structure : ~120kg, optimisation in progress
Can be done to save mass but increases complexity of structure
Can “drive” location of holes that will be necessary to pass signal cables
Topological optimisation

## Slide 27: Simulation 3 : Invar Super-Structure
Superstructure supporting 6 CRPs
Dimensions : 8m x 5m
2 Heights : 400mm and 200mm (crosses)
Plates thickness = 6,35mm
Weight : 1,6 tons

## Slide 28: Simulation 3 : Invar Super-Structure - Reference config
3 suspension points
Cathode is directly connected to the « summit » point
Step 1 : gravity (1,6 tons)
Step 2 : CRPs masses (200kg chaque)
Step 3 : Cathode mass (200kg x3)

## Slide 29: Simulation : Invar Super-Structure
Step 1 : gravity (1.6 ton) dmax = 5.3 mm
Step 2 : CRPs masses (200kg each) dmax = 9.6 mm
Step 3 : Cathode mass (200kg x3) dmax = 8.1 mm
Thickness = 6.35mm
Step 1 : gravity (1ton) dmax = 5.3 mm
Step 2 : CRPs masses (200kg each) dmax = 12.2 mm
Step 3 : Cathode mass (200kg x3) dmax = 12.3 mm
Thickness = 4mm
100mm lateral shift
Thickness = 6.35mm and
Top triangle suspension shifted by 100mm
Step 1 : gravity (1.6 ton) dmax = 9.2 mm
Step 2 : CRPs masses (200kg each) dmax = 16.2 mm
Step 3 : Cathode mass (200kg x3) dmax = 15.4 mm
100mm lateral shift
Reference
Reduced thickness
Shifted SPFT

## Slide 30: Invar Super-structure Load behaviour
Reduced thickness
dmax = 5.3 mm
dmax = 12.2 mm
dmax = 12.3 mm
Reference
Gravity: dmax = 5.3 mm
CRP masses: dmax = 9.6 mm
Cathode masses : dmax = 8.1 mm
Shifted anchoring
dmax = 9.2 mm
dmax = 16.2 mm
dmax = 15.4 mm
Immersion effects (Archimède) have to be estimated
More optimisation will be performed on this structure
Other design with stainless steel on going: first calculations performed

## Slide 31
Summary
This is a first design work on the CRP structures for VD detector:
Preliminary optimisation and calculations on anode, PCB frames and superstructures have shown results matching the defined criteria (at least for the symmetric suspended SuperStructure design)
CRP mechanical structures are identical between bottom and top
More optimisation and refinements needed and on going
Alternative structure material options are also considered and studied for the superstructure (SS)
Detailed definition of the CRP suspension points with cryostat feedthroughs positions in progress
Work on interface with cathode mechanical structure has started for the cathode frame suspension
Critical aspects to work on:
  Overall anode and superstructure dimensions in the cryostat to fit the area of the field cage
  Given the large SuperStructure dimensions and weights: important to asses reasonable functional clearances especially for installation => it cannot be only a few mm!
  Gaps needed for the cathode suspension to consider

## Slide 32
End

## Slide 33
Scénario A:
Superstructure: Invar
CRP: PCB
WARM
COLD
Each interCRP gap increases by about 6mm
9m
6.6m
Sketck of 2 neighbouring superstructure
2mm
4mm
9004mm
D mm
D+7 mm
Locked points on the structure

## Slide 34: INVAR – Possible Clearances wrt Field Cage
Field Cage
Clearance between SuperStructure and Field Cage is small along longitudinal axis
78 mm
40 mm
18 mm
20 mm

## Slide 35
7mm
7mm
Scénario C:
Superstructure: Stainless Steel
CRP: PCB
WARM
COLD
D mm
D+18mm
Locked points on the structure
7mm
5mm
8995mm
7mm
5mm
9014mm

## Slide 36: SSteel - Clearances wrt Field Cage
Field Cage
Clearance between SSt and Field Cage is small along longitudinal axis
73 mm
40 mm
12,5 mm
13 mm

## Slide 37: Production / installation

## Slide 38: Production
Production clean room(s)
Super-structures
Anodes
PCB panels
Machined parts
Tooling
(transport & installation)
Assembly / Glueing of PCB panels 3 x 3,375
Machined parts assembly
Anodes planes assembly 1,5 x 1,68
Electrical cabling
Packaging in transport boxes 3,5 x 3,5m
Manufactured in separable parts (inserable through TCO)
Max dimensions : 3000 x 3000?
Directly sent to cryostat
Manufacturers

## Slide 39: Installation : Cryostat
Super-structures assembly, on the cryostat ground
A super-structure cannot be transported in one piece
Super-structure 1/3
Super-structure 2/3
Super-structure 3/3
Super-structure 3/3
Super-structure 1/3
Super-structure 2/3

## Slide 40: Installation : Cryostat
Super-structure lifting with SPFT winches
Suspension points vertical pre-positioning
Planarity laser
Dummy CRP + cathodes masse
Dummy CRP + cathodes masse
Pre-stressed Super-structure

## Slide 41: Installation : Cryostat
Super-structure
CRP insertion in the cryostat
Lifting
Need for a structure on the ground to lay the CRP flat
Need a system to lift it
  Winches from super-structure?
  Plate-lifter?
Winch
Winch
Winch
Lifting structure

## Slide 42: Installation : Cryostat
Super-structure
Electrical connections
Mechanical connections
Need for a person lift to work at height
In function of the chimney position, need to step the planes under the super-stucture to do the connections
Electrical connections
SGFT
SGFT

## Slide 43
Connexions CRP - Signal
1
2
3
4
5
19
20
20 modules
1216
608
2432
1216
Top chimney topology: connexion at each CRP corner

## Slide 44: Installation : Cryostat
Planarity adjustment
Planarity laser
Super-structure
Dummy cathodes masse
Dummy cathodes masse
SGFT
SGFT
SGFT
SGFT

## Slide 45: Installation : Cryostat
Cathode
Super-structure
Cathode lifting and suspension
Winches?
Plate lift?
Winch
Lifting structure

## Slide 46: Installation : Bottom plane
Laser
Installation and pre-adjusting ot support feet

## Slide 47: Installation : Bottom plane
Laser
Réglage fin du plan d’anodes
Installation of CRPs (3000 x 3375mm each)
Merchanical and electrical connections
Planarity fine tuning
  Need to access above the planes

## Slide 48: Spare slides

## Slide 49: Simu. 1 : Anode support – alternative solution
  Alternative solution : less supporting screws (33 instead of 36)
  -> 1,5m x 1,68m anode plane
    Max displacement, outside part : 0,3 mm
    Max displacement, inside part : 1,3mm
    Few less screws, much higher displacements
    Not worth the change
    Material properties are very influential

## Slide 50: Anode material caracterisation for simulation
Dimensions : 1500 x 1680 (=3x0,56) x 3,2 mm
PCB initial density : 1850 kg/m3
PCB corrected density for anode simulation : 1424,32 kg/m3
Corrected Young Modulus : 3390 MPa (26400 for initial material)
Anode Mass for a 3000 x 3375 mm plane : 46 kg
To be validated with real tests
First contact with CCI EUROLAME (PCB supplier)
  Cedric Launay
  Max width : 1225 mm
  Max length : to be defined
  Coppered PCB
  Already in contact with CERN?
Masse volumique PCB plein | 1850 | kg/m^3
Longueur | 1680 | mm
Largeur | 1500 | mm
Epaisseur | 3,2 | mm
Diamètre des trous | 2,5 | mm
Espacement en largeur | 3,333333 | mm
Espacement en longueur | 2 | mm
Volume d'une plaque pleine | 0,008064 | m^3
Masse d'une plaque pleine | 14,92 | kg
Nombre de trous | 378000,0378 | trous
Volume de trous | 0,001855503 | m^3
Masse de trous | 3,43 | kg
Masse d'une anode 15x1,68 | 11,49 | kg
Masse d'un plan d'anode de 3x3,375 | 45,94 | kg
Densité corigée | 1424,32 | kg/m^3

## Slide 51
αanode = 8.10-6 K-1
αinvar = 1,8.10-6 K-1 (12.5% of PCB)
αStainless steel = 13.2.10-6 K-1
Thermal shrinkage at LAr temperature
CRP (anode + PCB frame)
3000 mm
3375 mm
2995mm
3369 mm
WARM
COLD
D = -5mm
D = -6mm
2 suspended point on INVAR structure separated by
3000 mm at warm => 2993mm at cold => -0.7mm between 2 CRPs
3375 mm at warm => 3366 mm at cold =>