## Slide 1: PyHEADTAIL examples
All our thanks to D. Amorim, Kevin Li, Lotta Mether and Michael Schenk CERN BE/ABP-HSC
and Martial Fol and Saïd Errghioui (AZIMUTEC), Marie Gauthier, Coline Morin, Stephanie Vandergooten et Lise Ribet (ESI)
Reference: http://kli.web.cern.ch/kli/

## Slide 2: Agenda
Goals
Plan
Introduction to PyHEADTAIL
Structure of ipython files
Tracking examples
Setting up the environment
  Virtual box
  Ubuntu
  Anaconda
  PyHEADTAIL

## Slide 3: Goals
Run macroparticle simulations with a state-of-the-art open source tracking code (PyHEADTAIL)
Simulate several case-studies related to the course
Play with beam parameters and observe the impact on the longitudinal beam dynamics

## Slide 4: Plan
1h00 towards the end of the course in the computer room
A virtual box with examples is prepared in the computer room
Following popular demand, it is also possible to set up your own simulation environment on your own PC.
The detailed procedure and examples are on the Indico site.
Note: we should expect incompatibilities linked to open source codes!

## Slide 5: Agenda
Goals
Plan
Introduction to PyHEADTAIL
Structure of ipython files
Tracking examples
Setting up the environment
  Virtual box
  Ubuntu
  Anaconda
  PyHEADTAIL

## Slide 6: Introduction to PyHEADTAIL
Open source macroparticle tracking code developed at CERN:
Download link: https://github.com/PyCOMPLETE/PyHEADTAIL
Primary use: tracking simulation of collective effects in synchrotron accelerators
  Transverse and longitudinal beam dynamics (with feedback)
  Electron/ion cloud
  Impedances
  Space charge
Reference: Introduction to PyHEADTAIL: USPAS course by Kevin Li et al (2015)
Not the only code of his kind!
  BLOND: longitudinal dynamics simulation code https://blond.web.cern.ch/
  HEADTAIL: the father of PyHEADTAIL! G. Rumolo et al (reference)
  elegant: 6D tracking code developed at Argonne National Lab (link)
  mbtrack and sbtrack: R. Nagaoka et al “Studies of Collective Effects in SOLEIL and DIAMOND Using the Multiparticle Tracking Codes sbtrack and mbtrack”, PAC09, Vancouver, May 2009.
  ORBIT (http://web.ornl.gov/~jzh/JHolmes/ORBIT.html), pyORBIT (http://sourceforge.net/projects/py-orbit/)
  And so many others!

## Slide 7: introduction to PyHEADTAIL
Courtesy Kevin Li
USPAS 2015

## Slide 8: introduction to PyHEADTAIL
Courtesy Kevin Li
USPAS 2015

## Slide 9: introduction to PyHEADTAIL
Courtesy Kevin Li
USPAS 2015

## Slide 10: introduction to PyHEADTAIL
Courtesy Kevin Li
USPAS 2015

## Slide 11: introduction to PyHEADTAIL
Courtesy Kevin Li
USPAS 2015

## Slide 12: introduction to PyHEADTAIL
Courtesy Kevin Li
USPAS 2015

## Slide 13: introduction to PyHEADTAIL
Courtesy Kevin Li
USPAS 2015

## Slide 14: introduction to PyHEADTAIL
Courtesy Kevin Li
USPAS 2015

## Slide 15: introduction to PyHEADTAIL
Courtesy Kevin Li
USPAS 2015

## Slide 16: introduction to PyHEADTAIL
Courtesy Kevin Li
USPAS 2015

## Slide 17: In our case: only RF systems

## Slide 18: Agenda
Goals
Plan
Introduction to PyHEADTAIL
Structure of ipython files
Tracking examples
Setting up the environment
  Virtual box
  Ubuntu
  Anaconda
  PyHEADTAIL

## Slide 19: Structure of the ipython file
Import needed libraries
Set beam and machine parameters
Generate a matched distribution corresponding to these parameters
Define RF system
track
monitor
plot
Loop over number of turns

## Slide 20: ipython cheat sheet
To restart the kernel at any point: “Kernel”  “Restart”
To only interrupt the kernel: “Kernel”  “Interrupt”
Shift-enter: execute current cell and move to next cell
Ctrl-enter: execute current cell and stay on current cell

## Slide 21: Agenda
Goals
Plan
Introduction to PyHEADTAIL
Structure of ipython files
Tracking examples
Setting up the environment
  Virtual box
  Ubuntu
  Anaconda
  PyHEADTAIL

## Slide 22: Tracking example: injection energy
0

## Slide 23: Tracking example: injection energy
0

## Slide 24: Let’s run that example
Use a small number of particles (n_particles~ 10) to observe the synchrotron motion at large and small amplitudes
 Can you estimate the synchrotron tune Qs? Is it consistent with the course?

## Slide 25: Synchrotron motion
Use a larger number of particles (~500) and reset the graph every time (“plt.cla()” uncommented)
Are the particles rotating in the correct direction?
Plot the phase space as in the course (in φ[degrees], ΔE [MeV])
Is the maximum energy consistent with the course?

## Slide 26: Top energy
What parameters should be changed for top energy (still no acceleration and h=8)?
What changes in the plot compared to injection energy?

## Slide 27: Agenda
Goals
Plan
Introduction to PyHEADTAIL
Structure of ipython files
Tracking examples
  Impact of phase mismatch
  Impact of voltage mismatch
  Impact of acceleration
Setting up the environment
  Virtual box
  Ubuntu
  Anaconda
  PyHEADTAIL

## Slide 28: Impact of phase mismatch
Remove the division by 10 in sigma_z_0
Generate ~1000 particles
Add e.g. 5 or 20 m to all particles:
Track particles for ~5000 turns
Plot the distribution every 10 or 100 turns:
 What will happen?

## Slide 29: Impact of phase mismatch
Use a smaller bunch length (e.g. divide by 10)
Generate ~1000 particles
Add e.g. 5m to all particles:
Track particles for ~5000 turns
Plot the distribution every 100 turns:
 What will happen?

## Slide 30: Impact of phase mismatch
Filamentation and eventually?
Use a smaller bunch length (e.g. divide by 10)
Use ~1000 particles
Add e.g. 5m to all particles:
Track particles for ~5000 turns
Plot the distribution every 100 turns:

## Slide 31: Impact of phase mismatch
Filamentation and eventually?
Use a smaller bunch length (e.g. divide by 10)
Use ~1000 particles
Add e.g. 5m to all particles:
Track particles for ~500000 turns
Plot the distribution every 1000 turns

## Slide 32: Impact of phase mismatch
 Eventually emittance growth
 Try also with larger mismatch (20 m)
Use a smaller bunch length (e.g. divide by 10)
Use ~1000 particles
Add e.g. 5m to all particles:
Track particles for ~500000 turns
Plot the distribution every 100 turns:

## Slide 33: Agenda
Goals
Plan
Introduction to PyHEADTAIL
Structure of ipython files
Tracking examples
  Impact of phase mismatch
  Impact of voltage mismatch
  Impact of acceleration
Setting up the environment
  Virtual box
  Ubuntu
  Anaconda
  PyHEADTAIL

## Slide 34: Impact of voltage mismatch (too high)
Use the nominal bunch length
track 1000 particles for 500 turns (plot every 10 turns)
Change V_RF to V_RF*10 after the bunch is matched to V_RF
 What will happen?

## Slide 35: Impact of voltage mismatch (too high)
Use the nominal bunch length
track 1000 particles for 500 turns (plot every 10 turns)
Change V_RF to V_RF*10 after the bunch is matched to V_RF
Bunch rotation
Bunch shortening, if phased correctly, but…

## Slide 36: Impact of voltage mismatch (too high)
Use the nominal bunch length
track 1000 particles for 5000 turns (plot every 100 turns)
Change V_RF to V_RF*10 after the bunch is matched to V_RF
But should not wait too long!
Emittance growth!

## Slide 37: Impact of voltage mismatch (too low)
Use the nominal bunch length
track 1000 particles for 500 turns (plot every 10 turns)
Change V_RF to V_RF/10 after the bunch is matched to V_RF
Adapt the deltap plotting limits

## Slide 38: Impact of voltage mismatch (too low)
Use the nominal bunch length
track 1000 particles for 500 turns (plot every 10 turns)
Change V_RF to V_RF/10 after the bunch is matched to V_RF
Adapt the deltap plotting limits

## Slide 39: Agenda
Goals
Plan
Introduction to PyHEADTAIL
Structure of ipython files
Tracking examples
  Impact of phase mismatch
  Impact of voltage mismatch
  Impact of acceleration
Setting up the environment
  Virtual box
  Ubuntu
  Anaconda
  PyHEADTAIL

## Slide 40: Impact of acceleration
Use the nominal bunch length
Use 200 particles
Use V_RF=20 kV
Use Bdot=2.2 T/s
Does it work? Why?

## Slide 41: Impact of acceleration
Use the nominal bunch length
Use 1000 particles
Use Bdot=2.2 T/s
Change VRF to 200 kV
Compute the synchronous phase
Plot the phase space in in φ[degrees], ΔE [MeV]

## Slide 42: Agenda
Goals
Plan
Introduction to PyHEADTAIL
Structure of ipython files
Tracking examples
  Impact of phase mismatch
  Impact of voltage mismatch
  Impact of acceleration
Setting up the environment
  Virtual box (if you do not have Linux already!)
  Ubuntu
  Anaconda
  PyHEADTAIL

## Slide 43: Setting up the operating system
Install a virtual box to get an Ubuntu environment
Ex: https://www.virtualbox.org/wiki/Downloads
Create a new virtual machine with Ubuntu 64-bit

## Slide 44
In case of a “VTx” error or an impossibility to select 64 bit operating system when launching the virtual machine, one needs to turn Virtualization Technology (VTx) on in the BIOS (see chapter 10.3 in https://www.virtualbox.org/manual/ch10.html#hwvirt )

## Slide 45: Create virtual machine

## Slide 46
 2 GB is recommended by Ubuntu. This setting can be modified later.

## Slide 49
 Assign 20 GB if possible.

## Slide 50: Tip: allow shared clipboard if you wish
In “settings”  “advanced” of the newly created VM

## Slide 51: Start the VM

## Slide 52: Agenda
Goals
Plan
Introduction to PyHEADTAIL
Structure of ipython files
Tracking examples
  Impact of phase mismatch
  Impact of voltage mismatch
  Impact of acceleration
Setting up the environment
  Virtual box
  Ubuntu
  Anaconda
  PyHEADTAIL

## Slide 53: Download ubuntu
https://www.ubuntu.com/download/desktop (beware quite large iso file – 2.6 Go)

## Slide 54: Select Ubuntu start up disk
You may have to click on the small green arrow to browse for your Ubuntu installation image

## Slide 55: Install ubuntu

## Slide 56: Choose the appropriate keyboard for your personal use (your physical keyboard configuration).
My keyboard is English (US)

## Slide 57: Choose normal installation

## Slide 58: Keep default installation and “install now” and confirm with “continue” on the pop up
Then choose time zone and login details

## Slide 59
Then wait for file copy and Ubuntu installation restart the machine after it is complete
If the screen is too small,
  Change the scaling/seettings in the VM
  or
  change the display settings inside Ubuntu or
  shut down the VM
  go to the VM Settings
  » Display
  » Screen
  » Graphics Controller = VBoxVGA

## Slide 60: Agenda
Goals
Plan
Introduction to PyHEADTAIL
Structure of ipython files
Tracking examples
  Impact of phase mismatch
  Impact of voltage mismatch
  Impact of acceleration
Setting up the environment
  Virtual box
  Ubuntu
  Anaconda
  PyHEADTAIL

## Slide 61: Install anaconda
Download anaconda for Linux at https://www.anaconda.com/distribution/#download-section
or type
> wget https://repo.anaconda.com/archive/Anaconda3-2020.11-Linux-x86_64.sh
Then install it by typing
> sh Anaconda3-2020.11-Linux86_64.sh
In the download directory

## Slide 62: Do not forget to add Anaconda to path (answer yes or add the path yourself in the “.bashrc” configuration file)
 Anaconda contains all the necessary libraries to run PyHEADTAIL.
Restart the shell (“>>source .bashrc” from the home directory)
Check that “>>ipython notebook” works

## Slide 63: Agenda
Goals
Plan
Introduction to PyHEADTAIL
Structure of ipython files
Tracking examples
  Impact of phase mismatch
  Impact of voltage mismatch
  Impact of acceleration
Setting up the environment
  Virtual box
  Ubuntu
  Anaconda
  PyHEADTAIL

## Slide 64: Installing PyHEADTAIL
website for installation and information: https://github.com/PyCOMPLETE/PyHEADTAIL
Add path to the end of the .bashrc to be able to import PyHeadtail from everywhere:
This only updates once a new terminal is opened (or do source ~/.bashrc)

## Slide 65
In case of issues with PyHEADTAIL installation, most likely it is that fortran and C need to be installed:
sudo apt-get install gfortran
Sudo apt-get install gcc

## Slide 66: Finding the examples
From JUAS 2021 Indico site in the last tutorial of the course: https://indico.cern.ch/event/976482/timetable/
 Download the *.ipynb files and open them browsing with “ipython notebook”

## Slide 67: Changing variables
For protons