## Slide 1: e+e- Circular Colliders
Frank Zimmermann
CERN, BE Department
JUAS, 28 January 2021
Work supported by the European Commission under Capacities 7th Framework Programme, Grant Agreement 312453
Geneva
Qinhuangdao

## Slide 2
centre-of-mass energy:
beam hits
a “fixed target”
two equal
beams collide
colliding two beams against each other can provide
much higher centre-of-mass energies than fixed target!
why colliders ? - energy
for two high-energy beams
of unequal energy
colliders were invented (1943) and patented (1953) by Rolf Wideröe

## Slide 3
colliders constructed and operated
Colliders with
superconducting arc magnet system
Colliders with
superconducting RF system
Colliders with
superconducting magnet & RF
advances by new technologies and new materials
A. Ballarino
Notes: New slide from Davide.
Showing that conductor development is launched at international level, Russia, Japan, (Korea and Europe in preparation)
Underline importance of that development as main cost driver for the hadron collider machine.

## Slide 4
colliders and discoveries
Standard Model
Particles and forces
powerful instruments for discovery and precision measurement
A. Ballarino
Notes: New slide from Davide.
Showing that conductor development is launched at international level, Russia, Japan, (Korea and Europe in preparation)
Underline importance of that development as main cost driver for the hadron collider machine.

## Slide 5
still many open questions
    Known matter is only 5% of universe!
    what is dark matter?
    what is dark energy?
    why more matter than antimatter?
    what about gravity?
also QCD,
quark-gluon plasma,
proton spin, etc.
F. Gianotti
Notes: New slide from Davide.
Showing that conductor development is launched at international level, Russia, Japan, (Korea and Europe in preparation)
Underline importance of that development as main cost driver for the hadron collider machine.

## Slide 6
collider figure of merit: luminosity
reaction rate
luminosity
R= s L
cross section
horizontal & vertical
rms beam size
at collision point
bunch
collision
rate
bunch
population
geometric factor
(crossing angle,
hour glass, pinch, …)
tends to
decrease
as energy-2
peak luminosity increased by almost
7 orders of magnitude over 60 years
V. Shiltsev & F.Z., arXiv:2003.09084, submitted to RMP

## Slide 7: Luminosity
N | Number of particles per bunch
nb | Number of bunches
f | Revolution frequency
σ* | Beam size at interaction point
G | reduction factor due to crossing angle and “hourglass effect”
ε | Emittance
εn | Normalized emittance
β* | Beta function at IP
M. Lamont
various limitations:
beam current (power)
beambeam tune shift
beamstrahlung….

## Slide 8
sketch of beam-beam collision
‘weak beam’ particles

## Slide 9
(nonlinear) beam-beam force
center of
opposing
beam
at small amplitude similar to effect of defocusing quadrupole
for single
collision
for pure head-on collision

## Slide 10
luminosity and vertical tune-shift parameter versus beam current for various electron-positron colliders; the tune shift saturates at some current value, above which the luminosity grows linearly
J. Seeman, SLAC-PUB-3825, 1985
beam-beam limit in e+e- colliders

## Slide 11: beam-beam limit in e+e- colliders with strong radiation damping
damping decrement per IP
R. Assmann,
K. Cornelis

## Slide 12
Future Circular Collider Study
launched in 2014
international FCC collaboration (CERN as host lab) to study:
pp-collider (FCC-hh)  defining infrastructure requirements
80-100 km infrastructure in Geneva area
e+e- collider (FCC-ee) as a possible first step
p-e (FCC-he) option, HE-LHC …
~16 T  100 TeV pp in 100 km

## Slide 13
CepC/SppC study (CAS-IHEP), 100 km collider,
one of the proposed sites
Qinhuangdao (秦皇岛）
easy access
300 km east
from Beijing
3 h by car
1 h by train
Yifang Wang
CepC, SppC
“Chinese Toscana”
100 km
50 km

## Slide 14
FCC-ee physics requirements
beam energy range from 35 GeV to 200 GeV
highest possible luminosities at all working points
physics programs / energies:
  Z (45.5 GeV) Z pole, ‘TeraZ’ and high precision MZ & GZ
  W (80 GeV) W pair production threshold, high precision MW
  H (120 GeV) ZH production (maximum rate of H’s)
  t (182.5 GeV): threshold, H studies
  more (aQED etc.)
possibly H (63 GeV) direct s-channel production with monochromatization
some polarization up to ≥80 GeV for beam energy calibration
A. Blondel, J. Ellis , C. Grojean, P. Janot, et al.

## Slide 15
circumference 27 km
in operation from 1989 to 2000
maximum c.m. energy 209 GeV
maximum synchrotron radiation power 23 MW
LEP/LEP2: highest energy so far
LEP energy close to FCC-ee target + record synchrotron radiation with ~MeV photons

## Slide 16
KEKB & PEP-II: high current, high L
KEKB
PEP-II
KEKB design
PEP-II design
source: KEK
Ie+=3.2 A, Ie-=2.1 A
Ie+=1.6 A, Ie-=1.2 A
PSR ~ 5 MW
C = 3 km
PSR ~ 8 MW
C = 2.2 km
performance of high-current high-luminosity e+e- factories
conservatively predicted

## Slide 17
Before Top-Up
After Top-Up
J. Seeman
average luminosity ≈ peak luminosity
J. Seeman
similar results from KEKB
KEKB & PEP-II: top-up injection
first colliders with top-up injection (constant current, no transients, continuous optics tuning,…)

## Slide 18
DAFNE: “crab waist” collisions
DAFNE Peak Luminosity
CRAB-WAIST Collision Scheme
Design Goal
M. Zobov

## Slide 19
crab-waist crossing for flat beams
regular crossing
crab waist -
vertical waist position
in s varies with horizontal
position x
allows for small by* and for small ex,y
and avoids betatron resonances (→higher beam-beam tune shift)
P. Raimondi,
et al.

## Slide 20
Marica Biagini
combining successful ingredients of several recent colliders → highest luminosities & energies
FCC-ee design concept
based on lessons and techniques from past colliders (last 40 years)
Marica Biagini
B-factories KEKB & PEP-II:
double-ring colliders,
high beam currents,
top-up injection
DAFNE: crab waist, double ring
S-KEKB: low by*, crab waist
LEP: high energy, SR effects
VEPP-4M, LEP: precision E calibration
KEKB: e+ source
HERA, LEP, RHIC: spin gymnastics

## Slide 21
FCC consistent machine layouts
FCC-hh
FCC-ee 1, FCC-ee 2,
FCC-ee booster (FCC-hh footprint)
consistent optics solutions for both machines available
9 m off-centred IPs
wrt. hh IPs

## Slide 22
similar solutions for FCC-ee and CEPC
FCC
Double ring colliders with full-energy top-up booster ring,
CEPC evolved from initial 54 km - single-ring design, practically to the FCC-ee 100 km design.
2 IPs, 2 RF straights, tapering of arc magnet strengths to match local energy
Asymmetric IR layout to limit SR of incoming beams towards detectors and generate large crossing angle
Common use of RF systems for both beams at highest energy working point (ttbar/ZH for FCC-ee/CEPC)

## Slide 23
A. Blondel, H. Burkhardt, M. Koratzinos, K. Oide
weak bends and asymmetric optics to soften SR photons emitted towards detector
SR fans in the interaction region (IR)

## Slide 24
curved orbit of e- in magnetic field
L. Rivkin

## Slide 25: final focus chromaticity
spot size increase due to (uncorrected) chromaticity,
d=0
d>0
d<0

## Slide 26
ttbar 182.5 GeV
4 sextupoles (a – d) for local vertical chromaticity correction and crab waist, optimized for each working point.
Common arc lattice for all energies, 60 deg for Z, W and 90 deg for ZH, tt for maximum stability and luminosity
yellow boxes:
dipole magnets
asymmetric IR optics to suppress synchrotron radiation toward the IP, Ecritical <100 keV from 450 m from IP (e)
FCC-ee asymmetric crab waist IR optics
K. Oide

## Slide 27
by* = 0.8 mm achieved in both rings in summer 2020 – using the FCC-ee-style “virtual” crab-waist collision scheme
Design: double ring e+e- collider as B-factory at 7(e-) & 4(e+) GeV; design luminosity 8 x 1035 cm-2s-1; by* 0.3 mm; nano-beam – large crossing angle collision scheme (crab waist w/o sextupoles); beam lifetime5 minutes; top-up injection; ce+ rate up to 2.5 1012 /s ; under commissioning
Y. Funakoshi, Y. Ohnishi, K. Oide
SuperKEKB is demonstrating FCC-ee key concepts
M. Tobiyama, K. Oide
SuperKEKB – pushing luminosity and b*

## Slide 28
synchrotron radiation power
energy loss per turn
critical (typical)
photon energy
arc synchrotron radiation (SR) 1
→ RF power
→ RF voltage
→ shielding
numerical values
for electrons
electrons: 23 MW for LEP, 100 MW for FCC-ee
protons: MW for LHC, 5 MW for FCC-hh
electrons: Ec,g 1 MeV
for LEP and FCC-ee;
protons: Ec,g ~40 eV LHC,
~4 keV FCC-hh

## Slide 29
arc synchrotron radiation 2
equilibrium emittance due to balance of radiation damping and quantum excitation
radiation damping of transverse and longitudinal motion
→beam shrinkage
electrons: 3 ms for LEP, 20 ms FCC-ee at 240 GeV cm
protons: 13 h for LHC, 0.5 h FCC-hh
increase of emittance with energy is compensated by large radius (r) and short cell length (lb)
→ cell length

## Slide 30
transverse emittances
Y. Papaphilippou

## Slide 31
horizontal emittance / g2
FCC-ee outperforming most of the
“ultimate storage ring” light sources
R. Bartolini, S. Casalbuoni

## Slide 32
vertical emittance & chromaticity
T. Charles
FCC-ee emittance and chromaticity Q’/Q similar to SIRIUS light source

## Slide 33
FCC-ee luminosity per IP

## Slide 34: can we understand the luminosity scaling ?
H  1
Hour-glass
2F
F  1
Crossing angle
Beam-beam parameter
J. Wenninger
ρ: bending radius

## Slide 35
x4
>x4.5
x1/25-1/50
<x2
>x2
luminosity from LEP-2 to FCC-ee
much bigger factors on the Z pole: 105LEP-1 luminosity !

## Slide 36
CDR baseline parameters
parameter | FCC-ee |  |  |  | LEP2
energy/beam [GeV] | 45.6 | 80 | 120 | 182.5 | 105
bunches/beam | 16640 | 2000 | 328 | 48 | 4
beam current [mA] | 1390 | 147 | 29 | 5.4 | 3
luminosity/IP x 1034 cm-2s-1 | 230 | 28 | 8.5 | 1.6 | 0.0012
energy loss/turn [GeV] | 0.036 | 0.34 | 1.72 | 9.2 | 3.34
synchrotron power [MW] | 100 |  |  |  | 22
RF voltage [GV] | 0.1 | 0.75 | 2.0 | 4.0+6.9 | 3.5
rms bunch length (SR,+BS) [mm] | 3.5, 12 | 3.0,6.0 | 3.2, 5.3 | 2.0, 2.5 | 12, 12
rms emittance ex,y [nm, pm] | 0.27, 1 | 0.84, 1.7 | 0.63, 1.3 | 1.5, 2.9 | 22, 250
longit. damping time [turns] | 1273 | 236 | 70 | 20 | 31
crossing angle [mrad] | 30 |  |  |  | 0
beam lifetime [min] | 68 | 59 | 12 | 12 | 434
FCC-ee & CEPC: 2 separate rings

## Slide 37: beamstrahlung – a new limit at 182 GeV
hard photon emission at the IPs, ‘Beamstrahlung’, can become lifetime / performance limit for large bunch populations (N), small hor. beam size (sx) & short bunches (ss)
r : mean bending radius at the IP (in the field of the opposing bunch)
for acceptable lifetime, rh must be sufficiently large
  flat beams (large sx) !
  bunch length !
  large momentum acceptance: aiming for >2% at 182.5 GeV
    - LEP: <1% acceptance, SuperKEKB ~ 1.5%
h : ring energy acceptance
g
e
e
lifetime expression by V. Telnov, modified version by A. Bogomyagkov et al
J. Wenninger, et al

## Slide 38
beside the collider ring(s), a booster of the same size (same tunnel) must provide beams for top-up injection to sustain the extremely high luminosity
  same size of RF system, but low power (~ MW)
  top up frequency ≈0.1 Hz
  booster injection energy ≈5-20 GeV
  bypass around the experiments
A. Blondel
FCC-ee top-up injection

## Slide 39
dynamic aperture
K. Oide
adequate dynamic aperture on- and off-momentum

## Slide 40
dynamic aperture limited by synchrotron radiation in quadrupoles !
Horizontal plane:
Radiative Beta-
Synchrotron Coupling (RBSC) [Jowett, 1994] –
additional energy loss due to radiation in quadrupoles shifts synchronous point and develops large synchrotron oscillations. → resulting horizontal tune shift onto the integer resonance
Vertical plane:
Radiation from quadrupoles modulates the particle energy
at twice the betatron frequency → parametric resonance independent of tune
dynamic aperture with
and without deterministic synchrotron radiation in quadrupoles (w/o quantum fluctuations)
A. Bogomyagkov et al.,
PRAB 22, 021001 (2019) ;
J. Jowett, Proc. 4th Workshop on LEP Performance,
CERN SL/94-06 (DI) (1994)

## Slide 41
LEP2
LHC
HL-LHC
Multi-years cycles for LHC
Cycles: 9m+3m
Cycles: 3 or 4 x (10m+2m) + 1.5yr
V. Mertens
energy consumption – example CERN

## Slide 42
RF as main power consumer
continually supplying circulating beam with
PSR=100 MW power (SR losses) requires
wall-plug power Pwall=PSR/h , note
with h=conversion efficiency wall-plug → beam
FCC strategy:
RF system optimized for each energy
higher-gradient SC cavities (negligible wall losses, low cryo power)
highly efficient RF power sources

## Slide 43
3 – 4 MV/m
Multipacting
5 MV/m
Thermal Breakdown
10 – 15 MV/m
Field Emission
Q > 5e10
At medium field !!
Q > 2e10
At high field
?
Eacc > 100 MV/m
Q > 3e10
Enabling future efficient High Energy Machines
Anna Grassellino - ICFA 2017
20 - 25 MV/m
High field
Q-SLOPE
35 – 40 MV/m
mid field Q-slope
bulk Nb, 1.3 GHz, 2K
SRF cavities over 30 years | high Q0 & Eacc → less cryopower
A. Grasselino, ICFA Seminar, Ottawa 2017
similar progress for Nb/Cu cavities

## Slide 44
after 80 years breakthrough in klystron technology
New bunching technologies.
Bunch saturation.
I. Syratchev

## Slide 45
twin-dipole magnet design with 2× power saving 16 MW (at 175 GeV), with Al busbars
prototype
prototype
A. Milanese, Efficient twin aperture magnets for the future circular e+/e- collider, Phys. Rev. Accel. Beams 19, 112401 (2016)
twin F/D arc quadrupole design with 2× power saving; 25 MW (at 175 GeV), with Cu conductor
2900 units, 10 T/m, 3.1 m
2900 units, 0.057 T, 22 m
low-cost, energy-efficient arc magnets

## Slide 46
Chart: electrical power budget [MW]
| Z | WW | ZH | ttbar
collider cryo | 1 | 9 | 14 | 46
booster rf & cryo | 3 | 4 | 6 | 8
collider rf | 163 | 163 | 145 | 145
magnets | 4 | 12 | 26 | 60
cooling & ventilation | 30 | 31 | 33 | 37
general services | 36 | 36 | 36 | 36
two experiments | 8 | 8 | 8 | 8
two data centres | 4 | 4 | 4 | 4
injector complex | 10 | 10 | 10 | 10
FCC-ee electrical power requirements

## Slide 47
M. Benedikt, A. Blondel, P. Janot, et al., Nat. Phys. 16, 402-407 (2020), and
European Strategy for Particle Physics Preparatory Group, Physics Briefing Book (CERN, 2019)
FCC-ee: efficient Higgs/electroweak factory
luminosity L per supplied electrical wall-plug power PWP is shown as a function of centre-of-mass energy for several proposed future lepton colliders
€200 electricity cost
per Higgs boson
Z
91 GeV
WW
160 GeV
ZH
240 GeV
350-365 GeV
FCC-ee is greenest collider from Z to

## Slide 48
SR effects of LEP
high currents of KEKB and PEP-II
top-up of KEKB and PEP-II
crab waist of DAFNE
crab waist & low by* of SuperKEKB
e+ source of KEKB
cryo availability of LHC
spin gymnastics of HERA
FCC-ee
individual parameters
mostly relaxed compared
with those in “demonstrator
machines”
“new” effects: beamstrahlung → lifetime limit, E spread,
synchrotron radiation in quadrupole magnets …

circular e+e- colliders: glorious history & exciting future
heeding lessons learnt:
trend & challenge: making future colliders truly green !

## Slide 49
“An e+-e - storage ring in the range of a few hundred GeV in the centre of mass can be built with present technology...” “…the most useful project on the horizon.”
Burt Richter, 1976
NIM 136 (1976) 47-60

## Slide 50
…surely great times ahead!
Kjell Johnsen
“Pief” Panofsky
Robert H. Wilson
Lyndon Evans
Herwig Schopper
Satoshi Ozaki
Mike Lamont
thank you !

## Slide 51
spare slides

## Slide 52: polarization
two primary interests:
accurate energy calibration using resonant depolarization  measurement of MZ, GZ, MW
  appealing feature – dMZ, dGZ ~ 0.1 MeV, dMW ~ 0.3 MeV
physics with longitudinally polarized beams
  transverse polarization must be rotated into the longitudinal plane using spin rotators (see e.g. HERA)
loss of polarization due to growing energy spread
LEP
scaling from LEP observations :
polarization expected up to the WW threshold !
Precession frequency  E
integer spin resonances are spaced by 440 MeV:
energy spread should remain below ~ 60 MeV
A. Blondel, M. Koratzinos, S. Mane, U. Wienands, J. Wenninger,..
R. Assmann
LEP like calibration up to the W threshold

## Slide 53: polarization build up
transverse polarization build-up (Sokolov-Ternov) is slow at FCC-ee (large bending radius r)
build-up is ~40 times slower than at LEP
tp 190 hours @ Z
wigglers may lower tp to ~12 h, limited by sE  60 MeV and power
  due to power loss the wigglers can only be used to pre-polarize some bunches (before main injection)
longitudinal polarization: levels of ≥ 40% required on both beams; excellent resonant compensation needed
  expected to be difficult, requires spin rotators or snakes, most likely only possible at lower intensity and luminosity
1 hour
 OK for energy calibration (few % P sufficient)
A. Blondel, U. Wienands, E. Gianfelice, J. Jowett, R. Rossmanith, J.Wenninger
SLIM, PETROS, SITF etc. simulations

## Slide 54
question of superperiodicity
SP=1
A
G
B
L
A
G
B
L
A
G
B
L
SP=1
SP=2
SP=4
resonance condition for lattice errors (DA) and for beam-beam
example 4 IPs
K. Oide
important for e+e-

## Slide 55
horizontal tune Qx
vertical tune Qy
particles at the center of the bunch
particles in the
transverse tail
tune spread
DQy
tune spread
DQx
beam-beam tune spread from head-on collision
maximum
acceptable
tune
spread
is limited
by resonances
nQx+mQy=p
up to resonance
order |n|+|m|~13
tune footprint

## Slide 56
horizontal tune Qx
vertical tune Qy
particles at the center of the bunch
particles in the
transverse tail
1 collision / turn
2 collisions / turn
tune spread
DQy

## Slide 57: luminosity scaling: damping
beam-beam parameter x measures strength of field sensed by the particles in a collision
beam-beam parameter limits are empirically scaled from LEP data (4 IPs)
In reasonable agreement with first simulations for FCC ee
J. Wenninger, R. Assmann, S. White, K. Ohmi, D. Shatilov, et al.
R. Assmann & K. Cornelis, EPAC2000
x4
x4.5
x1/25-1/50
<x2
FCC-ee
vs LEP
extremely high luminosity

## Slide 58
FCC-Conceptual Design Reports (completed in 2018):
  Vol 1 Physics, Vol 2 FCC-ee, Vol 3 FCC-hh, Vol 4 HE-LHC
  CDRs published in European Physical Journal C (Vol 1) and ST (Vol 2 – 4)
  EPJ C 79, 6 (2019) 474 , EPJ ST 228, 2 (2019) 261-623 , EPJ ST 228, 4 (2019) 755-1107 , EPJ ST 228, 5 (2019) 1109-1382
Summary documents provided to EPPSU SG
  FCC-integral, FCC-ee, FCC-hh, HE-LHC
  Accessible on http://fcc-cdr.web.cern.ch/
FCC CDR and Study Documentation
>1350 contributors from
> 350 institutes,
a truly global effort

## Slide 59
2020 Update of the European Strategy for Particle Physics
      Core sentence “order of the further FCC study”:
      “Europe, together with its international partners, should investigate the technical and financial feasibility of a future hadron collider at CERN with a centre-of-mass energy of at least 100 TeV and with an electron-positron Higgs and electroweak factory as a possible first stage. Such a feasibility study of the colliders and related infrastructure should be established as a global endeavour and be completed on the timescale of the next Strategy update.”