## Slide 1: Reverse engineering of TAS support jacks N. Kristensen EN-EA-PE 95th HL-LHC WP8 Meeting, November 24th 2020

## Slide 2: Why reverse engineer the support jacks?
Backlash found in one horizontal support jack
  Unknown reason causing the backlash
  Original drawings are only available in 2D
  3D drawings could help understand the mechanism
It is considered to manufacture a new support jack
  A reverse engineered model of the original could be used as a platform to design a new support jack
  An opportunity to take care of any concerns there might exist of the original design

## Slide 3: Challenges faced in the reverse engineering
Designed in America by University of California-Berkeley
  American dimensioning ex. holes, bearing seats, shaft diameter… (inches)
  American standard parts, ball bearings, bearings, washers, keys…
  CERN catalogue and Tracepartsonline.net mainly provide parts for the European metric system
Initially designed in year 2000
  The components used in 2000 is not necessarily similar to parts of today (jack screw)
Three missing drawings

## Slide 4: The process of reverse engineering
Three types of documents/files have been used in the process
  An Excel document – for overview of the process
  A word reporting document – for reporting how every item is reverse enginnered, or any complications there might have been
  CATIA files – the reverse engineered 3D model itself

## Slide 5: The process of reverse engineering
Three types of documents/files have been used in the process
  An Excel document – for overview of the process
  A word reporting document – for reporting how every item is reverse enginnered, or any complications there might have been
  CATIA files – the reverse engineered 3D model itself

## Slide 6: Original 2D model

## Slide 7: 3D model

## Slide 8: Evaluation of reverse engineered 3D model
Jack screw 3D model by Joyce Dayton
  Only provided as a non-editable version
  Has CERN customized features
  A shell model without mechanical parts
  It cannot be guaranteed that the model is similar to the original
Other standard components not found in its original version
  Some dimensions of several parts has been changed to compensate for the choice of parts with different dimensions
  Ultimately resulting in a compromising change of other dimensions
Despite some limitations, the work and the model is still considered to provide some insight into the working principals of the model, which can be used as platform from which further work can be based on

## Slide 9: Potential sources of backlash in horizontal support jack
Nothing can be guaranteed with certainty, only hypothesis
Potential sources
  Anti-backlash system - Without – as much as 0.4 mm of freeplay - With – best case, the freeplay is limited to 0.2 mm
  The use of external gearing system
  The use of grease - Radiation - Wrong positioning in the horizontal position
  16 bolt connections are used to make sure the support jack is tightly fixed. Could any of these be loosely fitted?

## Slide 10: What is next?
A report is being finalized
A new version will be designed from the ground up
  Will rely on the same mechanical principals
  Will be designed according to ISO standards (standard parts and the metric unit system)

## Slide 11: Thank you
And thanks to Maria for support and Francisco for insight