## Slide 1
Beam Loss Monitors
When energetic beam particles penetrates matter, secondary particles are emitted:
this can be e−, , protons, neutrons, excited nuclei, fragmented nuclei...
 Spontaneous radiation and permanent activation is produced.
 Large variety of Beam Loss Monitors (BLM) depending on the application.
Protection: Sensitive devices e.g. super-conducting magnets to prevent quenching (energy absorption by electronic stopping)
 interlock signal for fast beam abortion.
Operation: Alignment of the beam to prevent for activation
 optimal transmission to the target.
Accelerator physics: using these sensitive particle detectors for accelerator development.
Several devices are used, depending on particle rate and required time resolution
Some applications for usage

## Slide 2
Basic Idea of Beam Loss Monitors
Basic idea for Beam Loss Monitors BLM:
A loss beam particle must collide with the vacuum chamber or other insertions
Interaction leads to some shower particle:
e−, , protons, neutrons, excited nuclei, fragmented nuclei
detection of these secondaries by an appropriate detector outside of beam pipe
relative cheap detector installed at many locations
BLM detector
front-end
electronics
digitalization
& fast analysis
interlock
display
lost beam particle
Secondary products
from electro-magnetic or hadronic shower
vacuum pipe
beam

## Slide 3
Outline:
Physical process from beam-wall interaction
Different types of Beam Loss Monitors
different methods for various beam parameters
Machine protection using BLMs
Summary

## Slide 4
Scintillators as Beam Loss Monitors
Example: Analog pulses of plastic scintillator:
 broad energy spectrum
due to many particle species and energies.
Plastics or liquids are used:
detection of charged particles
by electronic stopping
detection of neutrons
by elastic collisions n on p in plastics
and fast p electronic stopping.
Scintillator + photo-multiplier:
counting (large PMT amplification)
or analog voltage ADC (low PMT amp.).
Radiation hardness:
plastics 1 Mrad = 104 Gy
liquid 10 Mrad = 105 Gy
Scintillator
2x2x5 cm3
Photo-multiplier
inside
HV base
40 ns
100 mV
Analog pulses U(t)
Pulse high distribution N(U)
50 mV

## Slide 5
Advantage:
Detection of fast electrons only
not sensitive to  & synch. photons
No saturation effects
Prompt light emission
Usage: Mainly at FELs for
short and intense pulses
Cherenkov detectors:
Passage of a charged particle v faster than propagation of light v > cmedium = c /n
Technical: Quartz rod n=1.5 & photomultiplier
Example: Korean XFEL behind undulator
Cherenkov light emission:
For v > cmedium = c /n
light wave-front like a wake
broadband light emission
H. Yang, D.C. Shin, FEL Conf. 2017
beam
11mm
v t

light propagation
beam
120mm
Cherenkov Light Detectors as Beam Loss Monitors

## Slide 6
Energy loss of charged particles in gases → electron-ion pairs → current meas.
W is average energy for one e- -ion pair:
Gas | Ionization Pot. [eV] | W-Value [eV]
Ar | 15.7 | 26.4
N2 | 15.5 | 34.8
O2 | 12.5 | 30.8
Air |  | 33.8
shower particle
Sealed tube Filled with Ar or N2 gas:
Creation of Ar+-e− pairs,
average energy W=32 eV/pair
Measurement of this current
Slow time response
due to  10 μs drift time of Ar+.
Per definition: Direct measurement of dose !
15 cm
Ionization Chamber as BLM
Notes: 6

## Slide 7
Ionization Chamber as BLM: TEVATRON and CERN Type
15 cm
38 cm
Parameter | TEVATRON, RHIC | CERN type
Size | 15cm,  6 cm | 50 cm,  9 cm
Gas | Ar at 1.1 bar | N2 at 1.1 bar
# of electrodes | 3 | 61
Voltage | 1000 V | 1500 V
Reaction time | 3 µs | 0.3 µs
TEVATRON, RHIC type
CERN type
4000 BLMs at LHC each  6m

## Slide 8
Different detectors are sensitive to various physical processes
very different count rate, but basically proportional to each other
 Linear behavior for all detectors
 Quite different count rate:
rIC < rBF3 < rliquid < rplastic
Example: Beam loss 800 MeV/u O8+
for different BLMs at GSI-synchr.:
Typical choice of the detector type:
Ionization Chamber:
Advantage:
- Measurement of absolute dose
Disadvantage:
- Low signal (low , eff, no neutron detection),
- Sometimes slow, ion drift time 10 ... 100 µs
 Often used at proton accelerators
Scintillator, Cherenkov detector:
Advantage:
- Fast current reading or particle counting
- Can be fabricated in any shape, cheap
Disadvantage:
- Need calibration in many cases
- Might suffer from radiation
 Often used at electron accelerators
Comparison of different Types of BLMs

## Slide 9
Outline:
Physical process from beam-wall interaction
Different types of Beam Loss Monitors
different methods for various beam parameters
Machine protection using BLMs
interlock generation for beam abort
Summary

## Slide 10
Machine Protection Issues for BLM
Losses lead to permanent activation  maintenance is hampered
and to material heating (vacuum pipe, super-cond. magnet etc.)  destruction.
Types of losses:
Irregular or fast losses by malfunction of devices (magnets, cavities etc.)
 BLM as online control of the accelerator functionality and interlock generation.
Regular or slow losses e.g. by lifetime limits or due to collimator
 BLM used for alignment.
Demands for BLM:
High sensitivity to detect behavior of beam halo e.g. at collimator
Large dynamic range:
 low signal during normal operation, but large signal in case of malfunction
 detectable without changing the full-scale-range
e.g. scintillators from 102 1/s up to 107 1/s in counting mode.
Monitoring of loss rate in control room and as interlock signal for beam abortion.

## Slide 11
Application: BLMs for Quench-Protection
Super-conducting magnets can be heated above critical temperature Tc by the lost beam
 breakdown of super-conductivity = ’quenching’.
 Interlock within 1 ms for beam abortion generated by BLM.
Position of detector at quadruples due to maximal beam size.
High energy particles leads to a shower in forward direction  Monte-Carlo simulation.
dispersion
x-function
y-function
lost
protons
dipole
dipole
0
10
20
30
40
50
Beam path s (m)
quadrupole
Example: Simulation of lost protons at LHC at 450 GeV
 at focusing quad. D & x maximum
Example: Simulation of shower particles
4
Beam path s (m)
0
8
12
Beam Loss Monitors
B. Dehning, JAS 2014, CERN-2016-002

## Slide 12
Poll concerning longitudinal Phase Space
Poll 28:
Which answer is wrong? Beam loss monitors are used …
to prevent for unnecessary activation
as a system to restrict people access outside of the accelerator shielding
for quench protection for super-conducting components
for beam alignment
Notes: 12

## Slide 13
Summary Beam Loss Monitors
Measurement of the lost fraction of the beam:
detection of secondary products
sensitive particle detectors are used outside the vacuum
cheap installations used at many locations
Depending on the application different types are used:
Frequently used:
Scintillators: very sensitive, fast response, largest dynamics, not radiation hard
PIN diode: insensitive, fast response, not radiation hard, cheap
IC: medium sensitive, slow response, radiation hard, cheap, absolute measurement of dose
Used for special application:
(Electron Multiplier: medium sensitive, fast response, radiation hard)
BF3 tube: only neutrons, slow response, radiation hard, expensive
Optical fibers: insensitive, very slow, radiation hard, very high spatial resolution.
Used as interlock in all high current machines for protection.
Additionally used for sensitive ‘loss studies’.