## Slide 1
Conclusion for Beam Diagnostics Course
Diagnostics is the ’sensory organ’ for the beam.
It required for operation and development of accelerators
Four types of demands leads to different installations:
Quick, non-destructive measurements leading to a single number or simple plots.
Instrumentation for daily check, malfunction diagnosis and wanted parameter variation.
Complex instrumentation used for hard malfunction and accelerator development.
Automated measurement and control of beam parameters i.e. feedback
A clear interpretation of the results is a important design criterion.
General comments:
Good knowledge of accelerators, general physics and technologies is needed.
Quite different technologies are used, based on various physics processes.
Each task and each technology calls for an expert.
Accelerator development goes parallel to diagnostics development.
Interesting and challenging subject!

## Slide 2
Beam Quantities and their Diagnostics I
LINAC & transport lines: Single pass  Synchrotron: multi pass
Electrons: always relativistic  Protons/Ions: non-relativistic for Ekin < 1 GeV/u
Depending on application: Low current  high current
Overview of the most commonly used systems:
Beam quantity |  | LINAC & transfer line | Synchrotron
Current I | General Special | Transformer, dc & ac Faraday Cup Particle Detectors | Transformer, dc & ac Pick-up Signal (relative)
Profile xwidth | General Special | Screens, SEM-Grids Wire Scanners, OTR Screen MWPC, Fluorescence Light | Ionization Profile Monitor Wire Scanner, Synchrotron Light Monitor
Position xcm | General Special | Pick-up (BPM) Using position measurement | Pick-up (BPM)
Transverse Emittance εtran | General Special | Slit-grid Quadrupole Variation Pepper-Pot | Ionization Profile Monitor Wire Scanner Transverse Schottky

## Slide 3
Beam Quantities and their Diagnostics II
Destructive and non-destructive devices depending on the beam parameter.
Different techniques for the same quantity  Same technique for the different quantities.
Beam quantity |  | LINAC & transfer line | Synchrotron
Bunch Length Δφ | General Special | Pick-up Secondary electrons | Pick-up Wall Current Monitor Streak Camera Electro-optical laser mod.
Momentum p and Momentum Spread Δp/p | General Special | Pick-ups (Time-of-Flight) Magnetic Spectrometer | Pick-up (e.g. tomography) Schottky Noise Spectrum
Longitudinal Emittance εlong | General Special | Buncher variation Magnetic Spectrometer | Pick-up & tomography
Tune and Chromaticity Q, ξ | General Special | --- --- | Exciter + Pick-up Transverse Schottky Spectrum
Beam Loss rloss | General | Particle Detectors | 
Polarization P | General Special | Particle Detectors Laser Scattering (Compton scattering) | 
Luminocity L | General | Particle Detectors | 

## Slide 4
Conclusion for Beam Diagnostics Course
For a successful construction and operation of an accelerator,
the understand and appropriate balance of all disciplines is required!
Beam diagnostics
Thank you for your attention!
Beam dynamics
Beam optics
Power supplier
Electrical engineering
Operation
Radio frequency
Magnets
Maintenance