## Slide 1: 3D-Finite Element Methods for Frequency Domain Impedance Modeling Erion Gjonaj Elektromagnetic Field Theory Technische Universität Darmstadt, Germany
November 23, 2020

## Slide 2: Frequency Domain Formulation
The 3D frequency domain problem
Weak formulation: find * such that:
boundary fluxes
High-order hierarchical FEM

## Slide 3: Frequency Domain Formulation
Treatment of boundary surfaces
Resistive wall boundaries
  Simple modification of the system matrix on SIBC surfaces
  No fitting of the surface impedance function or ADE/convolution is needed
resistive wall
in & outgoing pipes

## Slide 4: Frequency Domain Formulation
Beam pipe boundary conditions
  For an ultra-relativistic bunch (same idea for β < 1):
    solve 2D-electrostatic problem at both ends of the pipe
  Beam pipe BC and modal contribution to the RHS
    …do this for all waveguide modes supported in the pipe

## Slide 5: Frequency Domain Formulation
Beam pipe boundary conditions
  For an ultra-relativistic bunch (same idea for β < 1):
    solve 2D-electrostatic problem at both ends of the pipe
Curl-conforming interpolation for singular source?
  Idea: use hybrid meshes exploiting tensor-product form of current
Charge conservation is violated on unstructured (tetrahedral) grids for singular source excitation

## Slide 6: Frequency Domain Formulation
Petra III collimator – hybrid meshes
TET
HEX
PYRA
Longitudinal wakefield on axis at 100MHz

## Slide 7: Frequency Domain Formulation
Petra III collimator – impedance
comparison with CST PS
Ez = 1GHz
Ez = 1.5GHz

## Slide 8: Resistive Wall Impedance
Lossy round pipe
  Analytical solution:
Large mesh errors in time domain codes
Sparse unstructured mesh
Few evaluation points in the frequency domain

## Slide 9: Generalized S-Matrix
Hybrid S-Matrix/Z-Matrix representation
  Concatenation for cascaded structures:
  Total scattering matrix:
Matching conditions:
Phys. Rev. Accel. Beams 23, 034601, March 2020
Notes: Coupled S-Parameter Calculation

## Slide 10: 1.3 GHz - TESLA cavities
Tesla 1.3GHz cavity
Downstream
Cell 1
Cell 2
Cell 3
Upstream
15 TE-Modes
15 TM-Modes
15 TE-Modes
15 TM-Modes
TEM, …

## Slide 11: 1.3 GHz - TESLA cavities
Tesla 1.3GHz cavity
10 Modes

## Slide 12: 1.3 GHz - TESLA cavities
20 Modes
Tesla 1.3GHz cavity

## Slide 13: 1.3 GHz - TESLA cavities
30 Modes
Tesla 1.3GHz cavity

## Slide 14: 200 MHz - SPS Cavities
SPS 33-cell-cavities (simulations by S. Zadeh, Rostock)
  Goal: minimize impedance peak at ~630MHz
  Determine optimal combination for the positions of coupler cells
  Fast optimization using generalized scattering matrices in freq. domain
Notes: SPS
For this reason, the components with large beam impedance in the SPS, including the two 44-cell
and four 33-cell cavities, have to be optimized in the framework of LIU. Beam dynamical
studies have shown a large longitudinal impedance in the range of 628-630 MHz in the SPS
cavities.
Three different types of HOM couplers are used in the SPS
cavities for the damping of different HOM passbands. However, with a fixed
number of HOM couplers, the cells that require an HOM coupler have to be identified to
minimize the longitudinal impedance at the desired frequency range.
33-cell
Present HOM damping scheme (12 Couplers)
Suggested additional HOM couplers (6 Couplers)

## Slide 15: 200 MHz - SPS Cavities
SPS 33-cell-cavities (simulations by S. Zadeh, Rostock)
  Goal: minimize impedance peak at ~630MHz
  Determine optimal combination for the positions of coupler-cells
Convergence w.r.t. coupling modes
Optimized cell configurations
Notes: A different order of the HOM couplers of the three-section SPS cavity can reduce the HOM impedance peak by around 13% for 18 couplers and by around 30% for 12 couplers set-ups

## Slide 16: 200 MHz - SPS Cavities
SPS 44-cell-cavities (simulations by S. Zadeh, Rostock)
  16 x 630 MHz-couplers, 8 x fork couplers, 6 x loop couplers
  Reordering of the HOM couplers in the cavity can reduce the impedance peak by ~40%
fork coupler
Notes: A different order of the HOM couplers of the three-section SPS cavity can reduce the HOM impedance peak by around 13% for 18 couplers and by around 30% for 12 couplers set-ups

## Slide 17: Surface Roughness Modeling
Surface roughness impedance models
  1D-corrugations with regular shape (perfectly conducting)
  Thin dielectric layer model:
  The gradient model
Equivalent surface impedance for
height probability density function
2
Notes: A different order of the HOM couplers of the three-section SPS cavity can reduce the HOM impedance peak by around 13% for 18 couplers and by around 30% for 12 couplers set-ups

## Slide 18: Surface Roughness Modeling
Surface roughness impedance models
  Round pipe with rough wall (R = 3mm)
  Quasi-periodic model with S-Parameter coupling
h = 3.14μm
gz = 4.7μm
dz = 4.7μm
gφ = 4.7μm
dφ = 4.7μm
Notes: A different order of the HOM couplers of the three-section SPS cavity can reduce the HOM impedance peak by around 13% for 18 couplers and by around 30% for 12 couplers set-ups

## Slide 19: Surface Roughness Modeling
Surface roughness impedance models
  Round pipe with rough wall (R = 3mm)
  Quasi-periodic model with S-Parameter coupling
Notes: A different order of the HOM couplers of the three-section SPS cavity can reduce the HOM impedance peak by around 13% for 18 couplers and by around 30% for 12 couplers set-ups

## Slide 20
  Thank You for your attention

## Slide 21: Curved particle trajectories
E-XFEL BC0
Beam path
~6.5m
1st BC0 chicane:
Bending radius: 1m
Bending angle: 45○
Length: ~1.2m
Pipe dimensions: 100x50mm
smooth pipe assumption
Layout of BC0

## Slide 22: Curved particle trajectories
5GHz
10GHz
15GHz
extruded hex-mesh
num. convergence

## Slide 23
  Thank You for your attention