## Slide 1: LEIR extraction kickers impedance studies
N.Biancacci, L.C.Feliciano, L.Sermeus, C.Zannini
HSC meeting 30-11-2020

## Slide 2: Introduction
Complete list of known occurrences:
09/11/2018: elogbook link
07/08/2018: elogbook link
13/11/2018: elogbook link
15/11/2018: elogbook link
UNSTABLE
STABLE
Fast instabilities were observed in 2018 before RF capture.
Harmful during LHC run -> lengthened the ion beam setup time!

## Slide 3: Coherent motion
Beam looks horizontally unstable.
Doubles amplitude in ~ [~ 10k turns]
Damper was in operation
Capture
7 injections
Extraction

## Slide 4: Frequency content
Large amplitude from 10 to 20 MHz
HOM: MHz,
Not very reproducible, frequency seen to jitter

## Slide 5: Seek for a source…
Given the plane of instability, relatively low HOM frequency and low Q factor, we started to investigate the LEIR extraction kickers.
ER.KFH31 and ER.KFH32-34 are used in LEIR to extract the beam.
No CAD models available.
ER.KFH31
ER.KFH32-34

## Slide 6: Pictures KFH3234 (LEAR 1981)
Pictures scanned from negative (Dec. 1981) https://cds.cern.ch/record/754592

## Slide 7: KFH31 - KFH3234 CAD models
KFH31
KFH3234

## Slide 8: Ferrite material
Ferrite 8C11
Source:
https://www.ferroxcube.com/upload/media/product/file/MDS/8c11.pdf

## Slide 9: KFH31 Eigenmodes
Q factor
MHz

## Slide 10: Impedances
Wakefield simulations of kicker module do not show large transverse modes at the observed frequencies.
Longitudinal
Horizontal
Vertical
Kicker structure can sustain a quasi-TEM mode cable effect could play a role.
We tried also to include the effect of the cables with available information.
Due to kickers spacing
Notes: Add picture interconnection mode.

## Slide 11: Kicker with circuitry
Circuit model available in Design Report.
Pulse Formation Path made of parallel of saturating inductors and TL cables.
(characteristic cables impedance): 15.7
(saturating inductors): 10 series with = 10
(transmission cable length): ~24 m
(termination cable length): ~2.6 m
: kicker impedance
Transmission cables
Termination cables
Magnet

## Slide 12: Kicker with circuitry
Transmission cables
Termination cables
Circuit model available in Design Report.
Pulse Formation Path made of parallel of saturating inductors and TL cables.
(characteristic cables impedance): 15.7
(saturating inductors): 10 series with = 10
(transmission cable length): ~24 m
(termination cable length): ~2.6 m
: kicker impedance
Magnet

## Slide 13: Kicker impedance
P1
P2
Simulated the kicker impedance from P1 to P2
Magnet as series impedance approximation:
Inductive behavior up to ~20 MHz.
RF measurements between P1/P2 would help to cross-check the model!
with
/cell
= 170mm
= 66mm

## Slide 14: Transmission cables
Transmission cables
Saturating inductors show large load dominate response of transmission side
Transmission side studied for different load (short, match, open).
load

## Slide 15: Termination cables
Termination side is normally matched no issue.
Resonance with short: measurements recommended to benchmark the model
load
RC
filter
Termination side studied for different load (short, match, open).

## Slide 16: Kicker impedance with circuitry
Computed the effect of both transmission side () and termination side () with the approach of [1,2,3]:
[1] G. Nassibian and F. Sacherer, Nucl. Instrum. Methods159,21 (1979)
[2] D. Davino and H. Hahn, Phys. Rev. ST Accel. Beams6,012001 (2003)
[3] C.Zannini, G.Rumolo, V.G.Vaccaro, CERN-ATS-2012-134, Particle Accelerator Conference(IPAC’12) –May20-25, 2012, N. Orleans, USA
A large resonance at 20 MHz between transmission side () and magnet is generated.
Notes: Confronto con jOmegaL semplice. Ref -> Davino, hann, put both references.

## Slide 17: Kicker impedance with circuitry
Computed the effect of both transmission side () and termination side () with the approach of [1,2,3]:
[1] G. Nassibian and F. Sacherer, Nucl. Instrum. Methods159,21 (1979)
[2] D. Davino and H. Hahn, Phys. Rev. ST Accel. Beams6,012001 (2003)
[3] C.Zannini, G.Rumolo, V.G.Vaccaro, CERN-ATS-2012-134, Particle Accelerator Conference(IPAC’12) –May20-25, 2012, N. Orleans, USA
A large resonance at 20 MHz between transmission side () and magnet is generated.
Largely dependent on the saturating inductance value.
Notes: Confronto con jOmegaL semplice. Ref -> Davino, hann, put both references.

## Slide 18: Kicker impedance with circuitry
Computed the effect of both transmission side () and termination side () with the approach of [1,2,3]:
A large resonance at 20 MHz between transmission side () and magnet is generated.
Largely dependent on the saturating inductance value.
Negative impedance unphysical maybe related to the magnet approximation as a simple series impedance.
Benchmark with CST co-simulation wished/in progress.
[1] G. Nassibian and F. Sacherer, Nucl. Instrum. Methods159,21 (1979)
[2] D. Davino and H. Hahn, Phys. Rev. ST Accel. Beams6,012001 (2003)
[3] C.Zannini, G.Rumolo, V.G.Vaccaro, CERN-ATS-2012-134, Particle Accelerator Conference(IPAC’12) –May20-25, 2012, N. Orleans, USA
Notes: Confronto con jOmegaL semplice. Ref -> Davino, hann, put both references.

## Slide 19: Summary and conclusions
KFH31 and KFH3234 kickers were studied from the impedance and coupling to circuitry point of view.
Kicker CAD module made from drawings and pictures: might present several kind of approximations.
The kicker impedance related to core losses was computed no strong transverse resonance observed.
The kicker’s cables effect was computed a resonance at 20 MHz present:
  Some unphysical behavior of impedance may be related to the magnet approximation as a simple series impedance.
Next:
RF measurements on kicker and cables to be discussed/planned with experts.
CST co-simulation of kicker magnet + RF circuits.

## Slide 20: Appendix

## Slide 21: Original drawings
233mm
242.5mm
471mm
235.5mm

## Slide 22: Details on module spacing
471mm full length (235.5 half)
461mm plate-to-plate (230.5 half)
Module distance 7mm full module to middle
12 mm plate to middle
14 (24)mm

## Slide 23: Some references on kickers
M.Barnes “Injection and extraction magnets: kicker magnets ” CAS 2009: Specialised Course on Magnets, Bruges, 16-25 June 2009
L.Ducimetière, “Advances of transmission line magnets”, Proceedings of 2005 Particle Accelerator Conference, Knoxville, Tennessee.

## Slide 24: RF networks: series impedance
https://cds.cern.ch/record/1415639/files/p67.pdf

## Slide 25: KFH3234 front view

## Slide 26: A simplified kicker schematic
T.Kramer, “Kickers, Septa and Protection Elements”, CAS2018 https://indico.cern.ch/event/683936/contributions/2803312/attachments/1564570/2691879/Kickers_and_Septa_2018_CAS_ESI.pdf

## Slide 27: Kicker circuit model for impedance
https://journals.aps.org/prab/pdf/10.1103/PhysRevSTAB.6.012001