## Slide 1: SM18 TEST FACILITY shaping for HL-LHC and beyond in the last 10 years
M. Bajko TE-M SC-TF
1st of December 2020 for TE-MSC Seminar

## Slide 2: Abstarct
In this presentation I will show the strategy that was set up in 2009 for the modifications of the SM18 hall to fulfil the HL-LHC needs.
I will recall the main goals I proposed myself, in agreement with my line- and HL-LHC project-management, as a section leader of the magnet test stands.
I will show than the summary of the past 11 years accomplishments and give the status of the test facility today.
Before giving my own words on this great adventure that was the challenge of the SM18 test bench construction and the building of a great team of experts for its operation, I will tell you about the importance I payed for the communication in general, the exchange with experts at CERN and within the international community of people in the field.
I will finish my talk showing you my next challenge : the HL-LHC IT STRING that I am proposing to bring to success with a small, but very motivated team in the next coming (only few) years ? …once again in the SM18 ? shaping it even more!

## Slide 3: 2009
Project proposal August 2009
TE-MSC-TF is created with one of the main task of moving Block 4 from Prevessin to SM18

## Slide 4
Unify, Extend, Modify, Prepare = CONSTRUCTION
Optimize = OPITIMIZATION
(where cost, time and performance considerations are of equal level)
Service = to allow TESTING and OPEN SM18 to USERS
Man Power = TEAM BUILDING
The TE-MSC-TF mandate as I translated
THE TF SECTION OBJECTIVES
giving the best possible service
  making test with good, performing and smart equipment and obviously also in time
  Assuring the safety of the personnel and the equipment
  giving reliable feed back ( raw data, analyzed data , reports, planning ect) to the projects
work within international collaboration and become a reference in our field.

## Slide 5: FROM BLOCK4 to CLUSTER G
2009
TE-MSC-TF is created with one of the main task of moving Block 4 from Prevessin to SM18
2010
Start of civil engineering in the SM18 – Cluster G
2011
The new vertical test stand called Cluster G with the “LONG CRYOSTAT” is operational.
2012
2nd cryostat and the feed box are operational.
Start of optimisations: new insert for “Long Cryostat” and a new one for FReSCa2: HFM test stand idea is born.
A memorandum is written to ask for extension of the test stand to fulfil HL-LHC magnet test requirements on the cluster D and the SM18 Infrastructure Uprgade

## Slide 6: CLUSTER G extension with CLUSTER D
2014
In July Cluster D is dismounted, while the 3rd cryostat is operational in the cluster G.
2015
Start of civil engineering Cluster D, while we proved that Cluster A high current circuit can go up to 20 kA
2016
HFM cryostat ready for HL-LHC model magnets ; New demineralised water station, the new overhead crane became operational; new control room installed in August
2017
Cluster D ( but also G and A) is operational; ready for HL LHC magnet testing
Creation of the SM18 Infrastructure upgrade project.
Upgrade of the CERN Superconducting Magnet Test Facility
#28 Marta Bajko(CERN) et al. (Dec 2, 2016) Published in: IEEE Trans.Appl.Supercond. 27 (2017) 4, 9500307 Contribution to: ASC 2016

## Slide 7: CLUSTER F: extension of magnet stand for Sc link
2018
Secondary circuit of of HFM test stand with EE ( IGBT) installation done
2019
Diode cryostat modification for TRIM lead testing, reviewed interlock of Cluster G with 2 circuits
2020
Secondary circuit of Cluster D, participation to Demo2 installation
The idea of the SC link test stand on Cluster F is born…and we started to do a number of iterations
Creation of the functional specification for benches we plan major changes

## Slide 8: 2009
TE-MSC-TF is created with one of the main task of moving Block 4 from Prevessin to SM18
Project proposal August 2009

## Slide 9: 2010
Mars 2010
Avril 2010
May 2010
June 2010
July 2010
Civil engineering started in the SM18 Cluster G

## Slide 10: 2011
Block 4 operational in SM18
Block 4 on the road
Block 4 integration in SM18
The Cluster G with 1 cryostat fully operational

## Slide 11: 2012
Diode cryostat ready for test
Feed Box ready for FCM testing
2nd cryostat and the feed box are operational Start of optimisations: new insert for Long Cryostat and a new one for FReSCa2: HFM . A memorandum is written to ask for extension of the test stand of HL-LHC magnet

## Slide 12: 2013
Construction of the LN2 cryostat.
OPEN DAYS… we have external help: I can count on my daughter.. she is now 4, and with Tonio even under the rain is transporting magnets
We got our new offices
Special thanks to Hugo, Juan, Jorge, Maryline

## Slide 13: 2013-2014
Construction of the new Inserts for the old cryostats
While we kept the old Block 4 cryostats, we re-built the inserts. Ex. Diodes and LHC lead cryostats with an external satellite allowing us today to used a mixed gas to cool HTs coils at variable He gas temperature
Work of G. Villiger + V. Benda
New additional insert for the existing LONG cryostat with IMPROVED performance.
With an original idea of P. Viret
Design and produced by EN-MME design office and Main workshop
Integrated with CRG in the SM18 cooling system
SAFETY a continues work on a constantly growing installations
Work with E. Bigot + T. Otto + P. Viret

## Slide 14: 2014
In July Cluster D is dismounted. Creation of the SM18 Infrastructure UPG project. 3rd Cryostat is operational in the vertical test facility.

## Slide 15: 2015
June
July
September
October
November
December
18th of December
20 kA kept for 30 s in Cluster A. ….so is feasible ….
while work is ongoing for the civil engineering of Cluster D, we start testing Cluster A at high current

## Slide 16: 2016
Cluster A CL consolidation
New demineralised water station, Operational in April
the new overhead crane operational
new control room installed
HFM cryostat ready. Infrastructure improved

## Slide 17: 2017
Cluster G , D and A operational
And we enjoy EUCAS 2017 in SM18

## Slide 18: SM18 INFRASTRUCTURE UPGRADE
  DEMINERALISED WATER PRODUCTION: + 150 m3/h
  NEEDED FOR DEMINERALISED WATER ENTIRELY COMING FROM MAGNET OPERATION
  HANDLING: 25 T and longer rope
  NEEDED FOR OVERHEAD CRANE CHANGE ENTIRELY COMING FROM MAGNET OPERATION
  nCONTROL ROOM
  NEEDED TO EXTEND THE TOO SMALL CONTROL ROOM OF THE VERTICAL TEST FACILITY TO BE USED ALSO FOR HORIZONTAL BENCHES AND SC LINK
  PRIMARY WATER COOLING CAPACITY: +736 m3/h
  NEEDED FOR MAGNETS, CRYO AND RF
  POWERING FROM THE NETWORK: 3 MVA
  NEEDED FOR NEW OR MODIFIED PCs FOR MAGNETS AND IR STRING
  CRYOGENIC COOLING PRODUCTION: + 35 g/s LHe
  NEEDED ESSENTIALLY FOR THE RUNNING OF THE HL LHC IR STRING IN PARALLEL WITH MAGNET TESTING
The upgrade was driven by the recommendation to be able to carry out the full test programme withouth constraints
Operational from April 2016
Operational from 2019
Operational from February 2016
Operational from 2017
Is under final commissioning 2020

## Slide 19: SM18 handling infrastructure upgrade
  HANDLING: 25 t and longer rope
  NEEDS FOR OVERHEAD CRANE CHANGE ENTIRELLY COMING FROM MAGNET OPERATION
25 T HANDELING CAPACITY
To enable insertion of test objects into the HFM cryostat the operating height, had to be increased to 6 m (presently 5.3 m).
Cluster D, on the other hand, will be deeper than the existing vertical facilities. To handle the inserts the operation depth between the hook and the top of the cryostat must be increased to 9.3 m.
Operational from February 2016
Special thanks to Roberto R.

## Slide 20: SM18 electrical distribution infrastructure upgrade
To allow some flexibility and margin with new requests that are not formulated yet, the proposal is to INSTALL a TRANSFORMER OF 3 MVA CAPACITY
The new transformer will feed HL LHC IT STRING (Cluster J ) and the new Cluster F with the 20 kA power converter.
See document: https://edms.cern.ch/document/1604702.
Special thanks to Nuno D. S.

## Slide 21: New Control Room
  nCONTROL ROOM
  NEEDED TO EXTEND THE TOO SMALL CONTROL ROOM OF THE VERTICAL TEST FACILITY TO BE USED ALSO FOR HORIZONTAL BENCHES AND Sc link
OLD CONTROL ROOM WITH REDUCED SPACE
NEW LARGER CONTROL ROOM AT THE PROXIMITY OF THE CRYOSTATS
NEW CONTROL ROOM: THE GROUND FLOOR
Last adjustments before testing MQXFS5
Special thanks to Maryline Ch.

## Slide 22: SM18 CRIOGENIC infrastructure upgrade
Cold Compressor
WPU1
WPU2
Heater1
EuHIT
SC link tests
Feedbox
An additional 35 g/s liquefing capacity
The existing total pumping capacity in SM18 at 1.8 K is 12 g/s today that was obtained by combining the capacity of WPU1 and 2.
This 12 g/s is to be shared between magnet and cavity testing
  CRYOGENIC COOLING PRODUCTION: + 35 g/s LHe
  NEEDED FOR RUNNING IN PARALLEL MAGNET AND RF CAVITY WITH THE HL LHC IR STRING TESTING
Operational from April 2016
Should be operational from January 2021
“SM18 Cryogenics Infrastructure Upgrade Proposal”: EDMS 1571317
Special thanks to Antonio P.

## Slide 23
  DEMINERALISED WATER PRODUCTION: + 150 m3/h
  NEEDED FOR DEMINERALISED WATER ENTIRELY COMING FROM MAGNET operation
  PRIMARY WATER COOLING CAPACITY: +736 m3/h
  NEEDSED FOR MAGNETS, CRYO AND RF
SM18 water cooling infrastructure upgrade
Operational from 2019
See presentations of G. Cumer , A. J. Broche :https://indico.cern.ch/category/7651/
SFA18
Special thanks to Alexander J. B and Gerard C.

## Slide 24: Test stand for magnets ( in vertical cryostats)
Horizontal tests
CLUSTERS
Main entrance
A
B
C
E
F
Vertical tests
Cluster D
Vertical tests
Cluster G
Cryogenic
Magnets
All model magnets of (HL-)LHC and others can be tested in Cluster G or D
NO modification of the test stand is required. The cryostats are all operational; all ancillary equipment are present and adaptable to needs.
We can test 2 independent circuits both at high and low current.
We have 2 x 2 kA 4 Q PC on D with EE.
Cliq and symmetric quench detection operational.

## Slide 25: Test stand for HL-LHC : ongoing constructions
Interface the CFU with a new phase separator to allow 4.2 K testing conditions of the triplets and also D2.
Interface the the warm powering cables with the CL (replace the DCB with an adequate PP). Place order for WCC in time.
Interface the cryo infrastructure
https://indico.cern.ch/event/647714/timetable/#20171114.detailed

## Slide 26
Horizontal tests
CLUSTERS
Main entrance
A
B
C
E
F
Vertical tests
Cluster D
Vertical tests
Cluster G
Cryogenic
Magnetic measurements
Opticalfiber & diode Installation
Installation & storage
Magnets
Target : June 2021
Installations for WP3 cryo magnets: Q2a/b, (Q1,Q3)
Can be tested on cluster A and F
Modification of the test stand is required.
Strategy is to have two independent test bench fully equipped for Q2 type magnet testing. This implies modification of :
Electrical circuit
Cryogenic circuit
Handling
Interlocks
HORINZONTAL test | 
apertures | single
condutor technology | Nb3Sn
nominal/max current | 16 /20 kA
energy extraction | not possible
QH and CLIQ | possible
Energy | 10 MJ
handling | Modified Rocla
compatible CFU (LHC) | NO
The 2nd prototype will be tested on the cluster A with a modification on the cold mass instrumentation to insure the magnet testing at 4.2 K ( difficult for the 1st prototype). This will be done using the test cryostat.

## Slide 27: Testing WP6A: Sc Link system
Cluster G 20 kA
- 18 kA
 75 mm
+ 18 kA
62 kA
62 kA
3 2 kA (7 kA)
+ 13 kA
- 13 kA
Instrumentation wires
(twisted and cabled)
Including insulation
Protective insulation (outer layer)
Cluster F 20 kA,7 kA, 2kA, 0.6 kA, 0,12 kA
Should be tested on F2
Horizontal tests
CLUSTERS
Main entrance
A
B
C
E
F
Vertical tests
Cluster D
Vertical tests
Cluster G
Cryogenic
Magnetic measurements
Opticalfiber & diode Installation
Installation & storage
Magnets
Modification of the test stand is required.
This implies modification of :
Powering circuit ( major)
Cryogenic circuit ( minor)
Handling ( major)
Can be tested on cluster F

## Slide 28: Testing WP6a: Type test for CL
“The Feed Box” would be used for the high current lead test
Horizontal tests
CLUSTERS
Main entrance
A
B
C
E
F
Vertical tests
Cluster D
Vertical tests
Cluster G
Cryogenic
Magnetic measurements
Opticalfiber & diode Installation
Installation & storage
Magnets
Minor modification of the test is required.
Cryogenic circuit ( minor) with hopefully existing or already designed pieces
It is a test stand for type test , not implying extra charge for operation. Prototypes will be not tested here so it is not on the critical path.

## Slide 29
Testing WP6a: Type test for CL
Hopefully existing or already designed pieces:
a. in yellow all existing
b. in green CL
c. other to be designed

## Slide 30: The new distribution of test benches of SM18
Radio Frequency Cavities
Horizontal tests
CLUSTERS
Main entrance
A
B
C
E
F
Vertical tests
Cluster D
HTS Leads test
HL-LHC String test
Vertical tests
Cluster G
Cryogenic
LN2 test stand
Visitors
Cabling & electronics
Magnetic measurements
Opticalfiber & diode Installation
Installation & storage
Cryogenic
Mechanical
Workshop
Sc link system
Q1,Q2,Q3,CP
Q1,Q2,Q3,CD
Q1, Q3
D2
11T
MB, SS(SS), D1
MB, SS(SS), D1

## Slide 31
  Strain monitoring inside the coil
    Magnet powering to 15 kA @ 1.9 K
Minimum Quench Energy test on an HTS sample carried out in SULTAN test facility in Paul Scherrer Institut in the framework of CERN-MIT collaboration
Work of Antonella and Juan Carlos
  Quench detection in HTs sample in SULTAN
Work of Bernardo and Erica ( MIT)
The TF R&D. Optical fiber based sensing at Low Temperature
Article copyright is: SUST-104163.R1

## Slide 32
1st access granted 20th of November 2013
…to develop a non intrusive technology based on FOS for strain and temperature monitoring in the new generation of superconducting magnet and cryogenic devices…
Collaborations. Eucard2 and ARIES Trans National Access
EUCARD2
The objectives foreseen for MagNet WP9 were to deliver at least 1,920 access units (hours) to an estimated number of 64 users from 8 projects.
  University of Sannio (IT)
  University of Napoli, Federico II (IT)
  University of Padova (IT)
  University of Debrecen (HU)
  Institute of Polymers, Composites and Biomedical materials (IT)
The MagNet TNA at CERN provided access to 34 users from 15 different institutes, for a total of 2,660 access units of 9 projects, exceeding the initial requirement of 1,920 units.

## Slide 33: Collaborations International Workshops on Superconducting Magnet Test Facilities
Chart: The 65 registered PARTICIPANTS
| USA | J | CH | PL | FR | IT | S | DE
 | 8 | 3 | 37 | 3 | 4 | 2 | 4 | 2
Most of these participants has a valuable long experience and expertise
in superconducting magnet testing

## Slide 34
@ GENEVA CERN
https://indico.cern.ch/event/507584/
@ BNL LONG ISLAND
https://www.bnl.gov/mts2018/
There is a large international community that I “bridged” through (till now) these workshops
https://aries.web.cern.ch/content/application-and-follow-procedures
Thanks Virginia, Joe and Kevin for the help in organization

## Slide 35
Man Power = TEAM BUILDING
The TF section was the smallest section in the TE-MSC group!

## Slide 36
https://www.weka.ch/themes/competences-personnelles/gestion-de-soi/gestion-de-soi/article/modele-de-liceberg-comment-communiquons-nous-en-tant-quindividus/
Man Power = TEAM BUILDING
But we had a “non mandated extension” of the section!!!
They played a key role in the construction and/or the operation of the test stands.
Many thanks to them for their valuable help, flexibility and availability!
The TF section was the smallest section in the TE-MSC group!
H. Prin
J.C. Perez
F. Pincot
N. Bourcey
L. Fiscarelli
C. Petrone
S. Yamine
P. Perret

## Slide 37: The ACTORS of the bench construction
CFU TE-CRG
CRYO-magnet TE-MSC
Cryogenic cooling Cluster F Q2a
Power distribution Cluster F(E)
PC TE-EPC
WCC EN-EL
WC EN-CV
EE TE-MPE
CC EN-EL
Powering circuits
Cryo Cooling
TE-EPC
TE-MPE
EN-EL
EN-CV
TE-MSC
TE-CRG
EN-MME
Handling
TE-MSC
EN-HH
Satefy and Interlock
TE-MSC
BE-ICS
Daq and Software
EN-SMM
TE-MSC
Integration/Planning
EN-ACE
Measuring systems
TE-MSC
EN-MME
The main actors

## Slide 38: EN-MME with TE-MSC and TE-CRG
Design Office and Main Workshop EN-MME
From 3D design
Checking the existing, the needed
Making fabrication drawings for ordering at main workshop
Robin, Philippe
Herve, Gaelle
Gabriella, Olivier

## Slide 39: TE-CRG and EN-ACE
I think is no doubt that this group is the major partner of the SM18 magnet test bench construction and operation.
I will therefor give one example relevant for the UPG and operation together but there are examples of the bench modifications in the annex slides aswel.
Chart: LHe Consumption: estimates based on planning made 5 years ago for the UPG
Chart: VLP Consumption: estimates based on planning made 5 years ago for the UPG
LHe estimate based on last the last week activity coordination work by ( N. Guillotin)
LHe estimate based on last the last week activity coordination work by ( N. Guillotin)
These estimates are based on a full Ms Project based on HL-LHC Master Plan, but not only: including RF and Magnets and R&D + LHC needs. Test are pre-distributed on benches and benches are characterized by its consumptions estimated together with CRG.
Ex. Cluster D planning
Nicolas G. + Estrella V.

## Slide 40: TE-EPC
An other key partner:
Cluster A PC UPG to 20kA!!! Saving !!!
Cluster F 20kA PC already operational! And all PC in SM18…. And even more important: we had an excellent and online (onsite) support of expert!!!!
Samer Y

## Slide 41: TE-MPE
Magnet Protection and Energy Extraction: plans for needs in SM18
This is not the complete picture, but an example of a graphical example of an agreement of what we need and requested from MPE in time. We have EE and dump, QDS aswel.
… as in other cases: we have their experts with us for the constructions and operation!!!!
Felix + Gert

## Slide 42: TE-MSC and EN-SMM
Data Analysis with DIADEM
DAQ SPECIFIED PARAMETERS
Input channels: +/- 10 V analog
Nr of HF channels: 200 differential
HF frequency: 200 kHz
HF,MF,LF resolution: 16 bit resolution
HF,MF,LF accuracy: 1mV
MF frequency: 50 kHz
Nr of LF channels: 144
LF frequency: 1kHz
Timing: GMT synchronization
Example of HF system
Specification in 2016 for Cluster D
Hubert and Maryline

## Slide 43
https://www.weka.ch/themes/competences-personnelles/gestion-de-soi/gestion-de-soi/article/modele-de-liceberg-comment-communiquons-nous-en-tant-quindividus/
Man Power = TEAM BUILDING
But we had a “non mandated extension” of the section!!!
They played a key role in the construction and/or the operation of the test stands.
Many thanks to them for their valuable help, flexibility and availability!
The TF section was the smallest section in the TE-MSC group!
H. Prin
J.C. Perez
F. Pincot
N. Bourcey
L. Fiscarelli
C. Petrone
J. Fleiter
P. Perret
V. Parma, A.v.Craen , S. Yammine, H. Thiessen, A. Perin, V. Benda, O. Pirotte, G. Rolando, N. Guillotin, A. Kosmicki, R. Betemps, R. Ferrier, G. J. Coeling, F. R. Mateos, T. Otto , N. Dos Santos, R. Rinaldesi , E. Paulat, E. Bigot, E. Vergara, V. Mertens, F. Formenti, G. Cumer, L. Serio, V. Benda, A. Lee, M. Struik, S. Gianelli, P. Moyret, M. Strychalski, C. Gonzalves Perez, G.J. Coelingh, K. Dahlerup-Petersen, A. Dinius,V. Maire, A. J. Broche, R. Rinaldesi, R. F. Ortega, H. Reymond, M. I. Tapani, F. Gomez de la Cruz, C. Arregui, H. Botella, R. Morton, E. Perez Duenas, L. van den Boogaard
Many thanks to all our collaborators in the different sections, groups, departments; together we did and we will continue shaping the SM18 hall

## Slide 44: Measurements in the SM18: training?

## Slide 45
Chart: What we have done
| 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020
Vertical | 17 | 14 | 14 | 24 | 29 | 32 | 17
Horizontal | 8 | 9 | 11 | 10 | 9 | 9 | 11
Sc link or Other | 2 | 5 | 1 | 0 | 1 | 2 | 4
Chart: What we have expecetd in 2014
| 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020
horizontal benches | 9 | 20 | 7 | 3 | 10 | 18 | 18
vertical benches | 22 | 12 | 16
Sc link | 2 | 7 | 6 | 4 | 4 | 3 | 3
A part of the message that the test stand capacity is larger than expected, here I wish to say that we are also producing a lot of data, measurements, test results, reports and publications!!!
Service = to allow TESTING and OPEN SM18 to USERS
….and smiles!!!

## Slide 46: The core of the TE-MSC-TF section
Chart: TE-MSC-TF SECTION
| FELL | DOCT | TRNE | COAS | STAFF
 | 3 | 1 | 1 | 1 | 10
Chart: STAFF
| cat 2 | cat3
 | 3 | 7
Apart 2 staff members I have participated to hire all Staff, MPA and M4P of the section. We have trained people for FNAL, GSI, PSI (2) and of course for CERN. I thank you for all of YOU being so good COLLEAGUES AND COLLABORATORS.
We are today about 25 max 28 including M4P and MPA from which 10 STAFF members.
as in 2016
A big thank for the members of the TF section : Christian, Hugo, Gerard, Franco, Antonella, Michal S., Vincent R., Patrick, Jerome, Gaelle, Olivier, Mary, Guillaum, Vincent J.D., Bernardo, Jose, Sara, Ioannis, Daniel T., Salvador, Yacine, Fred R, Fred F, Raphael, Abdelhay, Bertrand, Yannick,Ruben, Gyopar, Jean-Luc, Clinton;

## Slide 47
The data is only produced because we get the magnets done by the others!
The data is produced because the others needs them to understand the magnets they designed!
The data we produced to help the understanding the magnets behaviour.
The data is produced thanks to our work!
The data produced is valuable only if is analysed and published!
The analysed data can only be understood if we understand how it was produced.
The data can only be understood if we can correctly corelate with the magnet design.
The data can be used only if is validated.
What is the role of TF ?
Who is the owner of the data? Who should analyse, report , publish ect.
THERE IS NO UNIQUE ANSWARE FOR THIS, but a continues willing to look for a correct attitude and balance between teams.
You can only make as well as you can measure
By Joseph Withworth,
When finally the data is analyzed, reported, published by the magnet designer, builder and not by you, think that your role was to make it possible to measure their magnet and this was crucial!!!

## Slide 48
After one year of measuring the 1st Nb3Sn magnet (the TQ) at CERN, in the old Block 4, and doing the LHC HWC, Lucio and Fredy to give me the challenge to merge Block 4 and SM18. If I have to summarise, it was:
  an honour to participate to this adventure and BE ONE OF THE MAJOR ACTORS of the shaping of the SM18 in these last 10 years.
  a pleasure to work with a great team ( remember the iceberg slide)
  a satisfaction to see how the SM18 hall get transformed for HL-LHC need during theses last years
I thank my line management: Lucio, Luca, Miguel and Volker for giving me this chance to participate to this work and to guide me during these years . Thank Ezio (WP3), Frederic (WP11) and Amalia(WP6a) for their collaboration.
I wish to those stepping behind me success and satisfaction in completing the remaining work for HL-LHC test benches and operation. I hope they will have also the chance to shape further the test benches for new projects and leave their own footprint in SM18!

## Slide 49
The HL-LHC IT STRING SCOPE
The scope of the WP16 IT STRING is to represent, as far as reasonably achievable in a surface, the various operation modes to STUDY and VALIDATE the COLLECTIVE BEHAVIOURE of the different systems of the IT zone of the HL-LHC (magnets, magnet protection, cryogenics for magnets and superconducting link, magnet powering, vacuum, alignment, interconnections between magnets and superconducting link). Ref. HL-LHC IT STRING Scope https://edms.cern.ch/document/1693312/1
A.Kosmicki_20201001_edms 1582348

## Slide 50
The next steps for me : HL LHC IT STRING
As from 1st of January 2021, I will dedicate my time fully to the HL-LHC IT STRING not only as co-WP16 leader of the HL-LHC project, but also as the section leader of the a new, small, but extremely motivated TE-MPE-SF section with the help of many other collogues of different groups and departments and continue shaping SM18!
TE-MPE-SF
Marta Bajko SL
Samer Yammine
Davide Bozzini
Nicolas Heredia Garcia
Julian Zawilinski

## Slide 51
Thank you for your attention