## Slide 1: IBS and cooling in RHIC, HE-LHC active emittance control W. Fischer and M. Blaskiewicz
14 Jan 2010
15 October 2010
High-Energy LHC, Malta
1st vertical stochastic cooling in RHIC
Notes: Friday 10/15/2010, 10:30-10:50, 15 min talk, 15 slides

## Slide 2: Content
LHC active emittance control − HE LHC damping times − Maximization of integrated luminosity
IBS and cooling in RHIC − Measurements and simulations for IBS − Au79+ beam dynamics with stochastic cooling

## Slide 3: High Energy LHC parameters (from F. Zimmermann)
 | Nominal LHC | High energy HE-LHC | 
beam energy [TeV] | 7 | 16.5 | 
peak luminosity [1034 cm-2s-1] | 1.0 | 2.0 | 
luminosity lifetime [h] | 23 | 13 | 
events per crossing | 19 | 76 | 
# bunches / beam | 2808 | 1404 | 
bunch population [1011] | 1.15 | 1.3 | 
Luminosity leveling | no | yes: ex,y | 
initial transverse normalized emittance [mm] | 3.75 | 3.75 (x) 1.84 (y) | 2.59
number of IPs contributing to tune shift | 3 | 2 | 
maximum total beam-beam tune shift | 0.01 | 0.01 | 
IP beta function [m] | 0.55 | 1.0 (x), 0.43 (y) | 0.6
full crossing angle [mrad] | 285 (9.5 sx,y) | ~180 (12 sx0) | 
longitudinal SR emittance damping time [h] | 12.9 | 0.98 | 
horizontal SR emittance damping time [h] | 25.8 | 1.97 | 
initial long. IBS emittance rise time [h] | 61 | 64 | 
initial hor. IBS emittance rise time [h] | 80 | 80 | 
initial ver. IBS emittance rise time [h], (k=0.2) | ~400 | ~400 | 
[R. Assmann et al, “First thoughts on a higher energy LHC”, CERN-ATS-2010-177]

## Slide 4: Means of active emittance control during stores
Assume that initial beam parameters have been adjusted to acceptable values.
Adjust strength of active cooling (currently not an option in LHC) change of gain, power, average “system on” time changes equilibrium emittance
Increase transverse emittance random dipole kicks q [M. Syphers, Handbook]
Use x-y coupling to equalize transverse emittances when operating at beam-beam limit, maintains same bb parameter in both planes works well in RHIC without and with active cooling
Increase bunch length to reduce peak currents random phase kicks dj [M. Syphers, Handbook]

## Slide 5: HE LHC emittances without and with heating
Courtesy of O. Dominiguez, F. Zimmermann, in CERN-ATS-2010-177.
Heating condition: x = 0.01 (constant)
Constant crossing angle q ~ 180 mrad.

## Slide 6: HE LHC emittance without and with heating
Heating determined by: x = 0.01 (constant)
Same luminosity with round and flat beams.
Courtesy of O. Dominiguez, F. Zimmermann, in CERN-ATS-2010-177.

## Slide 7: HE LHC luminosity with round beams
fc collision frequency g Lorentz factor
r0 classical proton radius N bunch intensity (N1=N2=N)
x beam-beam parameter b* envelope function at IP
F correction factor for hourglass and crossing angle q
Larger beam-beam parameter x allows for larger luminosity, or smaller N (and stored energy) for same luminosity
Assumed beam-beam parameter (xtot = 0.01) is conservative, smaller than SppS, Tevatron, RHIC
May be increased beyond 0.01 (and even further with electron lenses)
evolution without heating, max = 0.02, . (max = 0.035 for flat beams, ) 
Courtesy of O. Domininguez, F. Zimmermann in CERN-ATS-2010-177.

## Slide 8: 2 Tevatron electron lenses in operation (not operationally used for HOBBC). 2 RHIC electron lenses for head-on BB compensation under construction.
Drift tube 3
Solenoid GS1
Electron gun
Superconducting magnet
Electron collector
Drift tube 3
Solenoid GS2
Solenoid GSB
Solenoid CSB
Solenoid CS2
Solenoid CS1
Electron beam volume
Drift tube 4
BPM
Drift tube 1
Vacuum system
BPM
Drift tube 5
Drift tube 9
Drift tube 10
Electron collector
Drift tube 7
Drift tube 8
Drift tube 6
Drift tube 2
Electron gun
2x Ion Pump
Cryopump
Gate valve
Gate valve
Ceramic HV break
Ion pumps
RHIC electron lens

## Slide 9
2 superconducting 3.8 km rings
2 large experiments
100 GeV/nucleon Au
250 GeV polarized protons
Performance defined by
1. Luminosity L
2. Proton polarization P
3. Versatility Au-Au, d-Au, Cu-Cu, polarized p-p (so far) 12 different energies (so far)
Relativistic Heavy Ion Collider 1 of 2 ion colliders, only polarized p-p collider

## Slide 10: Intrabeam scattering in RHIC
IBS leads to debunching and transverse emittance growth of heavy ion beams
without cooling
Comparison of measured and simulated e(t) and ss(t) [A. Fedotov et al., proceedings HB2008.]
Emittance
bunch length
Beam: Au79+,100 GeV/nucleon, 95 deg/cell, Nb=0.92x109 Simulation: BETACOOL
Sim: 82 deg/cell
Sim: 95 deg/cell
Exp: 95 deg/cell

## Slide 11: RHIC – 3D stochastic cooling for heavy ions
M. Brennan, M. Blaskiewicz, F. Severino, Phys. Rev. Lett. 100 174803 (2008); PRST-AB, PAC, EPAC
longitudinal kicker (closed)
horizontal kicker (open)
horizontal and vertical pickups
longitudinal pickup
5-9 GHz, cooling times ~1 h
vertical kicker (closed)
Y h+v pickups
B h+v kickers
B h+v pickups
Y h+v kickers
Notes: Frequency range: 5-8 GHz transverse, 6-9 GHz longitudinal

## Slide 12: RHIC – bunched beam stochastic cooling for heavy ions
Longitudinal cooling since 2007
First transverse (vertical) cooling in 2010
14 Jan 2010
M. Brennan M. Blaskiewicz K. Mernick et al.
So far stochastic cooling increased average store luminosity by factor 2
Expect another factor 2 with full 3D cooling
Issues being addressed:
Vacuum leaks at feedthroughs
Mechanical motion of long. kickers
Cross-talk between Blue and Yellow vertical system (addressed by 100 MHz shift in Blue)
Construction, installation, and commissioning of horizontal systems

## Slide 13: RHIC Au beams with vertical stochastic cooling
[M. Blaskiewicz, J.M. Brennan, and K. Mernick, PRL 105, 094801 (2010).]
Blue emittances without vertical cooling
Yellow emittances with vertical cooling
Emittance measurement with Ionization Profile Monitor (IPM).

## Slide 14: Cooling only one beam
Because of Blue-Yellow cross talk of vertical cooling systems in 2010, only one beam could be cooled at the time. Loss rate of other beam increased as a result (from unmatched beam sizes at the IP).
HE LHC: Adjust heating to maintain same emittances in both beams. (Known effect from SppS, HERA, RHIC.)
B on
B on
B on
B on
Y on
Y on
Y on
Y on
Y on
Initial beam-beam parameter x ~ 0.002/IP (2 IPs)

## Slide 15: RHIC store evolution with 3D stochastic cooling
Simulation by M. Blaskiewicz
Longitudinal profiles with h1 = 360 (360 kV) and h2 = 7x360 (4 MV)
Simulations have matched observable cases so far.
0 35 70 time [ns]
0
6
current [A]
beginning of store after rebucketing
after 5 h in store
Au beam with Nb = 0.5x109 Nb = 1.0x109 Nb = 1.5x109
Notes: Simulation with nominal noise (estimated from 0.2 mm beam offset at pick-up).

## Slide 16: RHIC store evolution with 3D stochastic cooling
Simulation by M. Blaskiewicz
rms emittance [mm mrad]
0
0 5 time in store [h]
Au beam with Nb = 0.5x109 Nb = 1.0x109 Nb = 1.5x109
total beam-beam parameters (2 IPs) DQ = 0.0015 DQ = 0.0030 DQ = 0.0046
Expect ~3x larger DQ with 56 MHz SRF (under construction)
Then closer to LHC.
1
2
3
DQ = 0.0009 DQ = 0.0019 DQ = 0.0029

## Slide 17: Summary
LHC
LHC damping times of 1h (long.) and 2h (transv.) much shorter than IBS growth times (>50h)
Heating required to maintain constant beam-beam parameter x ~ 0.01 (increase in x allows for more luminosity or a reduction in intensity)
RHIC
Observations and simulations of IBS induced emittance growth generally agree well, evolution of with stochastic cooling predictable.
With cooled Au beams not yet operating at beam-beam limit (need new 56 MHz SRF to reduce debunching, >= 2013)
Even at relatively small beam-beam parameters, equal cooling in both beams (= equal heating in HE LHC) is necessary to maintain good beam lifetimes