## Slide 1
R. Capote, A. Trkov, M.T. Pigni, G. Noguere, D. Bernard,
J. Malec, O. Cabellos on behalf of the INDEN collaboration
https://www-nds.iaea.org/INDEN
Update of the U238 (and Pu239) RRR to
improve burnup and lattice criticality

## Slide 2
U-238 changes, validation and comments
Pu-239 changes, validation and outlook
Outlook

## Slide 3
U-238 new INDEN evaluation (post-B8b1)

## Slide 4
Loss of reactivity with burnup for
PWR with ENDF/B-VIII.0 library
compared to ENDF/B-VII.1
Reported by Kang Seong Kim at CSEWG 2019
Extensive analysis by Kang Seong Kim and William A. Wieselquist in J. Nucl.Eng. 2021,2, pinpointing the problem to U-238
  Criticality prediction of U-238 was benchmarked
  extensively – small differences overall
  Problems appear with burnup:
    FP yields library unchanged from ENDF/B-VII.1
    Major FP cross section not so different
    Focus on Pu-239 production
INTRODUCTION
Monte Carlo code Serpent was used
(at least for validation)

## Slide 5
Depletion vs criticality: Reactivity rates in VERA
Kang Seog Kim et al, CSWEG2019
INDEN u238_e80V02 (B81beta1) practically eliminates the ENDF/B-VIII.0 trend with burnup, but reduces criticality at BOC by 250pcm.
Kang Seog Kim calculations, 2022, priv. comm.

## Slide 6
Cumulative U-238 capture reaction rate integral in a PWR spectrum
Thermal part of the spectrum in a PWR is suppressed due to boron in the coolant, emphasizing the importance of the epithermal energy range.
Importance of the resonance range up to 200eV emphasized by D. Bernard and O. Cabellos at the INDEN IAEA TM (Nov. 2021)
Cumulative reaction rate integral ratio of U-238 capture (at infinite dilution) between ENDF/B-VIII.0 (label “e80”) and “e80V02” (with resolved resonance data substituted from ENDF/B-VII.1) increases up to ~200 eV, except at the 6eV resonance.
The opposite effect of the 6eV resonance diminishes when self-shielding is considered

## Slide 7
nds.iaea.org/INDEN/data/u238e80V02_ENDF.zip (B81beta1)
The ENDF/B-VIII.0 RRR is replaced by ENDF/B-VII.1 RRR evaluation (fission background in URR preserved). This update increases the calculated criticality at high burnup (due to higher Pu-239 accumulation)
INDEN workgroup did not reach a consensus on this issue. It is to be evaluated whether this change is worth taking considering the lack of direct experimental evidence.
Overview of INDEN U238 file V02

## Slide 8
Legacy LANL assemblies: validation
@LANL, calculated by S.Kahler & N. Kleedtke miniCSWEG 2023
BigTen lowish !

## Slide 9
Lattice criticality: LCT006 representative
@LANL, calculated by S.Kahler & N. Kleedtke miniCSWEG 2023

## Slide 10
INDEN e80V03i4 @ https://www-nds.iaea.org/INDEN/data/u238e80u8V03i4_ENDF.zip
The ENDF/B-VIII.0 RRR is replaced by JENDL-5 RRR evaluation
This update preserves the ENDF/B-VIII.0 BOC criticality but eliminates the U-238 linked depletion trend at high burnup (due to higher Pu239 accumulation).
A new U-238 nubar evaluation was produced by LANL colleagues (Neudecker et al). Nubar was tweaked to better reproduce Jemima trend (tweaked  change of mean values within uncertainties)
Summary: INDEN e80V03i4 evaluation
Update of the ENDF/B-VIII.0 evaluation (IAEA CIELO)

## Slide 11
INDEN e80V03i4 adopted JENDL-5 RRR changes
O. Iwamoto et al, JNST (Japan) 60 (2023) 1-60, JENDL-5 paper

## Slide 12
=INDEN U238 (post b1)
=U238 B8
Uses U238 from B8
INDEN e80V03i4: Depletion studies
JEF-DOC-2239, M. Astigarraga @JEFF meeting 04/2023

## Slide 13
INDEN e80V03i4: Depletion studies
JEF-DOC-2239, M. Astigarraga @JEFF meeting 04/2023

## Slide 14
U-238 e80V03i4 nubar dependence
Convergence between JEFF & JENDL & INDEN evaluations observed
INDEN latest : u238e80u8V03i4
u238e80u8V03i4 | (recommended) RRR evaluation taken from JENDL-5, u238 nubar from LANL-INDEN collaboration

## Slide 15
Lattice criticality: LCT006 representative
@LANL, calculated by S.Kahler & N. Kleedtke miniCSWEG 2023

## Slide 16
Legacy LANL assemblies: validation
@LANL, calculated by S.Kahler & N. Kleedtke miniCSWEG 2023

## Slide 17
Pu-239 evaluations
JEFF-4T – Noguere et al
ENDF/B-VIII.1 – ORNL/IAEA collaboration
Similar approaches, underlying data and validation discussed at INDEN meetings

## Slide 18: New integral constraints for RP fit fissile targets
Duran et al, 2021 (submitted to NDS)
Discussed at INDEN CM November 2021
Good consistency with TNC
(slightly lower)
Similar to libraries !!
Derived f(th)
Duran et al TNC
533.0(0.7) 533.0(2.2)
586.1(2.6) 587.3(1.4)
751.0(1.9) 752.4(2.2)
1019(3) 1024(11)
All measured ToF
high-resolution data
(1955-2019)

## Slide 19: New integral constraints for RP fit fissile targets
Duran et al, 2021 (submitted to NDS)
Discussed at INDEN CM November 2021
All measured ToF
high-resolution data
(1955-2019)
used to derive:
I1, I3, I3 /I1, f(th)/I1
May require small revision of
RP fits for all fissiles
Derived f(th) consistent with TNC

## Slide 20: 239Pu RTC-MISTRAL2 experiment, CEA
239Pu ( E)
Modifications to the RR fit required:
subthermal ,   till 1eV (closer to B8)
To improve RTC and  crit. @ high burnup
NOTE: In the light of latest U-238, we have to solve Pu239!
Presented by G. Noguere @ INDEN meet.
Pu-239 INDEN 2021
(=B81beta1)

## Slide 21
 | Bu[GWd/tU] | 0 | 0.925 | 5.3 | 30.3 | 60.3
 | Case | Delta_Rho |  |  |  | 
endfb8_orig(average) | Case 14-5 | 42 | -1 | -14 | 97 | 41
endfb8+P9(run 6) | Case 15-14 | 0 | -26 | -33 | -476 | -688
endfb8+U8e71(run 7) | Case 16-14 | -181 | -149 | -84 | -184 | 1
endfb71(run8) | Case 17-14 | 79 | 115 | 158 | -35 | 318
endfb8_orig(average) | Original OpenMC library based on ENDF/B-VIII.0 data |  |  | 
endfb8+P9(run 6) | Original endfb8+ INDEN Pu239 |  |  | 
endfb8+U8e71(run 7) | Original endfb8+U238 from ENDF/B-VII.1 |  |  | 
endfb71(run8) | Pure endfb71 |  |  | 
Burnup dependence (Pu-239 INDEN 2021)
OpenMC calculations by J. Malec & A. Trkov
Depletion studies

## Slide 22: New INDEN 239Pu file (Pu9 Vc), May 2023
Board learning
TNC

## Slide 23: New INDEN 239Pu file (Pu9 Vc), May 2023
INDEN 239Pu file labelled ENDF/B-VIII.1
@EPFL/CEA, M. Hursin, provided by G. Noguere
@50GWd/t CONVERGENCE !
Pu9Vc (B81) +400pcm gain
JEFF-4T similar

## Slide 24: New INDEN 239Pu file (Pu9 Vc), nubar

## Slide 25: 239Pu RTC-MISTRAL2 experiment, CEA
239Pu ( E)
Modifications to the RR fit done, B8 bound states adopted:
subthermal ,   till 1eV (closer to B8)
G. Noguere (priv.comm.): Pu9 production is acceptable (-0.7% JEFF-311)
Presented by G. Noguere @ INDEN meet.
239Pu Vc ~ -0.8 pcm/K

## Slide 26: INDEN 239Pu in PST034 benchmark (Gd)
e811
INDEN - post1
jeff33
more thermal spectrum (less Gd)

## Slide 27: INDEN 239Pu in PST034 benchmark (Gd)
e811
INDEN –
post1
JEFF-33
more thermal spectrum (less Gd)

## Slide 28: INDEN 239Pu in WPEC-SG34 benchmarks
e811
INDEN –
post1
JEFF-33
more thermal spectrum (ATLF)
PST
Very low leakage high leakage

## Slide 29: INDEN 239Pu in WPEC-SG34 benchmarks
e811
INDEN –
post1
JEFF-33
more thermal spectrum (ATLF)
PST
Very low leakage high leakage

## Slide 30: INDEN 239Pu in depletion studies
Pu9 Vc
+Pu241
Pu9 1
PWR 3x3 cell
4.75% U5
criticality
decreases
@50GWd/thm
Pu9Vc ~-300pcm
+Pu241 ~-100pcm

## Slide 31: INDEN Summary @nds.iaea.org/INDEN/
Pu-239 INDEN (B8b1) evaluation is shown to decrease criticality at
60GWD/tU by ~ -600pcm.
A similar effect is seen in JEFF-4T2.
A solution much closer to B/VII.1 achieved (Pu239 Vc).
Recommended to be updated in B81b3.
Changes to Pu-240/241 from JEFF-4T2 highly desirable
Similar updated possible in JEFF4Tx.
U-238 (https://www-nds.iaea.org/INDEN/data/u238e80u8V03i4_ENDF.zip)
Latest U-238 iteration with modified nubar and JENDL-5 RRR.
(loss of criticality at high burnup solved, lattice criticality increased).
Recommended to be updated in B81b3.
Similar updated possible in JEFF4Tx.