## Slide 1: Proposal for a new central + RB24 beampipe in ALICE in LS3
Corrado Gargiulo (EP-DT), Werner Riegler (EP-AIO), Arturo Tauro (EP-AIO)
TREX 10/12/2020

## Slide 2: ALICE layout
Central beampipe
RB24 beampipe
Central beampipe
RB24 beampipe

## Slide 3: The new RUN3 central beampipe
Installed in October 2020
Central Be section 870mm long
ID 36.4mm (inner radius 18.2mm), thickness 0.8mm
Mechanical adjustment precision better than 0.2mm

## Slide 4: Installation layout
MFT/FIT-C
ITS-OB
Cage
RB24
Central beampipe
Bellow
ITS-IB
ALICE Layout RUN3

## Slide 5: ALICE Layout RUN3
FIT-A
Compensator Magnet
Ion pump
Central beam pipe
(ID 36.4)
Gate Valve
RB24
(ID 80)
ITS2
MF/FIT-C

## Slide 6: Mechanical adjustment: <0.2mm precision
C1
C2
C3
C1
C2
C3
C2
C3
C1
C1
Adjusting device | 
Registered Torque average | 0.7 Nm
Registered Torque Max | 1.54 Nm
Standard Torque M5 | 6 Nm
Per screw turn | 0.2mm
Total adjusting capability | +/- 4mm

## Slide 7: The ALICE LS3 upgrade
Novel vertex detector (ITS3) consisting of curved wafer-scale ultra-thin silicon sensors arranged in perfectly cylindrical layers, featuring an unprecedented low material budget of 0.05 % X0 per layer, with the innermost layer positioned at only 18 mm radial distance from the interaction point.
New Forward Calorimeter (FoCal), located at 7m left from IP2 and requiring low material budget in 3 < η < 6.
ITS3

## Slide 8: Central beampipe layout: RUN4
Smaller central Be part: ID 32mm (inner radius 16mm)
Thinner wall of the Be part: 0.5mm
Conical A-side Al or Be section
No gate valve
IP
820
500 Beryllium
ID32 wt 0.5
4838
ID 58; wt 1
ID 31.4 wt 1
Angle ~0.34°/Ø wt 1
250
RUN4
(Aluminum or Beryllium)
(Aluminum)
Dimensions in mm

## Slide 9: Central beampipe layout: RUN3 vs RUN4
ID 48.4, wt 1
OD 60
OD152
674
RUN3
IP
(Aluminum)
4680
820
870 Beryllium
Dimensions in mm
ID 36.4 wt 0.8
IP
820
500 Beryllium
ID32 wt 0.5
4838
ID58, wt 1
ID31.4 wt 1
Angle ~0.34°/Ø wt 1
250
RUN4
(Aluminum or Beryllium)
(Aluminum)

## Slide 10: RB24 beampipe layout: RUN3 vs RUN4
Dimensions in mm
RUN3
RUN4
~1080
Gate valve
FoCal
Central pipe
RB24 pipe
IP2
Comp.magnet
No change wrt RUN3
Only this section is modified

## Slide 11: RB24 beampipe layout: RUN3 vs RUN4
RUN3
4030
ID80; wt 2
Copper pipe
3635
Dimensions in mm
RUN4
Aluminum flange
Aluminum bellows
ID 58; wt 1
UHV CF Bi-metallic flange DN100
Aluminum
3872.5
IP 4838
IP 4680

## Slide 12: ALICE Layout RUN4
FOCAL
FIT-A
Compensator Magnet
Ion pump
ITS3
MF/FIT-C
Bellow
(No Gate Valve)
RB24
(ID 58mm)
Central beam pipe
(ID 32mm)

## Slide 13: Tolerances
B
C
A
Support #1
Support #2
Support #3
 | RUN3 |  |  | RUN4 |  | 
Quantity | A-side section (A) | Central part (B) | C-side section (C) | A-side section (A) | Central part (B) | C-side section (C)
Construction and deflection | 1.3mm | 0.6mm | 0.5mm | 1.3mm (1 | 0.6mm (1 | 0.5mm (1
Mechanical adjustment precision | 2.5mm |  |  | 0.2mm |  | 
Survey to beamline uncertainty | 1.5mm (2 |  |  |  |  | 
Quad fiducial to beamline uncertainty | 0.5mm (2 |  |  |  |  | 
L3 movement | <0.5mm (3 |  |  |  |  | 
B field movement | <0.5mm |  | <2.5mm | <0.5mm |  | <2.5mm
Linear sum | 6.8mm | 6.1mm | 8.5mm | 4.5mm | 3.8mm | 5.7mm
Measured RUN3 BP
LEB 22.2.12
LEB 23.3.12

## Slide 14: Aperture at injection RUN3 vs RUN4 (preliminary ALICE)
RUN3: n1 min 13.2 sigma
RUN4 n1 min 13.7 sigma
n1_min 13.7
n1_min 13.2

## Slide 15: Conclusions
ALICE would like to introduce these modifications in LS3:
New 32mm ID central beampipe, with thinner central Be section (0.5mm) and conical A-side section
New 58mm ID RB24 beampipe (1 section only), made of 1mm thick Al
With the presented geometry and tolerances, we have estimated the n1 min at injection of more than 13.7 sigma.