## Slide 1
A.Petralia, F.Nguyen, A.Doria (ENEA)
L.Giannessi (INFN-LNF)
LEAPS-INNOV Annual Meeting 2023
INFN & ENEA collaboration on Apple-X undulators
March 28th 2023
This project has received funding from the European Union´s Horizon 2020 research and innovation programme under grant agreement No. 101004728

## Slide 2
Source of Advanced Beam Imaging for Novel Applications
Italian Regional Call
- NdFeB
- Circ./Linear pol.
- λu 55 mm
- Br 1.22 T
- Min gap 5 mm
- 22 periods
- Kmax 3.4 (CP), 4.8 (LP)
- Length 1.35 m
- 3 modules
- out of vacuum
B
pipe
φ 10 mm
gap
5 mm
SABINA Apple-X undulator
THz user facility @ l ~ 10-100 mm
Operating at low energy e-beam - 30-100 MeV
Magnetic studies and design started by A. Petralia
Undulator realization and mechanical structure by
Detailed inspection performed at the factory
First prototype to be delivered by the 12th week of this year
Notes: Please, state the main cutting-edge facility in your undulator lab (picture are welcome) and the main (public not confidential) development in your lab (preferably in written form)

## Slide 3
AQUA Apple-X undulator
Both Apple-X undulators will be operating at INFN-LNF with the collaboration of ENEA-Frascati
EuPRAXIA@SPARC_LAB: FEL user facility @ l ~ 3-5 nm – water (AQUA in latin) window
- NdFeB
- Circ./Linear pol.
- λu 18 mm
- Br 1.35 T
- Min gap 1.5 mm
- 110 periods
- Kmax 1.15 (CP), 1.6 (LP)
- Length 2 m
- 10 modules
- out of vacuum
Mechanical structure issues can be learnt from experience with the SABINA Apple-X
Vacuum chamber structure to be decided accounting for wakefield effects on FEL performance
Magnetic errors distribution modelled from the SABINA undulator measurements
Notes: Please, state the main cutting-edge facility in your undulator lab (picture are welcome) and the main (public not confidential) development in your lab (preferably in written form)

## Slide 4
Thanks
Tak
Tack
Bedankt
Danke
Dziękuję
Grazie
Merci
Gracias
شك
“ Foster open innovation for accelerator-based lightsources in Europe”
https://leaps-initiative.eu
This project has received funding from the European Union´s Horizon 2020 research and innovation programme under grant agreement No. 101004728