## Slide 1: Barium Extraction from Xe Gas and Identification for nEXO
Chris Chambers
Brunner Neutrino Lab
McGill University
Ba

## Slide 2
Barium Tagging as an upgrade to nEXO Experiment
Barium Tagging: identify barium daughter at 0νββ decay site for complete background elimination
Requires counting of single Ba daughter in macroscopic amount of Xe
nEXO Collaboration
Phys. Rev. C 97, 065503 (2018)
100% Ba Tagging Efficiency
Advantages of Ba-Tagging:
Increases the projected sensitivity by factor of 3-4
Provides POSTITIVE signal of ββ decay
nEXO is a 0νββ search using a 5000kg liquid Xe TPC
nEXO Overview: Erica Caden, Session TS4-2
Notes: Erica Caden Overview Session TS4-2 (day before)

## Slide 3
Stage1:
Extraction of detector volume around the location of the decay to gas phase using a capillary tube.
Stage2:
RF carpet for efficient transfer of ion from capillary to RF funnel
Stage4:
The Linear Paul trap for detection of barium ion via laser fluorescence
spectroscopy​.
Stage5:
Multiple Reflection TOF Spectrometer for systematic studies and determination of ion mass.
Stage3:
RF funnel facilitates separation of xenon accompanying the Barium ion.
Canadian Ba Extraction and Tagging from Gas Xe
Notes: “Canadian Effort”
“Review of progress”

## Slide 4: What is a Linear Paul Trap?
DC electric field for directing and confining axial motion.
Design by Yang Lan @ TRIUMF
Construction by Hussain Rasiwala @ McGill
Retrieved from: PhD thesis, Y. Lan
Quadrupolar potential
Radial confinement using radio-frequency (RF) potentials

## Slide 5: Linear Paul trap for Ba-tagging
Custom designed for Barium tagging
Composed of a quadrupole mass filter (QMF), precooler, cooler and an ion buncher.
Trap/
Buncher
QMF
Cooler
Precooler
Ion injection
Laser
Ion bunch
To MR-TOF
Ion bunch
Laser
Design by Yang Lan @ TRIUMF
Construction by Hussain Rasiwala @ McGill
Ion bunch
To MR-TOF

## Slide 6: Single Barium ion detection
Uses ion trap for confining ions and laser induced fluorescence for barium ion detection.
Single ion detection has been demonstrated by collaborators at Carleton University.
Demonstrated first by M. Green et. al by studying 493nm florescence intensity from single barium ion.
M.Green, et al., Phys.Rev.A 76 (2007) 023404
Retrieved from: PhD thesis, Ryan Killick (Carleton University)
Matthew Green @ Stanford
Ryan Killick @ Carleton University

## Slide 7: What is an MRTOF?
Ions accelerated by potential gain kinetic energy
Ions with different mass-to-charge separate in time, and can be resolved
Operating Principle
Design
Consists of central drift-tube and 2 electrostatic mirrors formed by 6 cylindrical electrodes.
Ions are reflected between the mirrors to dramatically increase the MRP.
MR TOF
LAS
LPT
Perform systematic studies of the Ba-tagging extraction technique. (What ion species are present in the LPT?)
Confirm the isotope of barium identified in the LPT. (Was it really 136Ba in the LPT?)
Goals
Design and Construction by Kevin Murray
@ McGill

## Slide 8: MRTOF First Ions – No Reflections
Copper
Gold
Example Raw Waveforms
Time of Flight Spectrum
Single ion signal is approx. 2 mV
Preliminary
Data by Kevin Murray
@ McGill

## Slide 9: Lab Progress
18 months
Dec 2019
Jun 2021
Notes: Dec 2019

## Slide 10
McGill Experimental Neutrino Group
The nEXO Collaboration
> 200 scientists worldwide!
Summer 2019