## Slide 1: Experience with MicroMegas chambers with resistive strips
Givi Sekhniaidze
INFN sezione di Napoli
On behalf of the ATLAS MicroMegas community
(MAMMA)

## Slide 2: Overview
Tests of the resistive chambers in different gas mixtures and different conditions
    Structure of chamber with resistive strips
    Laboratory tests
      55Fe source
      X-ray gun
      Spark shape and characteristics
      Neutron beam tests at Demokritos laboratory in Athens:
        Neutron beam spectra
        V-I characteristics under neutron beam
        Spark probability
        Beam tests at H6:
          V-I characteristics
          Spark probability

## Slide 3
R11, R12 and R13 (1)
Small 100 x 100 mm2 chamber with 100 mm long strips and 250 µm strip pitch (similar to the previous prototypes – S3, R9, R10), 360 strips in total
Characteristics:
Resistive strips connected to the ground
Thin insulating layer between of the resistive and readout strips
AC coupling of signals
Sparks are neutralized through the resistive strips to the ground
PCB
Resistive paste
Insulator
Mesh
PCB
Insulator
≈0.5, 2, 5 MΩ/cm
R
1 MΩ
d=128 µm/E≈50 kV/cm
Readout strip
Rground

## Slide 4
CHAMBER | R11 | R12 | R13
Resistance to Ground (MΩ) | 15 | 45 | 20
Resistance along strip (MΩ/cm) | 2 | 5 | 0.5
R11, R12 and R13 (2)
Resistive characteristics of the
chambers

## Slide 5
Laboratory tests (1)

## Slide 6
Laboratory tests (2)

## Slide 7
Laboratory tests (3)

## Slide 8
Laboratory tests (4)
Chart: R12, R13 Transparency (55Fe source)
| 1132.8125 | 566.40625 | 377.60416666666669 | 283.203125 | 226.5625 | 188.80208333333334 | 133.27205882352942 | 102.98295454545455 | 83.912037037037038 | 70.80078125 | 61.233108108108105 | 53.94345238095238 | 48.204787234042556 | 43.56971153846154 | 39.747807017543863 | 36.542338709677416
R13 - 85:15 Ar:CO2 | 0.95385 | 0.97692 | 0.98462 | 0.98462 | 0.98462 | 0.97692 | 0.98462 | 0.98462 | 0.99231 | 1 | 1 | 0.98462 | 0.96923 | 0.95385 | 0.92308 | 0.90769
R13 - 93:7 Ar:CO2 | 0.95699 | 0.97312 | 0.97312 | 0.97312 | 0.96774 | 0.97312 | 1 | 0.99462 | 0.99462 | 0.99462 | 0.97312 | 0.94624 | 0.9086 | 0.87634 | 0.83333 | 0.80645 | 0.74194 | 0.7043 | 0.66667 | 0.63441 | 0.60215
R12 - 85:15 Ar:CO2 | 0.95541 | 0.97452 | 0.98089 | 0.98089 | 0.97452 | 0.98726 | 0.98726 | 0.98726 | 0.99363 | 0.99363 | 1 | 0.98726 | 0.97452 | 0.95541 | 0.93631 | 0.91083
R12 - 93:7 Ar:CO2 | 1 | 0.99535 | 0.9907 | 0.98605 | 0.98605 | 0.9907 | 0.98605 | 0.9814 | 0.9814 | 0.9814 | 0.97674 | 0.94884 | 0.92093 | 0.88837 | 0.8186 | 0.75814 | 0.71628 | 0.68372 | 0.64651 | 0.61395 | 0.58605 | 0.54884 | 0.52093 | 0.47907 | 0.34419

## Slide 9
Laboratory tests (5)

## Slide 10: Spark shape & characteristics – R11
10 µs
[V]
Time (s)
R11
Laboratory tests (6)

## Slide 11: Spark shape & characteristics – R12 & R13
10 µs
10 µs
Laboratory tests (7)

## Slide 12: Homogeneity of chambers
Laboratory tests (8)
Chart: Distance from connection to ground (mm)
| 12 | 31 | 49 | 67 | 83
R12 c1 | 174 | 174 | 175 | 166 | 167
R12 c2 | 164 | 164 | 165 | 158 | 150
R12 c3 | 174 | 167 | 173 | 152 | 145
R12 c4 | 172 | 172 | 168 | 161 | 156
R12 c5 | 168 | 164 | 161 | 160 | 160
R13 c3 | 148 | 148 | 152 | 159 | 153 | 151 | 164
55Fe source, Ar:CO2 (85:15)

## Slide 13: Conclusions from the laboratory tests
R11, R12 and R13 are working fine with the 55Fe source and with X-ray gun.
Very good homogeneity along the strips
Low spark rate
Spark current is the order of 10-20 nA, almost 1000 times less than for S3 chamber (non-resistive)
No HV breakdown, no dead time

## Slide 14
Neutron beam test at
Demokritos National Research Center
Exposed R11 and a standard MM in first week of May to neutron beam at Demokritos NRC (Athens)
Neutrons of 5.5 MeV with fluxes up to 1.5 x 106 n/cm2
R11 & sMM were read out through
  Single preamplifier (OR of 72 or all 360 strips)
  Single preamplifier (mesh current)
  64 individual strips connected to Gassiplex readout system (under analysis, not reported here)
Gas mixtures tested: Ar:CO2 (85:20; 85:15, 93:7)

## Slide 15
Neutron spectra in R11
55Fe spectrum taken under neutron irradiation
Typical charge spectra recorded in neutron beam
Gas: Ar:CO2 (85:15)
Neutron beam test (1)

## Slide 16
MM mesh currents in neutron beam
Standard MM:
Large currents
Large HV drops, recovery time O(1s)
Chamber could not be operated stably
R11:
Low currents
Despite discharges, but no HV drop
Chamber operated stably up to max HV
Gas: Ar:CO2 (85:15) Neutron flux: ≈ 106 n/cm2
Neutron beam test (2)

## Slide 17
Spark rates
Neutron beam test (3)

## Slide 18
Conclusions from neutron test (R11)
R11 worked fine in a neutron flux of up to 1.5 x 106 n/cm2
Despite sparks, no HV breakdown, no dead time
Clear signal from a 55Fe source under neutron irradiation
Measured three Ar:CO2 gas mixtures, 93:7 looks very interesting, with a spark rate almost a factor 10 lower than for 80:20

## Slide 19
Beam test in H6
5-18 July 2010
R11, R12, R13, and P3 chambers were tested in +120 GeV pion beam (intensities 40 kHz & 5 kHz) for two Ar:CO2 mixtures, 85:15 and 93:7
Main goals:
  Study HV and current behaviour of resistive and non-resistive chambers in a hadron beam
  Measure performance (spatial resolution and efficiency) of resistive chambers
  Study performance of long strips (0.4 m & 1m, non-resistive)
A few million of events to be analyzed

## Slide 20
Beam test in H6 (1)
Ar:CO2 – 85:15

## Slide 21
Beam test in H6 (2)
Ar:CO2 – 85:15

## Slide 22
Beam test in H6 (3)
Ar:CO2 – 93:7

## Slide 23
Beam test in H6 (4)
Chart: R12 : Spark probability vs Gain
| 3481.5 | 4666.7 | 6296.3 | 8592.6 | 11629.6 | 16074.1 | 22592.6 | 34222.199999999997
R12(93:7) | 5.814e-06 | 2.7743e-05 | 6.4972e-05 | 8.8842e-05 | 0.00016493 | 0.00023968 | 0.00040068 | 0.00085724
R12(85:15) | 5.102e-06 | 2.3166e-05 | 3.0418e-05 | 4.1841e-05 | 5.7065e-05 | 7.5802e-05 | 0.00010132 | 0.00017871 | 0.00026357 | 0.0003735

## Slide 24
Chart: R13 : ArCO2 - 85:15 thr=100mV
| 1333.3 | 1777.8 | 2370.4 | 3185.2 | 4074.1 | 5629.6 | 7481.5 | 9703.7000000000007 | 13259.3
angle=0 | 1.25e-06 | 7.3171e-06 | 1.3571e-05 | 1.879e-05 | 3.2308e-05 | 5.4507e-05 | 8.1081e-05 | 0.00012763 | 0.00019059
angle=40 | 1.5385e-06 | 5.5556e-06 | 4.9566e-06 | 1.486e-05 | 3.4884e-05 | 3.3724e-05 | 5.9836e-05 | 9.3842e-05 | 0.00018141
Beam test in H6 (5)

## Slide 25
Overall conclusions
R11, R12 and R13 show very similar behavior
Robust & stable, no breakdown at all, excellent performance in neutron and hadron beams
Signals are clean, good gas gain and energy resolution (slightly better for R12)
Charge-up reduces signal by less than 10%
Homogeneity across chamber good
Short and small spark signals and fast recovery time
Ar:CO2 mixture 93:7 gives a factor 10 lower spark rate under neutron irradiation compared to 80:20 (no difference in hadron beam with 85:15)