## Slide 1: Status GEM Detectors
Bernhard Ketzer
COMPASS/AMBER Technical Board
19.01.2021

## Slide 2: Test of R&S Power Supply during Dry Run
Noise spikes increased using the new power supply
New pedestals were taken and loaded

## Slide 3: Occupancy compared to 2019
The occupancy has the same magnitude compared to 2019
XY is sligthly worse, U slightly better

## Slide 4: New Detectors for 2021 (G3G)

## Slide 5: Status of Production
GEM foils and readout circuit for 2 detector received from CERN, optical test ok
frames for 2 detectors received, being prepared
support plates for 2 detectors received, strong bending of large ones observed, will be reproduced by company

## Slide 6: APV Frontend Cards
3 Prototypes tested, ENC measured
Tested with Test Station + existing ADC
54 more frontends in production.
New ADCs for APV Readout
16 Channels, 12 Bit, 65 MSPS
2 units needed for one GEM detector
Schematic: I. Konorov
Layout: C. Tezel, C. H.
Assembly: 3 Prototypes

## Slide 7: Stabilized Voltage Divider
Prototypes assembled + tested
  Output voltage stable for small loads
  Current limited (~15µA)
  even smaller voltage change when loading neighboring pad
Todo:
  Test in detector

## Slide 8: Discharge Simulator
APV FE has protection against discharges
Different scenarios tested
  Discharge protection works
  Long-term stable
Discharge Simulator
Up to 800V / 800nC
Monitoring Output
Measure Voltage/Current
Fast rise time

## Slide 9: VMM Tests
Setup of an RD51 SRS VMM lab system:
Ordered electronics for one 30x30 cm² GEM prototype:
- 14 VMM hybrids, 1 DVMM, 1 CTF
- FECs and a crate from other group on loan
(we will order our own, when crates available in CERN store)
Status:
- 14 VMM hybrids currently in production, delivery expected in February
- DVMM, CTF ready at company SRS Technology, will be delivered with hybrids
- so far: few hybrids on loan, our own DVMM (prototype version)
- Michael assembled a new SRS create, almost complete

## Slide 10: Spare Slides

## Slide 11
First Generation GEMs (CG1G)
TP flat cable 2x25 cond., max. 60 cm
E - TWISTED PAIRS FLAT CABLES FOR IDC - PITCH 0.635 mm
3M type 79992-25P-270A
Repeater Card
TP Flat cable, 2x20 cond., max. 3 m
FLAT CABLE TWIST 40C 1.27MM AWG28
3M type 2100/40
HV Switch
A732N (6kV, 1mA)
A516 (12V, 1.5A)
CAEN SY527 Mainframe
±12V
ADC Cards
(2 Detectors)
TRG/CLK
SCREENED VIDEO CABLE, 4,7 mm, 2 PAIRS
type VB 04 P
APV LV: 2ch per plane (± 3.5V, GND, -0.9A, +0.7A)
FLEX.COPPER CABLE 12x 2,5 mm2
Deutronics DN35W-5 (5.5V, 6A)
ADC LV: 2ch per station (±5.5V, GND, +3.2A, -0.6A)
S-HV cable HV COAX.CABLE HTC-50-1-1, 5kV,RED
type HTC-50-1-1
1 station = 2 detectors = 4 planes
6 APV25 (S0/S1) per plane

## Slide 12
PixelGEMs (CG2G)
A732N (6kV, 1mA)
CAEN SY527 Mainframe
Deutronics DN35W-5 (5.5V, 6A)
TP flat cable 2x25 cond., max. 150 cm
E - TWISTED PAIRS FLAT CABLES FOR IDC - PITCH 0.635 mm
3M type 79992-25P-270A
S-HV cable HV COAX.CABLE HTC-50-1-1, 5kV,RED
type HTC-50-1-1
Drift
Center
1 station = 2 detectors = 4 planes
8 APV25 (S1) per plane
LV APV: 2 ch. per det. (±5V, GND)
LV ADC: 3 ch. per station (2x +5V, 1x -5V, GND)

## Slide 13
Upgraded Triple GEMs (CG3G)
1 station = 2 detectors = 4 planes
24 APV25 (S1) per plane
Required Power Supply Rails for 1 Detector:
4 kV, 1 mA for GEMs & Drift
3.3 V, 3 A (4x) for APV Supply (floating, remote sense wires)
5 V, 3 A for each ADC (floating)
A732N (6kV, 1mA)
CAEN SY527 Mainframe
New ADC chain (iFTDC)
(for 24 APVs in total)
Per ADC +5V & <3A
3,3V & 2x3A
S-HV cable HV COAX.CABLE HTC-50-1-1, 5kV,RED
type HTC-50-1-1
Flat cable
EQDP-014-40.00-STR-SBL-5-B
3,3V & 2x3A
Rohde&Schwarz HMP4040 | 4 chan. (each 10 A), 384 W

## Slide 14
Triple GEMs with VMM (CG4G)
1 station = 2 detectors = 4 planes
24 VMM3a ASICS per plane
Required Power Supply Rails for 1 Detector:
4 kV, 1 mA for GEMs & Drift
VMM ASICs:
(1.9 – 3.5) V, 24 x 1.67 A grouped to 4 x 10 A
Auxilary front-end electronics:
(2.9 – 3.5) V, 2.4 A (all front-end boards)
A732N (6kV, 1mA)
CAEN SY527 Mainframe
Rohde&Schwarz HMP4040 | 4 chan. (each 10 A), 384 W
Rohde&Schwarz HMC8043 | 3 chan. (each 3 A), 99 W
S-HV cable HV COAX.CABLE HTC-50-1-1, 5kV,RED
type HTC-50-1-1
VMM ASIC Power: (1.9 – 3.5) V, 4 x 10 A
→ 76 – 140 W
Auxilary front-end electronics: (2.9 – 3.5) V, 2.4 A
→ 6.9 – 8.4 W
Deutronics DN35W-5 (5.5V, 6A)
Or
Example SRS VMM hybrid:
2 VMM ASICs, Aux.(FPGA, ...)
VMMs: (1.9-3.5) V @ 1.67 A
Aux.: (2.9-3.5) V @ 0.1 A
→ 24 hybrids/detector
Bare VMM ASIC: ~0.8 A @ 1.2 V
48 VMM ASICs need/detector

## Slide 15
Does not work!
Old ADCs (CG1G) need 2ch with > 3A (?) per station
New ADCs (CG3G): 4 ADCs per station needed

## Slide 16: LV Configurations
Generation | p.s. type | GMnnU1 | GMnnV1 | GMnnX1 | GMnnY1
CG1G | APV: CAEN A516 | 2ch, 3.5V, -0.9A, +0.7A | 2ch, 3.5V, -0.9A, +0.7A | 2ch, 3.5V, -0.9A, +0.7A | 2ch, 3.5V, -0.9A, +0.7A
 | APV: HMP4040 | 2ch, 3.5V, -1.8A, +1.4A |  | 2ch, 3.5V, -1.8A, +1.4A | 
 | ADC: DN35-5 | 2ch, 5V, +3.2A, -0.6A |  |  | 
CG2G (PGEM) | APV: DN35-5 | 2ch, 3.5V, -1.8A, +1.4A |  | 2ch, 3.5V, -1.8A, +1.4A | 
 | ADC: DN35-5 | 3ch, 5V, +6A, -3A |  |  | 
CG3G | APV: HMP4040 | 1ch, +3.3V, 4-6A | 1ch, +3.3V, 4-6A | 1ch, +3.3V, 4-6A | 1ch, +3.3V, 4-6A
 | ADC: HMP4040 | 1ch, +5V, <3A | 1ch, +5V, <3A | 1ch, +5V, <3A | 1ch, +5V, <3A
CG4G | VMM (SRS): HMP4040 | 1ch, 1.9-3.5V, 9.6A | 1ch, 1.9-3.5V, 9.6A | 1ch, 1.9-3.5V, 9.6A | 1ch, 1.9-3.5V, 9.6A
 | Auxiliary | 1ch, 2.9-3.5V, 2.4A |  | 1ch, 2.9-3.5V, 2.4A | 
For Center HV switch: 1 ch 12V, no current  find simpler solution
green: existing
dark orange: plan for 2021
light orange: possible future

## Slide 17: Price Tags
Type | Web price | Needed per station
HMC8043 (3ch) | 1450 | 2 (Moritz‘ conf.)
HMP4040 (4ch) | 2310 | 1 (CG1G), 2 if also ADC
 |  | 2 (CG2G, CG3G)
but not sufficient for ADCs!
Note:
HMP4040 already in use for APVs at NA64 and in the lab
will perform rate test in the lab
compatibility with DCS?
connection on backside?

## Slide 18: Occupancy vs Trigger Rate

## Slide 19: Slides from Moritz: TB Nov. 12, 2019