## Slide 1
"Simulating Physics with Computers", International Journal of Theoretical Physics, volume 21, 1982, p. 467-488, at p. 486 (final words)
Richard Feynmann:
  “Nature isn't classical, dammit, and if you want to make a simulation of nature, you'd better make it quantum mechanical.”

## Slide 2: Why?
  Design new materials
  Design more efficient chemical processes
  Break RSA encryption
  Provide optimization solutions

## Slide 3
Quantum Computers
Trapped ions
Superconducting qubits
Majorana Electrons?
Diamond NV centers
Neutral atoms

## Slide 4
ECCTI
30.06.2022
Celeste Torkzaban
Collaborative design of a trapped-ion quantum computer with fully interconnected qubits

## Slide 5: Outline
Overview of the collaboration
Target specifications for the quantum computer
How to shuttle and entangle specific qubits
Design and fabrication details
Timeline

## Slide 6: Quantum Valley Lower Saxony (QVLS)
Collaborate on quantum technologies
Channel expertise from existing research groups
Speed up progress by involving more researchers
25M Euro in funding to create a 50 qubit trapped-ion quantum computer by 2025 and develop additional quantum technologies

## Slide 7: Areas of expertise
  Quantum algorithm developments
  Quantum machine learning
  Trap design
  Software integration
  Cryostat design
  Trap fabrication
  Laser setup in 19” racks
  Control routines for operating and benchmarking
  Electronics
  Integrated detectors
  Integrated waveguides
  Compact laser sources
  ....and more

## Slide 8: Collaboration
Vs.
http://clipart-library.com/clipart/697107.htm

## Slide 9: Usefulness of a Quantum Computer
Number of qubits
Qubit interconnectivity
Coherence time of qubits
Two-qubit gate fidelity
State preparation and measurement (SPAM) error
Speed of gate operations
} Quantum Volume

## Slide 10: Existing experiments at LUH and PTB
Number of qubits: 1-2
Qubit Interconnectivity: all-to-all
Coherence time: >7s
Two-qubit gate fidelity: ~0.5 % [1]
SPAM error: ~1% [2]
Speed of gate operations: ~2 ms
[2] S. Halama et al., arXiv:2204.09112 [quant-ph/]
[1] G. Zarantonello et al., Phys. Rev. Lett. 123, 260503 (2019) DOI: 10.1103/PhysRevLett.123.260503

## Slide 11: Target parameters of the QVLS Quantum Computing Demonstrator
Number of qubits: 50
Qubit Interconnectivity: all-to-all
Lifetime of qubits: much longer than necessary
Two-qubit gate fidelity: <10-4
Spam error: better than 1%
Speed of gate operations: ~5-10 ms

## Slide 13: Essential Ingredients
An Empty lab and a plan

## Slide 14: Essential Ingredients
  An empty lab and a plan
  An X-junction RF surface trap
    Be+ ion qubits driven by microwaves
    Ca+ ion for sympathetic cooling

## Slide 15: Essential Ingredients
  An empty lab and a plan
  An X-junction RF surface trap
    Be+ ion qubits driven by microwaves
    Ca+ ion for sympathetic cooling
  Cryogenic environment (5K)
  DC, RF, and microwave electronics
  Free-space lasers for cooling and detection
  Imaging system

## Slide 16: Trap design
M. Carsjens et al., Appl. Phys. B 114, 423-250 (2014)

## Slide 17: Trap Fabrication
State of the Art:
Multi-layer Trap Fabrication
1.
2.
3.
4.
A Bautista-Salvador et al 2019 New J. Phys. 21 043011
Under development:
Through-Substrate Vias
Socket made of PEEK with Fuzz buttons

## Slide 18: Cryostat Design
Inner vacuum chamber: thick copper walls at 5K
Closed-cycle cryocooler:
1.8W @ 4.2K
Ultra-low vibration interface via He buffer gas
50K Radiation Shield
Feedthroughs
Viewports
Based on the design of the 1st generation cryogenic experiment at LUH [3]
[3] T. Dubielzig et al. Rev. Sci. Instr. 92, 043201 (2021)
Imaging system

## Slide 19: Imaging Design
Primary mirror
Glass beam
Pillar
Secondary
mirror
Images from E. Vandrey, Cryogenic Schwarzschild Objective for the Detection of Trapped-ion Qubits, Bachelor thesis, Leibniz Universität Hannover (2021)
Achromatic Schwarzschild lens focuses light from ions onto either an EMCCD camera or a PMT [2]
 | [2] S. Halama et al., arXiv:2204.09112 [quant-ph/]

## Slide 20: Inner Design
Trap chip and interposer
Socket Socket mount
Schwarzschild Objective
Piezo translation stages
Filter board

## Slide 21: Electronics and thermalization of cables
  ARTIQ control system (Norman’s talk yesterday)
  RF resonator
Thermalblock: reduce conductive heat
Inner vacuum chamber @ 5K
Bobbins and clamps for thermalizing cables to 50K
Notes: Active impedance matching with resistance change

## Slide 22: Timeline
Run algorithms with 50 Be+ ions

## Slide 23: One design to rule them all
https://static.dw.com/image/15912725_403.jpg

## Slide 24: Beyond QVLS
ATIQ

## Slide 25: Interested in working with us?
PhD and Postdoc positions available
Contact me: torkzaban@iqo.uni-hannover.de
https://www.castleholic.com/2017/03/welfenschloss.html