## Slide 1: Update on electron lens impedance studies (without electrons)
B. Salvant, C. Zannini
Thanks to Antti Kolehmainen, Diego Perini (EN-MME) and Riccardo de Maria (BE-ABP)

## Slide 2: Context
Hollow electron lens for halo control for HL-LHC
Design discussed since a long time with EN-MME
Work in particular in 2017 by a 2-week HSSIP stagiaire Chloe Rakotoalivony in 2017

## Slide 3: New design (August 2020)
Provided by Antti from EN-MME

## Slide 4: Comments
Bellow should be shielded

## Slide 5: Comments
Bellow should be shielded
Pump should be shielded

## Slide 6: Comments
Bellow should be shielded
Pump should be shielded
Non-standard BPM (studied)

## Slide 7: Comments
Bellow should be shielded
Pump should be shielded
Non-standard BPM (studied)
Y chamber volume could be reduced

## Slide 8: Comments
Bellow should be shielded
Pump should be shielded
Non-standard BPM (studied)
Y chamber volume could be reduced
BGC design ongoing and not available
Coatings? ID60 should impose copper coating in plain tubes.
New request to have 2 bellows around the BGC
 Under discussion with EN-MME

## Slide 9: Y chamber
EN-MME followed the guideline we provided to minimize the volume around the incoming pipes
We could theoretically do a bit better, by adding a blade as in the other LHC Y chambers.
Nevetherless, contrary to the other Y chambers, not a simple symmetric merge of two pipes

## Slide 10: Longitudinal impedance
- First mode at 2.86 GHz (18 kOhm and Q=18,000 if copper coated, 2 kOhm and Q= 2800 if not)
- Im(Z/n)eff ~ 0.02 mOhm for 1 Y chamber (to be compared to 90 mOhm for full LHC)
Frequency (GHz)
CST Wakefield solver
CST Eigenmode solver
Z (LinacOhm)

## Slide 11: Transverse impedance (y  horizontal)
Beta ~280 m (from Riccardo)
Im(Zx)= 1.5 Ohm per 5 mm = 300 Ohm/m for 1 Y chamber

## Slide 12: Transverse impedance (x vertical)
Beta ~280 m (from Riccardo)
Im (Zy)= 0.5 Ohm per 5 mm = 100 Ohm/m for 1 Y chamber
First mode at 1.82 GHz
4 kOhm/m and Q=19,000 for copper from eignemode

## Slide 13: Adding a shielding blade
 Not a trivial geometry to manufacture

## Slide 14: Impact of shielding blade
Mode at 2.86 GHz disappears
No significant beneficial impact on Im(Z/n)
Vertical mode gets worse (30 kOhm/m instead of 4 kOhm/m)

## Slide 15: Conclusions for Y chamber
Current model leads to very moderate impedance contribution.
One could reduce longitudinal impedance if it is an issue by adding a blade, but
  (1) It is not clear that the shape is feasible
  (2) The first vertical mode at 1.85 GHz increases from 4 to 30 kOhm/m in simulations.
The additional request of adding two bellows around the BGC needs to be studied.

## Slide 16: Simulation model
Geometric impedance of the hollow electron lens
Design not yet finalized
Beam direction
Ychamber
BPM
ZG-elens≈ 2*Ychamber + 2*BPM + CBGC

## Slide 17: Beam position monitor impedance simulations
Wakefield solver
Longitudinal impedance

## Slide 18: Beam position monitor impedance simulations
Wake is not decayed. Impedance spectrum gives information about the frequency of the impedance resonances. First resonance expected at about 350 MHz. Four significant impedance resonances are expected below 1 GHz
Wakefield solver
Longitudinal impedance

## Slide 19: Beam position monitor impedance simulations
Very good agreement between eigenmode and wakefield solver for the frequencies of the impedance resonances
Longitudinal impedance magnitude
Wakefield solver
Eigenmode simulations
Frequency / GHz
Wake impedance / Ohm
Wake impedance / LINAC Ohm
Q- factors

## Slide 20: Beam position monitor impedance simulations
Wake is not decayed. Impedance spectrum gives information about the frequency of the impedance resonances. First detuning resonance expected at about 350 MHz.
First driving resonance expected at about 540 MHz.
Transverse impedance
Wakefield solver

## Slide 21: Beam position monitor impedance simulations
Very good agreement between eigenmode and wakefield solver for the frequencies of the impedance resonances
Horizontal impedance magnitude
Wakefield solver
Eigenmode simulations
Frequency / GHz
Wake impedance [Ohm/m]
Wake impedance [LINAC Ohm/m]

## Slide 22: Beam position monitor impedance simulations
Horizontal detuning impedance
Eigenmode simulations
Frequency / GHz
Wake impedance [LINAC Ohm/m]
Wakefield solver
Wake is not decayed. Impedance spectrum gives information about the frequency of the impedance resonances. First resonance expected at about 350 MHz. Four significant impedance resonances are expected below 1 GHz

## Slide 23: Beam position monitor impedance simulations
Horizontal driving impedance
≈ 3 kΩ/m
Eigenmode simulations
Frequency / GHz
Wake impedance [LINAC Ohm/m]
Wakefield solver
Wake is not decayed. Impedance spectrum gives information about the frequency of the impedance resonances. First resonance expected at about 350 MHz. Four significant impedance resonances are expected below 1 GHz

## Slide 24: Beam position monitor impedance simulations
Vertical driving impedance
Wake is not decayed. Impedance spectrum gives information about the frequency of the impedance resonances. First resonance expected at about 350 MHz. Four significant impedance resonances are expected below 1 GHz
Wake impedance [LINAC Ohm/m]

## Slide 25: Effect on HL-LHC stability
Courtesy of N. Mounet
Large margin on the shunt impedance of the three main HOMs

## Slide 26: Effect on HL-LHC stability
Large margin on the shunt impedance of the three main HOMs
Courtesy of N. Mounet

## Slide 27: Summary
A preliminary beam coupling impedance model of the electron lens including the effect of BPM and Y chamber has been built
The results are not final
  Design not yet finalized:
    BGC not integrated in the CATIA model
    BPM terminations not integrated in the CATIA model

## Slide 28: Appendix

## Slide 29: Beam position monitor impedance simulations
First detuning mode

## Slide 30: Beam position monitor impedance simulations
Second detuning mode

## Slide 31: Beam position monitor impedance simulations
First driving mode

## Slide 32: Single bunch stability

## Slide 33: Single bunch stability