## Slide 1: RF Power Network – Draft Slides
Matthew Capstick
26-01-2021

## Slide 2: Module

## Slide 3: RF Unit
BOC Cavities
x3.5 pulse compression
170MW
334ns
40.6MW
334ns
Double Height
Waveguide
Single Height WR90
Waveguide

## Slide 4: RF Components
New components required for the RF unit and waveguide network
  Double height waveguide
  Double height waveguide flanges
    Rectangular X-band WR90 – Bolted
    Rectangular X-band WR90 – Clamped
    Choke mode circular – Clamped
  Bends for DHWG
  DH Hybrids

## Slide 5: RF Components
New components required for the RF unit and waveguide network
  Double height waveguide
  Double height waveguide flanges
    Rectangular X-band WR90 – Bolted
    Rectangular X-band WR90 – Clamped
    Choke mode circular – Clamped
  Bends for DHWG
  DH Hybrids

## Slide 6: Flanges
DH X-band WR90 – Bolted
DH X-band WR90 – Clamped
Double Height Choke Mode

## Slide 7: DH X-band WR90 – Bolted
Rectangular Flange design:
Adapted from the current X-band WR90 flange:
  Assumes the current ‘square knife edge’ geometry will still work
  Assumes that 8 bolts will still provide enough gasket sealing pressure

## Slide 8: Vacuum Test Pieces
Currently in manufacture for testing:

## Slide 9: DH X-band WR90 – Clamped
Markus suggested and alternative flange based around the:
IUWR90 gasket RF connection and vacuum seal
KF50 equivalent external geometry
It would require alignment features (pins or dowels) to fix rotation
Whether the KF50 clamp would produce enough clamping force is unknown

## Slide 10: Vacuum Test Pieces
Currently in manufacture for testing:
Replace with correct
image
Whether chain clamps can provide the required sealing force is unclear.
In analysis the gasket reaches maximum deformation at 60% of the maximum QCF DN63 Clamp pressure

## Slide 11: Choke Mode
Advantages
  Uses standard CF DN64 Copper gaskets and chain clamps
    Vacuum sealing unlikely to be a problem
  Separates the RF and Vacuum connections
  Axially rotatable
Complications:
  Relatively complicated geometry
  Introduces additional brazing operations
Status:
  Required for waveguide pumping ports
  RF Geometry not final