## Slide 1: LHCb Vertex detector upgrade.
Jan Buytaert
C.E.R.N.
For the LHCb VELO Group.

## Slide 2: Vertex detector environment.
    => Danger of thermal run away !
    => Silicon must be cooled to -10 0C.
Severe & non-uniform irradiation damage.
500
50
5
Radius (cm)
Dose after 100 fb-1
neqcm-2 x 1016
TID (MRad)
7 mm
370 Mrad or 8 1015 neq/cm2.
Curves fitted to A.r-1.9
radius (cm)
Particle Hits / Event / cm2
Luminosity (cm-2s-1) | 2.1032 Current | 5.1032 | 10.1032 | 20.1032 Upgrade
A= | 0.98 | 1.46 | 2.46 | 4.80
~ 8 particles/cm2/event at r=7.5 mm
Particle occupancy per event (simulation)
      The detector operates in 10-6 mbar vacuum.
      Access after installation is VERY difficult!

## Slide 3: Pixel module.
Base design:
  Sensor tiles: made of 3 readout asic’s on a single sensor, with a guard ring of 500 um.
  2 sensor tiles are mounted on opposite sides of the substrate.
  Substrate choices:
    Diamond : excellent mechanical and thermal properties: => low mass
    carbonfibre/TPG : as used for the present VELO.
  Prototype work is starting using Timepix assemblies.
~15mm
ASIC
ASIC
ASIC
~43mm
Sensor tile
Top Sensor 150um
ASIC150um
Bot Sensor 150um
ASIC150um
Substrate 200um
Connector
Cooling channel
Glue 50um
  If the TSV technology becomes accessible soon, single sided modules could be possible.

## Slide 4: Pixel module & Detector layout.
A ‘station’ is made of 8 sensor tiles.
  active area is near 100% (except small gaps).
  Closest pixel is at 7.5 mm from the beam center.
top tiles in yellow, bottom tiles in green
Sensor tile
1.1 mm gap
    The full detector is composed of 26 stations.
    The modules on either side of the beam are staggered to create overlap regions.
    This layout has been simulated to be fully efficient (4 hit per track) in the LHCb acceptance 250x300mrad.

## Slide 5: Module Cooling.
  Initial ANSYS simulations done.
  Model includes radial (r-1.9) and temperature dependent leakage power generated in Si.
  Extreme conditions are just OK...
  Verifications with thermal mockups are planned.
CO2 cooling
temp -35 C
Tip temp -4 C
Asic power = 1.5W/cm2
Bias voltage = 900V
After 1016 nequivcm-2
Material | Thermal Conductivity (W / m K)
Silicon | 150
ASICs | 190
Glue | 1
Aluminum | 200
CVD Diamond | 1600
Silicon 0.150
ASIC 0.150
Substrate 0.200
Epoxy 0.050
Al 0.050
All dimensions in mm

## Slide 6: ASIC development: analog
We are collaborating with the Timepix2 design:
  Analog requirements overlap ~100%:
Input charge | Bipolar (h+ and e-)
Leakage current compensation | YES (both polarities)
Peaking time | ≤ 25ns
Preamp output linear dynamic range | < 40 Ke-
TOT linearity and range | <200 Ke- → Maximize linearity >200 Ke- → Monotonic response
ENC (σENC) | ~75 e-
Detector capacitance | < 50 fF
Discriminator response time | < 2ns
Full chip minimum detectable charge | < 500 e-
Threshold spread after tuning | < 30 e-
Pixel analog power consumption | < 15-20 µW @ 1.2V
Full chip analog<1.3W

## Slide 7: ASIC development: digital
Timepix2:
  Digital functionality :
    Simultaneous Time-over-threshold and time identification.
    sparse and data driven readout.
    High speed output links >N x 500Mbit/s.
    Still under discussion.
  Peripheral logic and DAC’s from Medipix3
  Total power budget <1.5W/cm2 @ 1.2 V.  <3W full chip
  Radiation hardness TID 400Mrad, but not SEU.
Final VELOpix will be derived from Timepix2 :
  Only modifications in digital parts : Clustering, formatting & buffering, SEU protection.
  Addition of multi-Gbit output links.

## Slide 8: Data rates
Numbers at highest occupancies:
    average particle rate per asic ~ 5 particles/25ns = 200MHz
    average pixel cluster size ~3: (pessimistic assumption, 300um Si)
Information bits per pixel : 32 !
      4 bit : Time over Threshold value.
      12 bit : bunch identification
      16 bit : pixel address.
=> Single asic data production can reach 19 Gbit/s !
30% data reduction can be achieved by clustering data: 13.6Gbit/s
    share the bunch id (12bit) between clustered pixels,
    ‘share’ address bits (by special encoding).
    must be done before column readout, i.e. inside pixel array !
    most efficiently in units of 4x4 pixels = “Super pixel”

## Slide 9: Super pixel
Super pixel layout:
  group digital logic in a single area.
    Advantages:
      Space saving : some functional blocks can be common (time-multiplexed).
      More efficient distribution of power and global signals.
      Better analog/digital isolation.
      Digital column logic is synthesized with standard library. Ease, reliability, yield …
    Disadvantages:
      Bonding pads on top of digital circuit:
        => digital feedback in analog frontend. Shielding ?
      Non-uniform analog input capacitance:
        => Only small effect
A
A
A
A
A
A
A
A
Super pixel
Digital
A
A
A
A
A
A
A
A
220 um
~140 um
220 um
    Status:
      The verilog code for digital column exists and has been laid out. Final simulations are done. We will have realistic power estimates soon.
      It would be extremely useful to have a ‘low speed/low power’ library for IBM 130nm ! Would result in a big saving in area and power !

## Slide 10: Pixel matrix readout architecture.
Pixel matrix readout architecture
  Internal bus speeds:
    Column bus : 8bit@40MHz
    Output bus : 16bit@320MHz
  Total ASIC output : ~16Gb/s.
  Buffering in :
    Super pixel : 2 clusters
    Super pixel group FIFO : ~400 bit
    Output FIFO: multi kbyte
Simulation shows losses< 0.5% in highest occupancy conditions.
4 x
FIFO
Super pixel
column
Super pixel
column
Super pixel
column
Super pixel
column
Periphery &
Output port
16x
Serializer
Driver
Analog
frontend
Analog
frontend
Analog
frontend
Cluster
logic
16x
Super pixel
buffer
FIFO
Super pixel
Super pixel
Super pixel
Super pixel
Super pixel group
4x
16x
Super pixel
column
Column bus
Super pixel group
Super pixel group
Super pixel group
EOC
logic
Super pixel group
~ 4Gb/s
Output bus
40MHZ
320MHz

## Slide 11: ASIC design. Data reduction
Address encoding in 4x4 super pixel :
  “Row hit indicator” : indicate which rows have hits (4 bit, always present).
  0 to 4 “row hit patterns” : indicate which pixels in row are hit (4bit).
  Super pixel address : 12 bit.
  Examples:
  Gain compared to individual pixel address :
  Reject large multiplicity :
    If hit > N then no readout.
    N is configurable and rejection can be de-activated.
Super pixel
Row hit indicator
0 1 0 0
X
0100
0010
Super pixel
Row hit indicator
0 0 1 1
X
0011
0110
0010
X
X
# hits | Individual address | Row hit encoding
1 | 16 bit | 20 bit
2 | 32 bit | 24 bit
3 | 48 bit | 28 bit
4 | 64 bit | 32 bit

## Slide 12: ASIC design. Data reduction
Sharing across super pixel boundaries :
  Only in 1 direction (column)
  some limitations may lead to wrong or no clustering. But never loss of data.
  Results in ~10% data reduction.
Super pixel n
X1
X2
Super pixel n+1
Hit X1 will be transferred
to super pixel n+1

## Slide 13: Packet format

## Slide 14: Simulations with Gauss/Boole data
Most exposed asic

## Slide 15: Simulations with Gauss/Boole data
Column | Efficiency (only missing packets)* | Efficiency (correct packets) | FIFO buffer size, # words, header/data | Avg. data rate, Mbps | Proportional and absolute area of FIFO
28 | 99.150 % | 98.916 % | 3/9 | 241.450 | 
28 | 89.816 % | 88.906 % | 4/8 | 218.606 | 
28 | 99.264 % | 99.120 % | 4/9 | 241.748 | 
28 | 99.341 % | 99.192 % | 4/10 | 241.924 | 14.7 %, 16612 um²
28 | 99.395 % | 99.264 % | 4/11 | 242.050 | 
28 | 99.407 % | 99.276 % | 4/12 | 242.072 | 15.7%, 18000 um²
28 | 99.413 % | 99.282 % | 4/14 | 242.089 | 
28 | 99.401 % | 99.240 % | 5/10 | 242.057 | 
28 | 99.497 % | 99.383 % | 5/12 | 242.303 | 
28 | 99.563 % | 99.473 % | 6/12 | 242.458 | 
28 | 99.677 % | 99.623 % | 8/16 | 242.723 | 
28 | 99.731 % | 99.695 % | 10/20 | 242.863 | 
28 | 99.749 % | 99.719 % | 12/24 | 242.908 | 
28 | 99.77 % | 99.74 % | 16/32 | 242.97 | 
More simulations still needed. Investigate margins.

## Slide 16: Copper/optical cabling.
Vacuum tank
24 x Differential
Cu links@4Gb/s ~ 1.5m
vacuum feed-throughs
Electro-optical
24 x optical links@4Gb/s ~60m
Tell 40
Network interface
1 half station readout slice

## Slide 17: Tell 40 issues.
Number of Tell40’s required:
  Assume Tell40 will use 4 input mezzanines with
    24 input links/mezzanine. => total 96 input data links.
    Output links ? 24 ?
  1 VELOpix half-station:
    (2 sensor tiles) x (6 asics/tile) x (4 links/asic) = 48 output data links.
  We will need 2 (left & right) x 23 (half-stations per side)= 46 x Tell40 units (with 48 input and 48 output links).
Possible tasks in Tell40:
  Re-order the VELOpix packets in time ?
    VELOpix produce non-time-ordered packets.
  Aggregate the packets from the same event :
    Group clusters with same time identification.
    Remove redundant time-id (12bit) ?
    less packets , reduced network traffic.
  Perform correct clustering:
    ‘Superpixel cluster’ may contain 2 or more clusters : split ?
    Combine clusters in ‘row dimension’ ? VELOpix cannot combine across superpixel in row direction.
  Correct data per pixel for gain and offset non-uniformity ?
  Compute a cluster center position ?
    Reduces data a lot !
    Reformat (total charge, position) ?
    Eta-weighted interpolation: non trivial ! Also, don’t know the track angle !
  Add alignement ?
    Save CPU time ?
The Tell40 will also provide the configuration and fast control signals (GBT-SCA).