## Slide 1: Progress of overall tunnel design toward the basic design
H. Hayano KEK
CFS-WG LCWS2021 03172021

## Slide 2
CFS design flow, currently on-going
Revise the lattice for ILC250 and create geometry file
Create 3D tunnel arrangement, draw out 2D arrangement
Create 3D arrangement of accelerator components
Optics Deck (as of Feb. 2020) -> Geometry file ( CSV format)
Geometry file -> 3D accelerator components ( by step format )
Check any interference and check tunnel shape,
then feedback to the tunnel design
This presentation

## Slide 3
Central Region
(3D View)
created 3D arrangement
(accelerator and tunnel wall)

## Slide 4
created 2D arrangement
(Detector Hall Region)

## Slide 5
created 2D arrangement
(Detector Hall cross section)

## Slide 6
created 2D arrangement
(Interaction Point to main beam dump)
plain view
side view
plain view
side view

## Slide 7
Check any interference, any issue during accelerator construction
Check was started on Nov. 2020, biweekly base, with optics group and CFS group.
Major concerns are listed.
1)Target room space, e+ capture device, e- beam dump
for undulator-base-positron is not considered in tunnel layout
and optics deck.
2)How to support the RTML beam line 1.65m above the BDS beam line
is not yet considered.
3)How to connect tunnels with different widths and hights?
4)Chicanes of e- LTR interfere with e+ BDS.
5)tune-up dump line of e- LTR interfere with e+ BDS.

## Slide 8
6)Polarized e- gun region may interfere with e+ RTML, 1.65m above.
7)Place of e- source and booster Linac are far away from access hall.
Gun laser need daily base maintenance, SC booster Linac is better
to close to He supply at access hall.
8)Tunnel connection at turn-around seem better to use over-sized hall,
not like just a tunnel-to-tunnel connection.
9)Tunnel shape of dump room might have not flat ceiling, but round ceiling.
10)There are spin rotator SC magnet at turn around region.
They require He supply. It should be noted.

## Slide 9
11)There need precise estimation of magnet power supply space,
electric substaion, cooling water and air-cooling device space
for damping ring. More space may be required.
12)Current damping ring tunnel design require crossing of maintenance
root with accelerator. Need to change the access hall location.
13)There need to check the space between Q and SX at arc section.
Concern examples ( red squared items ) are explained, in this report.
14)There need to consider the installation pass way of big main dump.
Direct connection between BDS tunnel and detector hall circular tunnel
might be a solution.

## Slide 10
4)Chicane of e- LTR interfere with e+ BDS.

## Slide 11
positron BDS-dump
positron RTML
positron BDS
electron DR-Injection
electron tune-up dump
shield wall
plane view
tune-up dump line is going down to dump
positron BDS-dump line
positron RTML(high position)
positron BDS
electron DR-Injection
electron tune-up dump line
klystron room
Beam lines interfere
side view (expanded)

## Slide 12
shield wall
positron BDS-dump
positron RTML
positron BDS
electron DR-Injection（chicane）
klystron room
positron RTML(high position)
positron BDS
electron DR-Injection
positron BDS-dump line
Beam lines interfare

## Slide 13
6)Polarized e- gun region may interfere with e+ RTML, 1.65m above.
7)Place of e- source and booster Linac are far away from access hall.
Gun laser need daily base maintenance, SC booster Linac is better
to close to He supply at access hall.

## Slide 14
TDR electron source

## Slide 15
Power supplies of 76MeV Injector
200kV DC
200kV DC
Laser
Laser
DC gun
optical fiber transport
20kW
SSA
20kW
SSA
10MW L-band klystron
Modulator
Solenoid power supply
76MeV electron beam
Magnet PS
Beam Monitor
Vacuum
Pol. meter
5.5MV/m
8.5MV/m
8.5MV/m
50kV
50kV
13m

## Slide 16
positron BDS region
A-A cross section
(width 9.5m)
B-B
cross section
(width 10.7m)
C-C cross section
(width 12m)
e-gun position
e- Injector cryomodule place
A-A
cross section
(width 9.5m)
B-B
cross section
(width 10.7m)
C-C
cross section
(width 12m)
IP
1994m
2588m
594m
-1630m
306m
-1936m
Location of e- source and booster Linac (yellow arrow)
Move e- source to PM+8

## Slide 17
positron BDS
RTML（high position）
〜364m
76MeV beam dump
klystron tunnel
accelerator tunnel
shield wall
Injector
13m
4m
9.5m
11m
electron booster SC Linac
Laser room
11m
1.5m
2.2m
1.5m
2.2m
1.2m
5.5m
〜2200m
PM+8
LTR curved position
2.2m
Moved e- source to PM+8 (plain view)

## Slide 18
PM+8 region
Mark Point
He dome
Electric dome
Utility dome
installation
tunnel
Gun Laser dome
tunnel width
expansion
30m
30m
30m
e+ ML cryomodule end
e- Gun
e- Injector
colling water,
air dome

## Slide 19
Cross section of 11m width tunnel for e- booster LINAC, e+BDS, e+RTML
e+ RTML
e- Injector
e+ BDS
Cryomodule transport
More consideration to the alignment work on BDS, behind the cryomodule, is necessary.

## Slide 20
12)Current damping ring tunnel design require crossing of maintenance
root with accelerator. Need to change the access hall location.

## Slide 21
Damping Ring

## Slide 22
2D drawing
of
Damping Ring

## Slide 23
300m
klystron room
300m
magnet power supply room
Simplified
Damping Ring Tunnel
transport passway
crossing !
crossing !
Transport passway cross the accelerator

## Slide 24
shield wall
Accelerator room (Injection/extraction section)
300m
magnet power supply room
Detector Hall
DR crossover tunnel
Damping Ring
East Straight
access tunnel
to detector hall

## Slide 25
shield wall
accelerator room
magnet PS room
Damping Ring
East Straight
Center
Expanded View
DR crossover tunnel
Detector Hall

## Slide 26
Damping Ring
East Straight
North
Expanded View
electron RTML
positron LTR
DR
shield wall
accelerator room
magnet PS room
accelerator room

## Slide 27
Damping Ring
East Straight
South
Expanded View
positron RTML
electron LTR
DR
shield wall
accelerator room
magnet PS room
accelerator room

## Slide 28
shield wall
accelerator room
Damping Ring
West Straight
He dome
electric dome
colling water,
air dome
utility dome
carry in
DR access tunnel
detector hall access tunnel
DR crossover tunnel
300m
klystron room

## Slide 29
shield wall
accelerator room
(RF/wiggler section)
klystron room
Damping Ring
West Straight
Expanded View
He dome
Electric dome
DR crossover tunnel

## Slide 30
Move access halls to DR inside
2D drawing
of
Damping Ring
proposal of
access hall
movement

## Slide 31
1. The arrangement of accelerator components and tunnel wall
housing were made by 3D-CAD base. And extracting 2D
drawing from them for checking interference and tunnel shape.
2. First round of cheking was almost done. More than 14 issues
were found, and explained in this report.
Summary
3. Feedback to optics deck and tunnel drawings is on-going.

## Slide 32
End of slide