## Slide 1: Status of SupreKEKB positron source
Yoshinori Enomoto
KEK electron positron injector LINAC group

## Slide 2: Last page of my presentation in LCWS2019

## Slide 3: Outline
Introduction
  SuperKEKB positron source
Upgrade works in 2020 summer shutdown
  New FC, steering coils, BPMs
Magnetic field measurement
Future plan

## Slide 4: SuperKEKB positron source
W target
BC (bridge coil)
FC(flux concentrator) head
LAS (large aperture S-band)
solenoid
FC head + BC + target = FC assembly

## Slide 5: Injection requirement
Life in ring | 360 s
Current | 3.6 A
Injection bunch charge | 4 nC
Injection rate | 25 Hz x 2 bunch
Injection efficiency | 50 %
Circulation frequency | 105
Short storage time and high storage current in the ring
→high intensity positron injection is desired

## Slide 6: Problems to be solved
Discharge of FC
  FC made of New material
  Optimization of support structure (done before 2020)
  External circuit to reduce voltage (done before 2020)
  Longer pulse width (will be done after 2021)
Orbit correction in solenoid
  Steering coils
  BPMs

## Slide 7: Outline
Introduction
  SuperKEKB positron source
Upgrade works in 2020 summer shutdown
  New FC, steering coils, BPMs
Magnetic field measurement
Future plan

## Slide 8: After large discharge…
Slit gap got narrow.
Not possible to apply high voltage unless the gap will be expanded.

## Slide 9: Cu alloys
Cu
Cu - Zr
Cu - Cr
Cu - Ni - Si
were tested

## Slide 10: Yield strength
Chart: Yield strength (Mpa)
| C1020 | SH-1 | SH-2 | NC50
before brazing | 322.3 | 293.6 | 348.2 | 551.8
after brazing | 12.9 | 57.9 | 40.8 | 109.7
brazing + aging | 513.1
x40
C1020 after brazing
NC50 after brazing
NC50
NC50 after aging
(precipitation hardening)
C1020

## Slide 11: Assembly, base management (2021/1 ver.)
 | Phase 1 | Phase 2 | Phase 3 | 2019 Q4 | 2020 ab | 2020c | delivered | removed | present | Note
Assembly 1 |  |  |  |  |  |  | <2015 | 2017/3 | In tunnel | 
Assembly 2 |  |  |  |  |  |  | 2016/3 |  | In operation | 
Assembly 3 |  |  |  |  |  |  | 2017/11 |  | Test bench | 
FC base 1 |  |  |  |  |  |  | <2015 |  |  | Test
FC base 2 |  |  |  |  |  |  | <2015 |  |  | Test
FC base 3 |  |  |  |  |  |  | <2015 | 2017/3 | In tunnel | 
FC base 4 |  |  |  |  |  |  |  | 2018/9 | In tunnel | 
FC base 5 |  |  |  |  |  |  | 2016/7 | 2020/9 | In tunnel | 
FC base 6 |  |  |  |  |  |  | 2017/11 |  | Test bench | bad quality
FC base 7 |  |  |  |  |  |  | 2019/10 |  | Test bench | New material
FC base 8 |  |  |  |  |  |  | 2020/6 |  | In operation | Final version
FC base 9 |  |  |  |  |  |  | 2021/3 |  | In production | Saper for Final version
in operation
spare
test bench
Material test started in 2018/10

## Slide 12: Orbit deflection in solenoid section
Measured by T. Kamitani
1,Prepare ballistic beam between SP_15_T and SP_16_5
2,Energize a part of solenoid by
1/10* max. value step.
3, Monitor beam position at SP_16_5
Measurement of deflection amount of 3 GeV electron beam
by asymmetric field in solenoid section
SP : BPM
SL : solenoid
QF/QD : quad
PX/PY : pusled steering
BM : bend
SC : screen
AC : acc. structure

## Slide 13: Asymmetry of magnetic connection
Iron yoke to connect flux of solenoid
need space for waveguide and support
Bx
By
Inner diameter of solenoid changes

## Slide 14
target
BPM and 1st steering
There were no BPMs and steerings for 22 m after the target

## Slide 15: BPMs and steering coils inside solenoid
Steering coils
BPM
Fast BPM
electron
positron
175 ps
To monitor positron in solenoid section, very fast response BPM was developed by
Monitor group (T. Suwada, F. Miyahara, M. A. Rehman)
Simulation by F. Miyahara
Small antenna
e+/e- separation chicane

## Slide 16: BPM and steering coils inside solenoid
K. Yokoyama and K. Kakihara
BPM
Steering coil
support

## Slide 17: installation
During 2020 summer shutdown,
  A new FC
  Two fast BPMs
  Two ordinary BPMs
  One vertical steering coil
  Three horizontal steering coils
Remove old positron source
Install new positron source

## Slide 18: Positron yield vs FC current
Design (0.58)
Present
(Further tuning was done after this measurement. Now the yield almost reached design value. See next page)
Before upgrade
(To avoid discharge,
FC current was limited very low)

## Slide 19: Achievement rate
 | design | 2020ab | 2020c | 2021a | 2021a (10 nC, 0.58)
Energy (e-) | 3.5 GeV | 3.5 GeV | 3.5 GeV | 3.5 GeV | 
primary charge (e-) | 10 nC | 8.4 nC | 8 nC | 9 nC | 
e+/e- | 0.58 | 0.24 | 0.51 | 0.58 | 
e+ @ first BPM after the target | 5.8 nC | 2.0 nC | 4.1 nC | 5.1 nC | 5.8 nC (assume)
e+ @ before DR | - | 1.6 nC | 2.5 nC | 3.2 nC | 4.2 nC
e+ @ after DR | - | 1.4 nC | 2.1 nC | 2.9 nC | 3.3 nC
e+ @ Linac end | 4 nC | 1.4 nC | 2.1 nC | 2.9 nC | 3.3 nC
Primary beam
  90% (9 nC / 10 nC)
Positron yield（e+/e-）
  100% (0.58 / 0.58)
transport
  Assuming 5.8 nC (design value) @ first BPM after the target and present transport efficiency, charge @ Linac end is expected to be 3.3 nC.
  There is still room for improvement
Primary electron
First BMP after target
Before DR
After DR
Linac end
e+/e- design
Further beam tuning
Hardware upgrade

## Slide 20: Outline
Introduction
  SuperKEKB positron source
Upgrade works in 2020 summer shutdown
  New FC, steering coils, BPMs
Magnetic field measurement
Future plan

## Slide 21: Magnetic field measurement
Pick up coil is mounted on FRP rod.
XYZ stage with motor drive
Rotary stage with motor drive
XYZ positions are monitored by linear gauge by 10um precision

## Slide 22: Looking from downstream side with the measurement system attached

## Slide 23: Typical waveform from pick up coil
Signal from the coil
Integration of left waveform

## Slide 24: Comparison between simulation and measurement
Chart: z (mm)
| 100 | 94.999999999999901 | 89.999999999999901 | 84.999999999999901 | 79.999999999999901 | 75 | 70 | 65 | 60 | 55 | 50 | 45 | 40 | 35 | 30 | 25 | 20 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 5 | 4.7999999999999901 | 4.5999999999999899 | 4.4000000000000004 | 4.2 | 4 | 3.7999999999999901 | 3.5999999999999899 | 3.3999999999999901 | 3.2 | 3 | 2.7999999999999901 | 2.5999999999999899 | 2.3999999999999901 | 2.19999999999999 | 2 | 1.7999999999999901 | 1.5999999999999901 | 1.3999999999999899 | 1.19999999999999 | 1
exp x2 | 0.15497 | 0.1959 | 0.21521 | 0.24804 | 0.26996 | 0.29178 | 0.31555 | 0.32743 | 0.35086 | 0.36473 | 0.38128 | 0.452 | 0.47391 | 0.49298 | 0.51528 | 0.55739 | 0.58844 | 0.58884 | 0.59933 | 0.60532 | 0.61396 | 0.6219 | 0.62485 | 0.63785 | 0.65382 | 0.67115 | 0.71149 | 0.75099 | 0.77719 | 0.81174 | 0.88055 | 0.93879 | 0.97571 | 0.97477 | 0.98448 | 0.99453 | 0.99017 | 0.99451 | 0.99777 | 1 | 0.99334 | 0.98329 | 0.97316 | 0.95992 | 0.93789 | 0.91412 | 0.88005 | 0.83813 | 0.81469 | 0.76529 | 0.67364 | 0.62621 | 0.53194 | 0.46263
Vertical axis is normalize at peak value to 100%
Target exit surface is z = 0
Distance between FC and target is 2 mm
Solid line shows simulation using CST

## Slide 25: Outline
Introduction
  SuperKEKB positron source
Upgrade works in 2020 summer shutdown
  New FC, steering coils, BPMs
Magnetic field measurement
Future plan

## Slide 26: Future plan
Phase 1 (1 ~ 2 years)
  Higher FC current operation
    Max. current is limited by capacity of the pulsed power supply
  Optimization of transport to the DR
    Several DC magnets will be replaced pulsed magnets
  Increase primary electron charge
    Possible but care must be taken evaporation of cathode material which lead to increase of dark current from the gun.
Phase 2 (2 ~ 3 years)
  Optimization of FC shape
    In collaboration with CERN (H. Bajas).
  Moving target
    To bring both hole for electron path and target for positron production online
  Shorten the distance between FC and the first Acc. structure
Phase 3 (3 ~ 5 years and more, if there is a requirement from the ring…)
  New electron gun for higher charge?
  Replace LAS with L-band acc. structure??
  Superconducting solenoid???
We hope closer collaboration with people working on the future projects.
Major upgrade works were successfully done in 2020.
Now it’s time for us to consider future plan.

## Slide 27
backup

## Slide 28: Positron source setup 1
Positron target and capture section

## Slide 29: Positron source setup 3
Φ2 mm hole for electron
W target
Temp sensor
Cooling water pipe
beam

## Slide 30: Target detail
X = 0
X = 0 hole for electron
X = 2 center of the FC
X = 3.5 center of the W target
looking from downstream side
Target material : W
Target size : Φ4 x 14
Inserted in the pule Cu block
Connected by HIP process

## Slide 31: Positron source setup for SuperKEKB 4
Bridge coil
DC magnet
I = 650 A
Flux Concentrator
pulsed magnet
I = 12 kA
Ratio B @ target / B @ entrance of the LAS is important
stronger field is preferred in the following solenoid section
much stronger field is required @ target
Calculated by T. Kamitani

## Slide 32: Capture section after the target 1
AC_15_1
AC_15_2
AC_16_1
AC_16_2
AC_16_3
AC_16_4
FC
+
target
AC_17_1
AC_17_2
AC_17_3
AC_17_4
AC_18_1
AC_18_2
AC_18_3
AC_18_4
solenoid
solenoid
Q
Normal
LAS
Solenoid section (15 m)
Quad section (115 m)
Electron / positron separator
 | LAS | Normal S band
Acc. Gradient (MV/m) | 14/10 | 20
Aperture (mm) | 30 | 20

## Slide 33: Capture section after the target 2
To dumping ring
1-5
1-6
1-7
1-8
Normal x 32
LAS x 10
10m
2-6
2-1
2-2
2-3
2-4
2-7
2-8
Target & FC
15m long solenoid
About 100 Quad magnet
1.1 GeV @ DR

## Slide 34: Pulse width dependence
Magnetic field shape is determined by skin depth
It is important to use realistic current waveform for simulation.

## Slide 35: Gradient after the target
name | Design gradient (MV/m) | Operation gradient (MV/m) 2020/10/30 | Max gradient @ KLY power = 40 MW
AC_15_1 | 14.0 | 7.3 | 17.0
AC_15_2 | 14.0 | 7.3 | 17.0
AC_16_1 | 10.0 | 11.3 | 12.2
AC_16_2 | 10.0 | 11.3 | 12.2
AC_16_3 | 10.0 | 11.3 | 12.2
AC_16_4 | 10.0 | 11.3 | 12.2
Data from H. Ego
https://www.pasj.jp/web_publish/pasj2014/proceedings/PDF/SAP0/SAP045.pdf
https://doi.org/10.18429/JACoW-IPAC2014-THPRI047
Due to the load problem, gradient of the first and second acc. structure after the target is low.
This may cause poor bunching which can be one of the reason for large beam loss during transportation to the DR.

## Slide 36: Orbit deflection by yoke
Asymmetric shape of yoke and saturation of magnetic field generate Bx, By inside yoke.
Simulation explain experimental results well.
A Yoke to concentrate magnetic flux by the BC to the target
Transvers magnetic field on beam axis (center) is not proportional to BC current.
If permeability is infinite, Bx, By is zero inside the yoke even if the shape is not symmetric

## Slide 37: Upgrade the yoke
old
new
Shape was optimized
To increase Saturation magnetic flux density,
material was changed from
ordinary steel (SS400, 1.5 T) to
permendur (K_MP11, 2.2 T)

## Slide 38: Comparison between simulation and measurement
Chart: z (mm)
Chart: z (mm)
| 100 | 95 | 90 | 85 | 80 | 75 | 70 | 65 | 60 | 55 | 50 | 45 | 40 | 35 | 30 | 25 | 20 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 8 | 7 | 6 | 5 | 5 | 4.8 | 4.5999999999999996 | 4.4000000000000004 | 4.2 | 4 | 3.8 | 3.6 | 3.4 | 3.2 | 3 | 2.8 | 2.6 | 2.4 | 2.2000000000000002 | 2 | 1.8 | 1.6 | 1.4 | 1.2 | 1
x0 | 0.16723 | 0.18655 | 0.21092 | 0.22857 | 0.2521 | 0.27311 | 0.29076 | 0.31597 | 0.32773 | 0.3563 | 0.37563 | 0.39748 | 0.40252 | 0.42353 | 0.46975 | 0.50924 | 0.52437 | 0.52521 | 0.52941 | 0.55042 | 0.55882 | 0.56639 | 0.56471 | 0.58403 | 0.5916 | 0.59244 | 0.61765 | 0.64874 | 0.7521 | 0.78403 | 0.84874 | 0.89916 | 0.89076 | 0.90756 | 0.91597 | 0.93277 | 0.92437 | 0.93277 | 0.94958 | 0.95798 | 0.98319 | 0.9916 | 1 | 1 | 0.9916 | 0.96639 | 0.93277 | 0.87395 | 0.77059 | 0.73193 | 0.67395 | 0.55966 | 0.46134
x2 | 0.15497 | 0.1959 | 0.21521 | 0.24804 | 0.26996 | 0.29178 | 0.31555 | 0.32743 | 0.35086 | 0.36473 | 0.38128 | 0.452 | 0.47391 | 0.49298 | 0.51528 | 0.55739 | 0.58844 | 0.58884 | 0.59933 | 0.60532 | 0.61396 | 0.6219 | 0.62485 | 0.63785 | 0.65382 | 0.67115 | 0.71149 | 0.75099 | 0.77719 | 0.81174 | 0.88055 | 0.93879 | 0.97571 | 0.97477 | 0.98448 | 0.99453 | 0.99017 | 0.99451 | 0.99777 | 1 | 0.99334 | 0.98329 | 0.97316 | 0.95992 | 0.93789 | 0.91412 | 0.88005 | 0.83813 | 0.81469 | 0.76529 | 0.67364 | 0.62621 | 0.53194 | 0.46263
x3p5 | 0.16704 | 0.18419 | 0.22008 | 0.24481 | 0.26173 | 0.29384 | 0.31243 | 0.31692 | 0.3737 | 0.35855 | 0.38047 | 0.44048 | 0.46394 | 0.48367 | 0.50619 | 0.53466 | 0.56988 | 0.5697 | 0.57847 | 0.58412 | 0.59528 | 0.59725 | 0.60777 | 0.62463 | 0.63924 | 0.6771 | 0.7027 | 0.74535 | 0.77739 | 0.8109 | 0.85461 | 0.92223 | 0.95059 | 0.95172 | 0.96091 | 0.97345 | 0.9728 | 0.98161 | 0.98914 | 1 | 0.99995 | 0.99948 | 0.9955 | 0.99379 | 0.98015 | 0.96093 | 0.93147 | 0.88591 | 0.84412 | 0.80742 | 0.74438 | 0.63396 | 0.57936 | 0.48247
Vertical axis is normalize at peak value to 100%
Target exit surface is z = 0
Distance between FC and target is 2 mm
Simulation by CST
measurement

## Slide 39: Target detail
X = 0
looking from downstream side
Target material : W
Target size : Φ4 x 14
Inserted in the pule Cu block
Connected by HIP process
X = 0 hole for electron
X = 2 center of the FC
X = 3.5 center of the W target

## Slide 40: Magnetic field simulation
~ 2014
Now
Simulation using realistic model and measured current shape was established
Excitation current