## Slide 1: Novel sensors for highly compact electromagnetic calorimeters
The FCAL collaboration and the LUXE ECAL group
Speaker: Anton Tyazhev,
Tomsk State University, Tomsk, Russia

## Slide 2: Structure of compact EM calorimeter
W absorber plates interspersed with sensor layers
The very forward region of the ILD detector
1mm spacing between W plates leads to a Moliere radius equal to the one of W that makes EM compact as the definition

## Slide 3: Current sensor design
Radiation hard 500 um thick GaAs sensor
320 um thick Si sensor
EM calorimeter prototype 2020
830 um
Sensor: 500 um
Sensor assembly
830 um thick

## Slide 4: Novel concept: GaAs sensor with tracings
15x10 pixel array
Pixel
Al tracings
Al tracings
Al pads for wire bonding
Pixel
Pixel
Cross section of the sensor with tracing (not in scale)
Thin sensor
assembly 700 um !
Sensor : 500 um Conductive glue
(sensor - RO kapton ): 100 um RO kapton : 100 um
Compact
sensor module

## Slide 5: Conclusion
Sensor with tracings allows to make the sensor planes extremely thin that is the key point for compact electromagnetic calorimeters
The sensor prototypes will be produced and tested up to the end of 2021

## Slide 6: Wireless readout
Yan Benhammou
Tel Aviv University

## Slide 7: READOUT
Sensor signal is send to a dedicated ASIC : FLAME
32 mix mode channel comprising:
  Variable gain front end
  10 bit SAR ADC with sampling rate up to 50MSps
  Ultra low power consumption
Mutli-phase PLL based fast serializer
Fast SST driver
Two 5.2 Gbps links to the FPGA (we need ~5 FLAME per sensor)
From FPGA to DAQ : zero suppressed and trigger so rate depends on the occupancy and event rate

## Slide 8: Typical setup
SENSOR
FEB
DATA Processing (FPGA,…)
DAQ PC
Ethernet/optic fiber
Could be a problem of space in the very forward region : cables,…

## Slide 9: What we want to test
SENSOR
FEB
Data processing (FPGA,…)
DAQ PC
Ethernet/optic fiber
Thanks to the WADAPT CERN group
Up to 6Gbps