## Slide 1: Parameter table for Task 3.5/Task 3.6 and first layout

## Slide 2: Goals
Provide the input for the Tasks 3.5 and 3.6 to start working on
  Simulation of the radiation environment (quasi-DC power distribution in target vicinity distribution of expected integrated dose over life time) <= high priority (important for continuation of the SC solenoid design)
  Energy deposition simulation (average and PEDD) for the target, matching device and the acc. structures
  Target design (dimensions, rotation speed, cooling system, etc. )
See for more details: WP3_task_list_January2021.docx

## Slide 3: Parameter Table: FCC-ee (preliminary)
Simulations with the conventional scheme + FC + S-band acc. structures
e- drive beam
Goal: provide 2.1 ⨯ 1010 e+/bunch ⨯ 2 = 4.2 ⨯ 1010 e+/bunch accepted by the DR
Assumptions up to now (to be validated):
Limit of Peak Energy Deposited Density (PEDD) for a Tungsten-Rhenium alloy (W74Re26) is 35 J/g
Target Heat Load (THL) is not higher than 15 kW
Target thickness:
6 GeV: 5X0
20 GeV: 6X0
X0 (W) = 3.5 mm

## Slide 4: FCC-ee positron source
e+ production and capture section
e+ acceleration up to DR energy (1.54 GeV)

## Slide 5: Geometry to put in the simulations for the FCC-ee and PoP @SwissFEL
The simulation can start for the FC based scheme (layout is well defined, see slides from Pavel)
Should the fields (FC, acc. Structures and solenoid) be taken into account from the beginning?
e- beam
6/20 GeV
S- or L- band structures
embedded in the solenoid
~ 150* (S-band)
~ XXX (L-band)
To be discussed within the Tasks 3.5 and 3.6
(Bridge Coils) + DC solenoid
FC or
SC solenoid
~ 110
~ 3
~ 8
~ 44
3*
~ 50* (period)
96*
40*
(*) S-band 2.9985 GHz