## Slide 1: "Single Photon Detection with gaseous detectors"
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
Stefano Levorato
Limited to the PID applications of gaseous photon detectors………

## Slide 2
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
Single photon detection with gaseous detector: a beautiful marriage
More than 100 years of tradition on gaseous detectors development and operation
…the discovery and the exploit of the photoelectric phenomenon and the Cherenkov effect ….

## Slide 3
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
The motivation
Needed for π-K identification from HEP Experiments
Large momentum acceptance  Cherenkov angle measurement technique
Large angular acceptance  large area of efficient single photon detection
1970s: large area position sensitive gaseous detectors available
Suitable photo-ionizing agent:
Benzene: Seguinot-Ypsilantis NIM 142
(1977) 377,
TEA (7.6 eV) NIM 173 (1980) 283,
TMAE (5.3 eV) NIM 178 (1980) 125.
a gas gain high enough to detect single photoelectrons
conflicting requirements because of the copious UV emission by the multiplication avalanche.
solution: multistep avalanche chamber
(Charpak-Sauli Phys. Lett. B 142 (1977) 377) or TPC
Gaseous detectors: 1) cheap, 2) magnetic insensitive, 3) low material budget
10-5 Db/b ~ 80 GeV/c p/K separation

## Slide 4
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
Photoconverting Vapor based RICH coupled to large MWPC: the first generation
OMEGA
DELPHI
TMAE(Tetrakis-Dimethylamine-Ethylene)
SLD - CRID
TEA (Tri-Ethyl-Amine)
CLEO III
E605

## Slide 5
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
TMAE gas
QE,
NIMA 323 (1992) 351
thick photosensitive volume (slow photon detectors, parallax error)
heating and temperature control
(T bubbling <T of operation)
photon feed-back from amplification region (protections)
chemically extremely reactive
NIMA Volume 433, Issues 1–2, 21 August 1999, Pages 92-97 ( HERA-B RICH)

## Slide 6
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
1956: CsI layer has large QE for photons with hν > 6 eV (Philipp and Taft)
The revolution of the CsI, the conversion on solid photocathode

## Slide 7
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
Semitransparent and reflective mode, photoelectron escape probability from thin film photocathodes
Semitransparent photocathode:
Reflective photocathode:

## Slide 8
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
RD26: MWPC coupled to CsI for the large area fast rich detectors
1992, F. Piuz et al. Development of large area advanced fast-RICH detector for particle identification at LHC operated with heavy ions
  TO ACHIEVE HIGH CsI QE:
  Substrate preparation:
  Cu clad PCB coated by Ni (7 µm) and Au(0.5 µm), surface cleaning in ultrasonic bath, outgassing at 60 oC for 1 day
  Slow deposition of 300 nm CsI film:
  1 nm/s (by thermal evaporation or e--gun) at a vacuum
  of ~ 10-7 mbar, monitoring of residual gas composition
  Thermal treatment:
  after deposition at 60 oC for 8 h
  Careful Handling:
  measurement of PC response, encapsulation under dry Ar, mounting by glove-box.
fused silica cut
A. Di Mauro, NIM A 525 (2004) 173.
Schematic structure of the Photon Detector:

## Slide 9
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
RICH with large area single photon detector based on CsI and MWPC, the second generation
MWPCs with solid state photocathode (the RD26 effort)
TIC, NA44
COMPASS RICH-1 2002 CsI > 5 m2
JLAB-HALL A
ALICE-HMPID
2009
CsI > 10 m2
STAR
CsI ~ 1 m2
HADES 1999
CsI > 1 m2

## Slide 10
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
The COMPASS RICH photodetectors

## Slide 11
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
RADIATOR: 15 mm liquid C6F14, n ~ 1.2989 @ 175nm, βth = 0.77
PHOTON CONVERTER: Reflective layer of CsI (QE ~ 25% @ 175 nm)
PHOTOELECTRON DETECTOR: MWPC with CH4 at atmospheric pressure (4 mm gap) HV = 2050 V.
- Analogue pad readout
The ALICE RICH photodetectors
Full QC
of the
Photon
detector

## Slide 12
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
Photoelectron extraction from a CsI film, the role of gas and E
C. D. R. Azevedo et al., 2010 JINST 5 P01002
Breskin et al., NIM A 367 (1995) 342
M. Alexeev et al., NIM A (2010)
Backscattering of photoelectrons in the gas medium → QE degradation
Escada et al., J. of Physics D 43(2010)65502

## Slide 13
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
H. Hoedlmoser et al., NIM A 574 (2007) 28.
MPWC based signal
slow signal formation ms and low gain  “slow” electronics (signal integration, low noise level)
  Gassiplex FE : integration time ~ 0.5 ms, time res> 1 ms
  APV (COMPASS RICH-1 upgrade) : resolution ~ 400 ns
   Detector memory, i.e. not adequate for high rates
The limits of the CsI and MWPC technology
Severe recovery time (~ 1 d) after detector trips
  Ion accumulation at the photocathode
Feedback pulses
  Ion and photons feedback from the multiplication process 2pi  50%
Aging after integrating a few mC / cm2
  Ion bombardment of the photocathode 50, 60 %
Operation at moderate gain < 105
Breskin et al., NIMA 371(1996)116
Degradation not well understood – physical and chemical mechanisms competing? Evaporation? Cesiation?..

## Slide 14
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
An option for the ALICE HMPID upgrade

## Slide 15
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
The Micro Pattern Gaseous Detector technology triggered new possibilities for Gaseous PD performance
    Intrinsic mitigation of the photon feedback
    Strategies for Ion backflow reduction
    High gain
    High position resolution
    Fast signals
    Visible sensitivity
    Nano/Pico second resolution
The MPGD era

## Slide 16
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
A. Breskin and R. Chechik, NIM A 595 (2008) 116
Semi-transparent PC
Reflective PC
e- avalanche
ion avalanche
No photon feedback, reduced ion feedback
An “old” idea
R. Chechik et al., NIM A 419 (1998) 423
The MPGD ion and photon feedback suppression
Bachman et al. NIMA 438(1999)376
Breskin et al. NIMA 478(2002)225
Bondar et al. NIMA 496(2003)325
Chechik and Breskin NIMA 595(2008) 116
- triple gem with CsI pc
- semi-transparent vs reflective pc
- typical stable gains ~ 10⁵
- large area > 1 m² can be produced
3% IBF @ 0.5 kV/cm
Gain ~ 105

## Slide 17
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
On IBF
IFB in GEM-based detectors
IC
IA
Ibottom3
Itop1
ED = 0.5 kV/cm
ED = 0.1 kV/cm
E ~ 1 kV/cm needed for good photoelectron extraction
strong dependence from gain and EDRIFT
poor dependence from pressure and gas type
A. Bondar et al., NIMA 496 (2003) 325
A. Breskin et al., NIMA 478 (2002) 225d
IBF: a few % level in
effective GEM-based
photon detectors
semi-transparent PC

## Slide 18
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
Hadron-Blind detector (HBD) at RHIC-PHENIX reflective mode
- Triple GEM
- CsI reflective pc
- G~10⁴
S. Milov, et al., J. Phys. G: Nucl. Part. Phys. 34 (2007) S701
Z. Fraenkel, et al., NIMA 546 (2005) 466.
Anderson et al., NIMA 546 (2005) 466.
-Proximity focus configuration, no window, no mirror
-CF4 radiator and active gas.
-Lrad=50 cm Very large bandwidth 108 – 200 nm
Detector operated in reverse bias mode to repel the ionization charge from dE/dx
Cherenkov light is formed only by e+ or e-
Successfull operation at PHENIX since several years
It is not a detector of single photons

## Slide 19
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
Large gain, one of the key element for an effective single photon detection
LARGE GAIN RELEVANT FOR SINGLE PHOTON DETECTION
GEM-based PDs in laboratory studies
  for single photoelectron detection, they have been operated at gains > 105 (see, for instance, the plots of the previous slides)
GEM-based detectors in experiments
Always a MIP flux and small rates of heavily ionizing fragments crossing the detectors (even when the detectors are used as photon detectors)
    At COMPASS: G ~ 8000 (B. Ketzer, private comm.)
    At LHCb: G ~ 4000 (M.Alfonsi NIMA 581 (2007) 283)
    At TOTEM: G ~ 8000 (G. Catanesi, private comm.)
    Phenix HBD: G ~ 4000 (W. Anderson et al., NIMA 646 (2011) 35)
In experiments, small chances
to operate GEM-based PDs at gains > 104

## Slide 20
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
THGEM-based PD
PCB technology, thus:
robust
mechanically self supporting
industrial production of large size boards
large gains can be easily achieved (rim !)
Gain stability is challenging
Comparing to GEMs
Geometrical dimensions X ~10
  But e- motion/multiplic. properties do not!
  Larger holes:
    dipole fields and external fields are strongly coupled
    e- dispersion plays a minor role
introduced in // by different groups:
L. Periale et al., NIM A478 (2002) 377.
P. Jeanneret, PhD thesis, Neuchatel U., 2001.
P.S. Barbeau et al, IEEE NS50 (2003) 1285
R. Chechik et al, .NIMA 535 (2004) 303
RIM
About PCB geometrical dimensions:
Hole diameter : 0.2 – 1 mm
Pitch : 0.5 – 5 mm
Thickness : 0.2 – 3 mm

## Slide 21
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
THGEM-based PD
M. Alexeev et al. JINST 10 (2015 ) P03026
High-rate device
photoelectron trajectories from a THGEM
photocathode,simulation, multiplication
switched off
thickness 0.6 mm, diam. 0.4 mm,
pitch: 0.8 mm, ΔV = 1500 V
Photoelectron extraction from
THGEM PC fully confirmed by direct
observation with “Leopard”
G.Hamar and D.Varga,
NIMA 694(2012) 16

## Slide 22
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
ALICE VHMPID
THGEM & HYBRID
beam
Č photon
V.Peskov et al., NIMA 695 (2012) 154
COMPASS, RICH-1 upgrade by Triple THGEM detectors
THGEM R&D for RICHes
N of detected photons is ~60-70% of MWPCs with CsI
Ne+10%CH4, used with DV at 650-750 V

## Slide 23
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
THGEM 1- provide support for the CsI pc, gain and partial block of ions and photons
THGEM 2 -extra gain and extra ion blocking and charge splitting
Micromegas – discrete element approach efficient for ion trap and provide extra gain and spark mitigation
THGEMs+Resitive Micromegas combination

## Slide 24
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
THGEMs+Resitive Micromegas combination, performance

## Slide 25
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
InGrid – Micromegas integrated in a Timepix
The future...

## Slide 26
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
RICH at the EIC, exploiting the COMPASS hybrid PD upgrade
-1<η<+1 (barrel) : sPHENIX + Compact-TPC + DIRC
-4<η<-1 (e-going) : High resolution EM calorimeter + GEM trackers
+1<η<+4 (h-going) :
  1<η<4 : GEM tracker + Gas RICH
  1<η<2 : Aerogel RICH
  1<η<5 : EM Calorimeter + Hadron Calorimeter
Along outgoing hadron beam: ZDC and roman pots
Studies performed with Ar/CH4 mixtures, towards a windowless
approach using CF4  Chandradoy Chatterjee
and different photoconverters Daniele D’Ago
Different lever arm w.r.t. COMPASS requires pads of small size to improve the space resolution(3mmx3mm)
minimum material budget

## Slide 27
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
InGrid – Micromegas integrated in a Timepix
Innovative approaches to single photon detection with GPD, R&D

## Slide 28
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
- Very interesting performance for imaging (high granularity)
- Compact system with integrated electronics
- Limited to small detection areas – timePix limitation
Melai et al., NIMA 628 (2011)133
InGrid – Micromegas integrated in a Timepix

## Slide 29
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
MM-TGHEM – Multi-Mesh
Oliveira and Cortesi., JINST 13 (2018) P06019
First performance evaluation of a Multi-layer Thick Gaseous Electron Multiplier with in-built electrode meshes—MM-THGEM

## Slide 30
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
MM-TGHEM + RWELL – Multi-Mesh
Oliveira and Cortesi., JINST 13 (2018) P06019
- Gain ~10⁶
- Fair IBF for CsI pcs
IBF ~2-3%
First performance evaluation of a Multi-layer Thick Gaseous Electron Multiplier with in-built electrode meshes—MM-THGEM
MM-THGEM/WELL-THGEM detector
Low IBF contribution when the WELL-THGEM electrode contribution to the total gain is high

## Slide 31
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
2 THGEMs
a THCOBRA with 2 d R-O structure
T. Lopes 2013 JINST 8 P09002
HYBRID MPGD PDs (THGEM + THCOBRA) a low rate application
IBF high but

## Slide 32
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
Carbon based photocathodes coupled to Gaseous Detectors, HND and THGEMS
Uncoated THGEM
Coated THGEM
Below Quartz cutoff
Windowless approach for
RICH
Velardi et al., Diamond & RM 76(2017)1 ; Valentini et al. Patented
Still presenting some ageing →
Ion bombardment resistance !
Compatible with MPGD operation !
 Daniele D’Ago Talk

## Slide 33
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
Picosec
PICOSEC Collaboration aims for the development of a Micromegas based detector coupled to a photocathode for time resolution in the ten pico second time scale, not single ph.
Lukas Sohl et al. For the PICOSEC Collab., presented in RD51 collaboration meeting, Munich, June 2018
Papaevangelou et al, Fujiwara et al., EPJ Web Conf., 174(2018)02002
Ne(80%)/CF4(10%)/C2H6(10%)

## Slide 34
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
A comment
Advances in DLC films triggered the possibility of producing photocathodes to operate in gas medium for MPGDs
DLC – Diamond-like carbon
  Widely used in industry as a solid lubricant
  Recently introduced to the MPGD field as excellent resistive electrodes
  Tested with success in the PICOSEC Collaboration
A breakthrough in carbon based photocathodes would favour:
GPMs performance in general
RICH detectors for PID for future NP/HEP experiments: i.e. HND nanodiamonds

## Slide 35
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
InGrid – Micromegas integrated in a Timepix
Innovative approaches to single photon detection with GPD, R&D , visible range

## Slide 36
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
The visible range, challenges
  Chemical reactivity (gas purity better than ppm level needed  UHV materials and sealed detectors
  PC stability under ion bombardment - work function lower than CsI one
  AGEING CsI: -16% QE at 25mC/mm2
  Bilkaly: -20% QE at 0.4mC/mm2
T.Moriya et al., NIMA 732 (2013) 263
F.Tokanai et al., NIMA 628 (2011) 190
Ion induced secondary emission in CsI is negligible
A.V.Lyashenko et al., 2009 JINST 4 P07005
F-R-MHSP,
IBF: 3 x 10 -4
K-Cs-Sb vs CsI
Double GEM,
IBF: ~ 10 -2

## Slide 37
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
IBF trapping with dedicated geometries
More complex geometries needed with extra electrodes to trap the ions:
Micro-Hole & Strip Plate (MHSP), COBRA
J.F.C.A. Veloso et al.,
Rev.Sc. Instr. 71 (2000) 2371
A.V. Lyashenko et al.,
JINST 2 (2007) P08004
MHSP
COBRA
A.V. Lyashenko et al.,
NIMA 598 (2009) 116
A.V. Lyashenko et al.,
NIMA 598 (2009) 116

## Slide 38
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
Visible range single photon detection, GEM approach
Lyashenko et al., JINTS 4(2009)P07005

## Slide 39
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
Visible range single photon detection, GEM approach

## Slide 40
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
Visible range single photon detection, Micromegas approach
Nicely working!

## Slide 41
Stefano Levorato | 16 February 2021 | RD51 Workshop on Gaseous Detector Contributions to PID
GASEOUS PHOTON DETECTORS
  Most effective approach to instrument large surfaces at affordable costs
MPGD-BASED PHOTON DETECTORS
  Allow to overcome the limitations of open geometry gaseous PDs
  A wide effort to refine and consolidate the technology
MANY APPLICATIONS OF MPGD-BASED PHOTON DETECTORS
  From PID to n, DM, medical applications …
  First step toward large area: Hybrid THGEM+MM for COMPASS
BRIGHT FUTURE FOR:
  Inventions: new ideas, new techniques
  Technology consolidation, new applications
  Large scale projects
SUMMARY/CONCLUSIONS