## Slide 1: MPGD-based photon detectors for the upgrade of COMPASS RICH-1 and beyond
Chandradoy Chatterjee
INFN Trieste
PID in COMPASS Experiment
Towards 2016 COMPASS RICH upgrade
Quality control of hybrid components
The upgrade
Detector performance
Summary of COMPASS RICH upgrade
PID in EIC and its challenges
R&D for EIC PID with MPGD technologies
Beam test performance
Summary of EIC related activities

## Slide 2
In 2016-2017 data taking COMPASS RICH used three different photon detection technology
Approved SIDIS data taking in 2021 RICH is crucial. Future COMPASS++/AMBER requires efficient RICH for pbar cross-section, spectroscopy measurements.
PID in COMPASS Experiment
NIM A 577 (2007) 455
NIM A 779 (2015) 69
NIM A 553 (2005) 215;
NIM A(2008) 371;
NIM A(616) (2010) 21;
NIM A 631 (2011) 26
5.6 m2 photon detection surface 21 m2 UV reflective mirror

## Slide 3
Reduced wire-cathode gap because of :
• Fast RICH (fast ion collection)
• Reduced MIP signal
• Reduced cluster size
• Control photon feedback spread
To overcome the limitations: • Less critical architecture
• suppress the PHOTON & ION feedback
• use intrinsically faster detectors MPGDs
2016 COMPASS RICH UPGRADE
Resistive MICROMEGAS by bulk technology
 traps the ions
 ~100 ns signal formation
THGEM, detail 77% surface for CsI coating
2016 COMPASS RICH UPGRADE
NIMA 560 (2006) 405.

## Slide 4
Quality Control of components
In Trieste a specific cleaning procedure is applied : polish with fine grain pumice powder, pressure water cleaning, ultrasonic bath with Sonica PCB solution (PH11), distilled water rinsing and oven @ 160OC
Our thickness uniformity requirements are stricter than those offered by producers  material selection  thickness measurement
Mitutoyo EURO CA776 coordinate measuring machine with ruby touch probe, hosted in a thermalized room
Post polishing protocol
NIMA 610 (2009) 174, NIMA 617 (2010) 396, NIMA 639 (2011) 130
JINST 9 (2014) C09017, JINST 9 (2014) P01006, JINST 10 (2014) P03026

## Slide 5
Uniformity:
3 % r.m.s. within a photocathode
10 % r.m.s. among photocathodes
mean value: 93% of reference
CsI coating at CERN

## Slide 6: The Upgrade: challenging and acrobatic
More acrobatic images or details of upgrade related adventures?
 S.S. Dasgupta CERN-THESIS-2017-069

## Slide 7
Similar hardware & software have been prepared and tested for MWPCs. Will be used in 2021 data taking!
T/P fluctuations and way-out
Without correction roughly 25% fluctuation of gain is expected.
NIMA 952(2019)162378

## Slide 8: Event displays
6.4 GeV pion
Hybrid
PMT
PMT
6.76 GeV pion
Hybrid
PMT
6.36 GeV pion
Hybrid
Ring center calculated from particle trajectory
Detected photoelectrons : hits on the sensors. No noise filtering
Ring center
from track
photons
For reference:
Θ (β = 1) = 52.5 mrad

## Slide 9
Effective gain : ~14000 +- 140
Single photon resolution: 1.83 +- 0.01 mrad
Characterization of the novel Photon detectors
Dedicated pion beam was used to characterize the novel detectors and by extracting the following properties from reconstructed rings
Effective Gain
Single photon resolution
Number of photons per ring at saturation
Fit Range: 50 to 160
Formula: p0*exp(-p1*x)
1 ADC Channel -> 300 electrons
Dedicated pion beam to characterize!

## Slide 10
Characterization of the novel Photon detectors …
Extrapolate to saturation, number of photon= 12.9
First part of the function = 11.5 +/- 0.4
Second part of the function= 1.4 +/- 0.3
N(ϴCh) = p0sin2ϴCh+ p1ϴCh

## Slide 11: COMPASS 2016 RICH upgrade summary
A 7 years long R&D program had been dedicated to upgrade COMPASS RICH with MPGD based single photon detection.
COMPASS has pioneered MPGD based PDs for RICH application in 2016.
The detector performance is thoroughly studied, and results are encouraging for use of MPGD based single photon detectors for future RICH applications.
The hybrid PDs are working at an effective gain of 14k, with a level of 5% stability. An IBF below 3% is achieved (thanks to inclusion of MM and staggered THGEMs).
Single photon resolution is 1.83+-0.01 mrad.
In best working condition the detector can detect ~11 signal photons per ring at saturation.

## Slide 12
Compact collider set-up short radiator length (around 1m)  Limited number of generated photons
Standard quartz window opaque λ < 165 nm  possibility windowless RICH (M. Blatnik et al., IEEE NS 62 (2015) 3256 )  Gaseous detectors
CsI most used, however ageing due to humidity and ion bombardment  quest for novel PC with sensitivity in the far UV region  H-ND powder as possible alternative photocathode of CsI (Talk by D.D’Ago).
Improvement of Spatial resolution Smaller pad size.
Operation in intense magnetic field  MPGD based single photon detectors are tested cost effective solution (Thanks to COMPASS 2016 upgrade).
4π detector setup. Challenge include high momentum PID detectors in hermetic detector!
PID in the EIC at USA
A.Accardi et al., “Electron Ion Collider: The Next QCD Frontier,” Eur. Phys. J., vol. A52, no. 9, p. 268, 2016. National Academies of Sciences, Engineering, and Medicine, “An Assessment of U.S.- Based Electron-Ion Collider Science.” The National Academies Press, Washington DC, 2018. https://doi.org/10.17226/25171.
EIC is Approved!!!

## Slide 13
Modular structure: all components and services within the active area.
Prototype with 10x10 cm2 active area.
1024 square pads of 3x3 mm2 with 0.5 mm inter-pad space
Minipad detector setup

## Slide 14
Components: Lab Test and performance
Standalone THGEM test
COMPASS Protocol
Standalone MM test
8 x 16 (=128) pads connected via SAMTEK1143 (130 pin) SMD connector Individual 470 MΩ SMD resistor per pad on HV distribution cards (128/card). 8 cards
CAEN N1471H
Produced at CERN, standard bulk technology woven stainless steel mesh,18 μm wires, 63 μm pitch One pillar per pad, 500 μm diameter. Gap = 128 μm.
NIMA 936 (2019) 565

## Slide 15
Read-out system : SRS (from RD51)
FE chip: APV25
DAQ: RAVEN, an original system developed for these studies based on LabVIEW.
Decoding and online analysis included.
Good rate capability: 10 kHz for single APV.
Ar:CH4 50:50 Picoquant PLD 4000B pulsed UV laser source
DAQ and online analysis: RAVEN
Master Thesis: M.Baruzzo, Construction, characterisation and DAQ development of a single photon MicroPattern Gaseuos Detector for the future EIC RICH.
Home made DAQ and Decoder based on LABView and C++

## Slide 16
Towards beam test at RD51 beamline

## Slide 17
Development of an optimized detector for increased resolution based on the hybrid THGEM + MM and 3mm x 3mm minipad.
Study the compatibility of these hybrid PDs with CF4 for a windowless RICH for the future Electron Ion Collider
Beam test results
Timing
Gain from cluster amplitude : 30 K

## Slide 18: Summarizing Minipad activities
COMPASS hybrid like PD prototype has been coupled to miniaturized pad size.
THGEMs and MMs have been studied in standalone and in hybrid architecture in lab.
Dedicated DAQ has been prepared for decoding and online analysis.
A beam test had been conducted at CERN H4 beamline.
Clean signature of photon is observed.
Covid-19 outbreak has been a show-stopper in 2020 activities.
Further R&Ds in both activities are foreseen in 2021.
Thanks for your attention.