## Slide 1: Follow-up on compressed convolution
Ivan Karpov
BLonD code development meeting, 12.03.2021

## Slide 2: Motivation
We aim to speed up simulations for beam with periodic gaps (LHC type in SPS, LHC, FCC, etc.)
Compressed wake calculation can be implemented (similarly to PyHEADTAIL J. Komppula, K. Li, & N. Mounet, PyHEADTAIL Meeting #19, 2018)
Method is based on:
Picking relevant data and removing the rest
Using fast FFT convolution

## Slide 3: Motivation
We aim to speed up simulations for beam with periodic gaps (LHC type in SPS, LHC, FCC, etc.)
Compressed wake calculation can be implemented (similarly to PyHEADTAIL J. Komppula, K. Li, & N. Mounet, PyHEADTAIL Meeting #19, 2018)
Method is based on:
Picking relevant data and removing the rest
Using fast FFT convolution

## Slide 4: Motivation
We aim to speed up simulations for beam with periodic gaps (LHC type in SPS, LHC, FCC, etc.)
Compressed wake calculation can be implemented (similarly to PyHEADTAIL J. Komppula, K. Li, & N. Mounet, PyHEADTAIL Meeting #19, 2018)
Method is based on:
Picking relevant data and removing the rest
Using fast FFT convolution

## Slide 5: First implementation in BLonD*
Mostly InducedVoltageTime class in impedance.py is modified
Requires additional info for masking ’n_window’, ‘n_sampling’; is activated by passing dictionary compression_dict
Masks for profile and wake function are introduced in process()
Method induced_voltage_1turn() is overridden; SciPy fftconvolve is used for speed-up
*More details in fork https://github.com/IEKarpov/BLonD

## Slide 6: Example EX_23_compressed_wake.py
Simulation set-up:
SPS flat bottom
200 bunches spaced by 100 ns (20 RF buckets)
Single resonator impedance
Comparison of full, compressed and frequency domain calculations
Artefact of circular convolution

## Slide 7: Example EX_23_compressed_wake.py
Simulation set-up:
SPS flat bottom
200 bunches spaced by 100 ns (20 RF buckets)
Single resonator impedance
Comparison of full, compressed and frequency domain calculations
Artefact of circular convolution

## Slide 8: Small performance test
induced_voltage_sum() is called 50 times
MEAN and STD values are calculated
200 bunches spaced by 100 ns (20 RF buckets), n_window = 2*n_slices_per_bucket

## Slide 9: Small performance test
induced_voltage_sum() is called 50 times
MEAN and STD values are calculated
200 bunches spaced by 100 ns (20 RF buckets), n_window = 1.5*n_slices_per_bucket
Can be used for shorter bunches

## Slide 10: Small performance test
induced_voltage_sum() is called 50 times
MEAN and STD values are calculated
500 bunches spaced by 25 ns (5 RF buckets), n_window = 1.5*n_slices_per_bucket

## Slide 11: Summary and outlook
First version of compressed FFT convolution is implemented.
Can be easily activated, but profile object need to be carefully generated.
Factor of 6-13 speed-up is achieved for example case.
Further optimization potentially can be done.

## Slide 12: Thank you!

## Slide 13: Smaller window function
n_window = 1.5*n_slices_per_bucket