## Slide 1
H2020 SANDA: Supplying Accurate Nuclear DAta for energy and non-energy applications
WP2. New nuclear data measurements for energy and non-energy applications
TASK 2.6: New measurements for non-energy applications
Task coordinator: USE, partners: IST, NPL, PTB
NPL (Mike Bunce), PTB (Ralf Nolte), IST (Pedro Vaz) & USE (Carlos Guerrero)
SANDA meeting, February 9th 2021

## Slide 2
Subtask 2.6.1. Spectrum averaged cross sections for dosimetry (NPL)
NPL will perform spectrum-averaged benchmark measurements of the activity induced in foils by neutrons from a 252Cf source via the 117Sn(n,inl)117mSn and 60Ni(n,p) reactions. […]
D.2.9 Spectrum averaged cross sections for dosimetry (NPL) M44
Subtask 2.6.2. Measurement of cross sections relevant for hadron therapy (PTB and IST)
PTB and IST will collaborate in the research of secondary high neutron production in particle radiation therapy of cancer. […] double-differential charged-particle emission cross sections will be carried out at the CERN n_TOF facility […] Part of the necessary equipment will be developed by HZDR within WP1.
D.2.10 Report on the measurement of double-differential charged-particle emission cross sections at the CERN n_TOF facility in the neutron energy range from 20 MeV to 200 MeV. (PTB) M48
Subtask 2.6.3. Measurement of b+ emitters for proton therapy (USE)
USE will perform measurements of production cross sections of beta+ emitters used for range verification in proton therapy. The list of isotopes covers the high priorities of IAEA: 11C, 13N, 15O, 30P produced by protons with energies up to 250 MeV. Other recently proposed isotopes for range verification, with shorter half-lives such as 10C, 12N, 38mK and 29P will be considered along the project.
D.2.11 Report on the production cross sections of beta+ emitters used for range verification in proton therapy. (USE) M30
H2020 SANDA: Supplying Accurate Nuclear DAta for energy and non-energy applications
WP2. New nuclear data measurements for energy and non-energy applications
TASK 2.6: New measurements for non-energy applications
Task coordinator: USE, partners: IST, NPL, PTB

## Slide 3
Measurement of spectrum averaged cross section of the 117Sn(n,n’)117mSn reaction using 252Cf source at NPL low scatter facility (supported by NMS and SANDA collaboration).
Cross section determination via ()
18 day irradiation – fluence rate ~42k neutrons/s/cm2
Measurement using NaI scintillator ~43 days (10 days after irr. end, t1/2 ~14 days)
GEANT4 simulations and measurements to determine efficiency
Subtask 2.6.1. SACS for dosimetry (NPL)
D.2.9 SACS for dosimetry (NPL) (M44, May 2023)
18d
10d
43d
Impact: The International Reactor Dosimetry and Fusion File (IRDFF) aims at providing evaluated neutron dosimetry reactions validated for all applications related to fission reactors and fusion technology development
Justification document: Accurate cross sections as well as (SACS) in relevant and well-characterized neutron fields are essential for improvement and validation of the evaluated data.
NEA
HPRL

## Slide 4: Preliminary results
Preliminary results look promising. Scaling the evaluation to match measured spectrum-averaged cross-section agrees with data. Still more analysis to finalise!
Re-measure 2021 (hopefully!) using HPGe
Investigate a monoenergetic measurement at ~ 5 MeV
Measurement of spectrum averaged cross section of the 117Sn(n,n’)117mSn reaction using 252Cf source at NPL low scatter facility (supported by NMS and SANDA collaboration). Reaction on NEA HPRL, required for reactor dosimetry.
D.2.9 Spectrum averaged cross sections for dosimetry (NPL) (M44. May ‘23)

## Slide 5
Subtask 2.6.2. Measurement of cross sections relevant for hadron therapy (PTB and IST)
D.2.10 Report on the measurement of double-differential charged-particle emission cross sections at the CERN n_TOF facility in the neutron energy range from 20 MeV to 200 MeV. (PTB) M48

## Slide 6
WP1, Task 1.4: detectors for non-energy application
WP2, Subtask 2.6.2. Measurements of DDX for light charged particles at n_TOF (En> 100 MeV)
• First of this kind at n_TOF
• Final experiment not before 2023
• Acceptance of the proposal by the INTC required
D.2.10 Report on measurements of DDX for (n, lcp x) at n_TOF (M48, Aug ’23)
[…] test beam time for detector development is requested to extend the existing techniques from the 235U(n,f)/1H(n,n)p experiment to this more demanding task.
Subtask 2.6.2. Measurement of cross sections relevant for hadron therapy (PTB and IST)
D.2.10 Report on the measurement of double-differential charged-particle emission cross sections at the CERN n_TOF facility in the neutron energy range from 20 MeV to 200 MeV. (PTB) M48

## Slide 7
Subtask 2.6.3. Measurement of beta+ emitters (USE)
D.2.11 Report on the production cross sections of beta+ emitters used for range verification in proton therapy. (USE) M30
PET
protons
Monitored table
Aizawa Hospital, Japan
Verification of dose delivered to the patient by measuring the activity induced by the proton beam: PET range verification
[Full exploitation of the technique by minimizing safety margins]
The corresponding activation (long-lived: 11C, 12N, 13N, 15O, 30P; short-lived: 10C, 29P, 38mK) cross sections in C, O, N, P and Ca involved are poorly known in the range of interest [Ep=0-230 MeV]

## Slide 8
Submitted to Physics in Medicine & Biology (01/2021)

## Slide 9
Production of short-lived (12N, 29P and 38mK) up to 230 MeV
Test experiments@KVI (July 2019)
Production of long-lived (11C, 13N and 15O) up to 230 MeV (July 2020)
D.2.11 Report on the production cross sections of beta+ emitters used for range verification in proton therapy. (M30, March 2022)
- True for long-lived (11C, 13N and 15O)
- Maybe 3-6 months more needed for short-lived (10C, 12N, 29P and 38mK)
Nylon-6 @ 98.8(6) MeV
Test @KVI only partially succesful:
Background from degraders dominates
KVI technical+pandemic delays
Work to continue a PT center:
  Quiron salud (Madrid, ES)
  WPE (Essen, GE)