## Slide 1
SPring-8 upgrade : a fast kicker system
for beam injection
Japan Synchrotron Radiation Research Institute (JASRI)
SPring-8
T. Nakamura
CFA Beam Dynamics Mini Workshop on Low Emittance Rings 2011, 2011-10-05

## Slide 2: Injection to 2mm Dynamic Aperture Ring
Bucket-by-Bucket Injection Control (BBI)
On-axis Swap Injection
Aperture < 1-2mm at Early Stage of Tuning
Full bucket filling
100mA with Top-up Swap Injection with SACLA Linac
Off-axis for high bunch bunch current for variety of filling Aperture > 1-2 mm
Minimum Perturbation on Stored Beam
Rejection of Impurity Electrons from SACLA Linac
for High Purity High Current Singlet Bunch
SPring-8 II : 70 pm rad => Dynamic Aperture ~ 2mm, 6 GeV
Injector : SACLA XFEL Linac ( < 0.1 nm rad, 0.25nC )
Bucket-by-Bucket On-axis/Off-axis Injection

## Slide 3
Kicker for Bucket-by-Bucket On-axis/Off-axis Injection
Fast TEM mode Kicker ( ~ 2ns ) [ ex. DR extraction Kickers ]
with Variable Field by changing drive Power and Polarity
Dipole Kick => On-axis swap Injection
Quadrupole Kick => Off-axis Injection
Kick duration < 4ns ( +/- 2ns )
Beam
High Power Pulser 50kV
(FID FPG-50 )
Upper Outer Conductor
is removed
Length 0.2m
(time constant~ 1.3ns)
High Power Pulser 50kV
(FID FPG-50 )
Kicker : Unit x 5

## Slide 4: Time Structure of Kick
Output of
High Power Pulser
50kV (FID FPG-50 )
Kick Strength
( L = 0.2m )
with MAFIA-T3
2ns : bucket spacing
Additional Correction Kicker might be required for neighboring bunches
Should be smaller than 1/10

## Slide 5
1 V
-1 V
-1 V
-1 V
10mm
Dipole Kick
for On-axis Injection
Quadrupole Kick
for Off-axis Injection
Kick Field = 0
Injected
beam
Stored beam
Field Distribution of Kicker
Field Strength ~ 1/(vertical gap)
Counter Propagating TEM Mode
( Kick by Ex ) = ( Kick by By ) => Total Kick = 2 Ex

## Slide 6
Dipole Kick
11 MeV/m (+50kV,-50kV)
+ 1V
-0.45 V
Quadrupole Kick at 2mm
4 MeV /m (+50kV,+50 kV)
-1V
-1V
Stored
Off-axis Injected
On-axis Injected
Field Strength Distribution in Horizontal

## Slide 7: Discharge Limit
50 kV
Kilpatrick Limit
30 kV
1V
-1V
~ 500 V/m
Electric Field Strength Distribution
Maximum Field Strength without Discharge
Kilpatrick Limit for CW field
Frequency Dependence ~ 250 MHz ( 4ns )
50 kV < Limit but It’s Pulse ! Needs Test
250 MHz

## Slide 8: High Transverse Impedance (Horizontal) !!
Total Loss Factor vs Vertical half gap b
Total Loss Factor vs Vertical half gap b
Total Loss Factor vs Vertical half gap b
Total Loss Factor vs Vertical half gap b
Total Loss Factor vs Vertical half gap b
Total Loss Factor vs Vertical half gap b
Total Loss Factor vs Vertical half gap b
Total Loss Factor vs Vertical half gap b
Total Loss Factor vs Vertical half gap b
Total Loss Factor vs Vertical half gap b
Total Loss Factor vs Vertical half gap b
Total Loss Factor vs Vertical half gap b
Total Loss Factor vs Vertical half gap b
Total Loss Factor vs Vertical half gap b
Total Loss Factor vs Vertical half gap b
Total Loss Factor vs Vertical half gap b
Total Loss Factor vs Vertical half gap b
Total Loss Factor vs Vertical half gap b
Loss Factor
Gap Dependence of
Quadrupole Field
Strength
Horizontal value (kx ) is
x 70 of
our Bunch-by-bunch kicker
( Dipole ~ 1/gap )
Quadrupole ~ 1/(gap)2

## Slide 9: Injection Scheme at Long Straight Section
Swapped out
From SACLA linac
βH = 25m
15 mm
15 mm
0.6 m rad
βH = 25m
βH = 25m
Dipole Field
0.08 m rad
2mm
15mm
0.6 m rad
Quadrupole Field
+50 kV, +50 kV
+18 kV, -18 kV
0.6 m rad x 6 GeV = 3.6 MeV
5 units (0.2m) < 2 m
Off-axis
On-axis

## Slide 10: Injection Scheme at Long Straight Section
15mm
1mm
0.04 m rad
-1mm
0.04 m rad
+50 kV, +50 kV
2mm
15mm
0.08 m rad
-2mm
0.08 m rad
+15 kV, +34 kV
Dipole + Quadrupole Field
Additional
Dipole
kicker
with Position Shift 1mm
Quadrupole Field
Sharing Injection : Offset => Injected Beam + Stored Beam
Reduction of Input Field Strength
Reduction of Offset
No field for injected beam

## Slide 11: Summary
Bucket-by-bucket Injection
On-axis 100mA top-up injection
Off-axis to 1-2mm dynamic aperture
with quadrupole
with minimum perturbation on stored beam
Fast TEM mode Kicker with Variable Field Distribution
+/- 2 ns pulse
Dipole filed for On-axis
Quadrupole field for Off-axis
But
Emax > Discharge Field Limit ?
Large Horizontal Impedance !!